QL· Technical

Guide

by Tony Tebby and David Karlin

Edited by Michèle Wright

First published in 1985

Sinclair Research Ltd

25 Willis Road, Cambridge CB1 2AQ, England

ISBN 1 850160368

Documentation and packaging © Sinclair Research Ltd

sinclair logo, QL and QL Technical Guide are

Registered Trade Marks of Sinclair Research Ltd.

All rights reserved. No part of this program, documentation or packaging may be reproduced in any form. Unauthorized copying, hiring, lending or sale and repurchase prohibited.

Made in the UK.

Contents

\

3.4	Operating System Extensions	21

4.0	Memory Allocation	22

4.1	Heap Mechanism	23

5.0	Input/Output on the QL	24

5.1	Serial I/O	25

5.2	File I/O	26

5.3	Screen and Console I/O	27

6.0	Qdos Device Drivers	31

6.1	Device Driver Memory Allocation	32

6.2	Device Driver Initialisation	32

6.3	Physical Layer	33

6.4	The Access Layer	34

7.0	Directory Device Drivers	38

| 7.1 | Initialisation of a Directory | Driver | 39 |
| --- | --- | --- | --- |
| 7.2 | Access Layer |  | 40 |
| 7.3 | Slaving |  | 44 |

8.0	Built-in Device Drivers	46

Contents continued

9.0	Interfacing to SuperBASIC	47

9.1	Memory Organisation within the SuperBASIC Area	47

9.2	The Name Table	48

9.3	Name List	49

9.4	Variable Values Area	49

9.5	Storage Formats	50

9.6	Code Restrictions	52

9.7	Linking in New Procedures and Functions	52

9.8	Parameter Passing	52

9.9	Getting the Values of Actual Parameters	53

9.10	The Arithmetic Stack Returned Values	54

9.11	The Channel Table	55

10.0	Hardware-related Programming	56

10.1	Memory Map	56

10.2	Display Control	57

10.3	Display Control Register	58

10.4	Keyboard and Sound Control	58

10.5	Serial I/O	59

10.6	Real-time Clock	59

10.7	Network	59

10.8	Microdrives	60

| 11.0 | Adding Peripheral Cards to the QL | 63 |
| --- | --- | --- |
| 11.1 | Expansion Connector | 63 |
| 11.2 | CPU Interface | 64 |
| 11.3 | Peripheral Card Addressing | 65 |
| 11.4 | Add-on Card ROMs | 66 |

12.0	Non-English QLS	67

12.1	Video	67

12.2	Non-English-language	Keyboards	68

12.3	Character Set	68

12.4	Special Alphabets	69

13.0	Manager Traps	69

14.0	I/O Management Traps	93

15.0	I/O Traps	98

/

16.0	Vectored Routines	134

17.0	Qdos System Standards	157

18.0	Qdos Keys	158

18.1	Error Keys	158

18.2	System Variables	159

18.3	SuperBASIC Variables	161

18.4	Offsets On BASIC Channel Definitions	164

18.5	Job Header And Save Area Definitions	164

| 18.6 | Memory | Block Table | Definitions | 166 |
| --- | --- | --- | --- | --- |
| 18.7 | Channel | Definitions |  | 166 |

18.8	File System Definition Blocks	168

18.9	Screen Driver Data Block Definition	169

18.10	Queue Header Definitions	170

18.15	List Of Vectored Routines	176

| 19.0 | Doing Business with Sinclair | 178 179 180 |
| --- | --- | --- |
| 19.1 | How To Offer A Product To Sinclair |  |
| 19.2 | Where Software Products |  |
|  | Should Be Sent For Review |  |
| 19.3 | How Products Are Reviewed |  |
|  | And What Sinclair Are Looking For | 181 |
| 19.4 | Contractual Options In Dealing With Sinclair Research | 182 |
| 19.5 | Promotion And Distribution | 184 |
| 19.6 | Summary | 185 |

20.0	Bibliography	186

1.0 About this Guide

This guide describes the methods which may be used for machine code

programming on the QL. Its contents are also relevant to compiler

writers who must implement a run-time library for other languages. This guide describes only those techniques which are specific to the QL. It does not contain a general description of 68000 or 68008 assembly language programming: this information can be obtained from a number of different sources, details of which may be found in the bibliography. It is, therefore, strongly recommended that a reference book describing 68000 assembly language be consulted before attempting to understand this guide.

The guide also gives details of how various peripherals such as hard

disk interfaces, add-on memory and ROM cartridges may be added on to the QL, with many details about how the firmware for such devices should be written.

Readers may notice that there are no circuit diagrams or detailed

explanations of the QL's internal hardware structure in this manual.	 This is because it is not necessary to have such information in order to

write software for the QL. We have tried in the design of Qdos to

provide you with a stable interface to the machine through its operating system; everything you need is there and so long as you build your products using the interface provided there is no danger that any future upgrade of the QL will introduce an incompatibility with existing software products. We will, in short, continue to support all of the system routines documented in this guide, but specifically reserve the right to change the QL's hardware or firmware in any other way we think fit. Provision of circuit diagrams and the like would, apart from endangering the safety of our design patterns, be giving you a route to build products that rely on nonsupported elements in the QL's design.

The commercial section of this guide sets out the various options

offered by Sinclair Research for the distribution of QL Software. Its aim is to give you an idea of the way in which we work and the likely

channels through which a potential product would pass before it is

accepted for publication and offered for sale to our customers. The

section also gives information on the purchase and duplication of

Microdrive cartridges.

Finally, should you feel that anything essential is missing from this manual we would be very grateful if you would write and tell us. The address to write to is:

Software Publishing Department

(Technical Manual)

Sinclair Research Limited

25 Willis Road

Cambridge CB1 2AQ

2.0 Introduction to Qdos

Qdos is the QL operating system. It is a single-user multi-tasking

operating system: that is, it provides the means for several independent programs to run concurrently in the QL, but does not provide any mechanisms to prevent those programs from interfering with each other. Qdos can be thought of as a collection of several things:

1. A set of useful routines for performing functions such as memory allocation, Input/Output, etc.

2. A mechanism for maintaining lists of things to be done on interrupt, including the function of allocating slots of CPU time to programs which require them.

3. A mechanism for starting up the computer, and determining the configuration	of any add-on hardware that is connected to it.

The Qdos mechanisms for start-up are described in section 2.4. Once

start-up has been performed, Qdos does not "run" in the sense that traditional operating systems run: its pieces of code and data structures simply exist for programs to use. There is no Qdos "main program" that maintains continuous control of the machine: the SuperBASIC interpreter, which takes the place of the command interpreter found in traditional operating systems, is simply a program which runs on the QL and uses Qdos's facilities, albeit with a number of special provisions. It is possible, and indeed commonly done, to destroy the SuperBASIC interpreter completely, and yet still use all the facilities of the operating system.

Note that in this guide, hex numbers are preceded by a dollar sign ($)

as used in the Motorola assembly language format.

2.1 Memory Map

This section describes how Qdos maintains its RAM area. In the QL, the RAM starts with the screen RAM at address $20000, and the area available to Qdos starts at $28000. In an unexpanded QL, the RAM finishes at $3FFFF, whilst in a QL with expansion memory, the RAM may go up as far as $BFFFF. The Qdos initialisation routine determines the amount of RAM present and adjusts the position of its pointers accordingly.

The memory map is as follows:

SV_RAMT SV_RESPR

SV_TRNSP

SV_BASIC SV_FREE

SV_HEAP

2.1.1 Principles-

Base of system variables

Base of RAM

There is no memory management hardware in the QL. This means that all code must execute from fixed addresses in physical memory, and

that a piece of code may not be moved after it has been loaded into

memory. For this reason, memory is usually allocated in fixed size areas which remain in a fixed location until deleted. The SuperBASIC area is an important exception to this.

2.1.2 System Variables -

The Qdos system variables are a block of memory containing information required by the operating system.

This block is normally located at address $28000, but is not fixed at this address in principle. Applications programs should not rely on that

fixed address, but should get the address of the base of system

variables by calling the MT.INF trap (see section 13.0).

Some of the system variables can usefully be monitored by applications programs, and some of them can safely be altered. A complete list of the system variables, each with its size and offset from the base of system variables, is given in section 18.2.

Included in the system variables area are a set of longword pointers indicating the locations of the other areas in the memory map.

2.1.3 System Management Tables-

Immediately above the system variables are various tables used by Qdos to maintain the list of jobs and various other pieces of information. The supervisor stack also resides in this area.

2.1.4 Common Heap Area-

The common heap area contains the channel definitions which are maintained by the I/O sub-system, together with the working storage) required by the I/O drivers or programs. The allocation of space in this area is carried out either by device drivers, when invoked, or directly by jobs. There are two traps provided to allocate and release space in this area: MT.ALCHP and MT.RECHP (see Section 13.0). The heap allocations of a job are automatically	released when the job is removed.

The common heap is an example of the use of a general heap mechanism provided by Qdos, which operates in the way described in the entry for MT.ALLOC in section 13.0.

The user code needs to retain one pointer to the free space in the heap. This is a long word and is a relative pointer to the free space in the heap. When the heap has no free space, either because it does not exist, or because it is full, this pointer is zero.

2.1.5 Free Memory Area-

The free memory area is used by Qdos as a buffer memory for the Microdrives, or, if Qdos is suitably extended, for other filing system devices. The area is structured as a collection of slave blocks, that is,

blocks which are associated with a physical block on a medium. When memory is allocated in another area which would encroach on the free memory area, Qdos must remove one or more slave blocks. Before such a removal takes place, Qdos ensures that a true copy of the information is present on the medium.

Whilst the common heap grows upwards into the free memory area, the areas above it grow downwards into it. As there are three areas above it (the resident procedure area, the transient program area and the SuperBASIC area), special provisions are made so that all three can grow at the appropriate times.

2.1.6 SuperBASIC area-

The SuperBASIC interpreter owns a special area located immediately above the free memory area: this area is used for all the interpreter's storage requirements such as the SuperBASIC program, its variables, its table of I/O channels and the interpreter's working storage. This area is noteworthy	in that it can be moved by Qdos without the knowledge of the SuperBASIC interpreter if an area above it needs to grow, or if the SuperBASIC area itself needs to shrink. Its size may also be altered. The mechanism which makes such movement or alteration in size possible operates as follows.

All references to the SuperBASIC area are made relative to the address register A6, and the value of A6 on entry to the interpreter is adjusted by Qdos to the current base of the SuperBASIC area (which is held in the system variable SV_BASIC), offset by the length of the interpreter's job header (currently $68 bytes).

The SuperBASIC interpreter divides its working area into several portions, details of which may be found by looking at the BV definitions in section 18.3. All of the pointers to these various portions are also relative to A6.

2.1.7 Transient Program Area-

The transient program area is the area of memory into which the user's applications programs are loaded. Each job is allocated a block of

memory in the transient program area, which it keeps until it is deleted:

this area is used for the job's code, data and stack. Programs loaded in this way are not normally re-entrant, but it is relatively straightforward

to use the mechanisms in the system to set up a single piece of code which is shared by several different jobs with different data areas.

There is no safe way of determining a priority where a program will be loaded, therefore programs are normally position independent (see section 3.1 on jobs).

2.1.8 Resident Procedure Area-

Memory allocated in this area is unavailable to the operating system. The system knows only two things about the resident procedure area: how to allocate memory in it, and how to release it completely. Both of these operations can only be carried out when there are no transient programs in the machine, due to the fact that the transient program area cannot be moved. Normally, the allocation is done immediately after start-up, and deallocation is never performed.)

The area is normally used to load in machine code procedures and functions written to extend the SuperBASIC language (see section 9.7), and occasionally for loading in the code of device drivers when these are not located in ROM in an add-on device.

2.2 Calling Qdos Routines

There are two categories of Qdos routines available to the user: traps and vectored routines. The mechanism for calling a routine is different for each of these two categories.

2.2.1 Traps-

Traps are called using the 68008 TRAP #n instruction: on the QL, this has the effect of a subroutine call to a defined location which has the side effect of saving the status register and entering supervisor mode.

Of the sixteen trap numbers available on the 68008, numbers 0 to 4 inclusive are defined for use by Qdos, the remainder being free for the user to redirect to his own routines. Roughly speaking, the traps are utilised as follows:

| TRAP TRAP | #0 #1 | Special trap for entering supervisor mode Manager traps - routines which perform overall control |
| --- | --- | --- |
|  |  | of the QL hardware and of the operating system's resources |
| TRAP | #2 | Input/Output management traps (I/O traps which allocate resources) |
| TRAP | #3 | Input/Output traps which do not allocate resources |
| TRAP | #4 | Special trap for the SuperBASIC interpreter. |

Traps are called by setting up any required parameters in registers A0-A3 and D1-D3, setting up the code for the required trap in D0 (usually with a MOVEQ instruction), then executing the TRAP instruction. Trap routines do not affect D4 to D7 or A4 to A6. There are, however, a few defined cases which are exceptions to this.

When the TRAP operation is complete, control is returned to the program at the location following the TRAP instruction, with an error key in all 32 bits of D0. This key is set to zero if the operation has been completed successfully, and is set to a negative number for any of the system-defined errors (see section 17.1 for a list of the meanings of the possible error codes). The key may also be set to a positive number, in which case that number is a pointer to an error string, relative to address $8000. The string is in the usual Qdos form of a word giving the length of the string, followed by the characters.

Note that all traps can return the error code ERR.BP (for bad parameter). Note also that the condition codes may not be set according to the error code on return from a trap, thus a program wishing to detect an error should execute a TST.L D0 instruction immediately after the TRAP instruction.

Details of all the Qdos traps are given in sections 13.0-15.0.

2.2.2 Vectored Routines-

In addition to the routines accessed by traps, there are several utility routines which are available to the applications program: their

addresses are held in a vector table which is located in the ROM

starting at address $C0. A vectored routine can be accessed by the

following code:

MOVE.W	VECTOR_ADDRESS,An

JSR	(An)

where VECTOR_ADDRESS is the address of the vector table entry, and An is a suitable address register which is not required by the particular routine on entry.

There are some exceptions to this technique: for some vectored routines, the code is:

MOVE.W JSR

VECTOR_ADDRESS,An

$4000(An)

The entries in section 16.0 for vectored routines which require this treatment are suitably marked.

There are no general rules covering the handling of errors in vectored routines. Some routines return an error code in D0 in the same way as traps, but others use the technique of returning to one of a set of alternative return addresses. An example is the vectored routine

MD.SECTR, which returns to the location after the call if there is a "bad

medium" error detected, to the address 2 bytes later if there is a "bad sector header" error detected, and to the address 4 bytes later for a correct completion. Thus the correct code to trap these errors would be:

MOVE.W JSR BRA.S BRA.S

VECTOR_ADDRESS,An

$4000(An)

BAD_MEDIUM_ERROR

BAD_SECTOR_ERROR

* Code for processing a correct return starts here

"

“

“

BAD_MEDIUM_ERROR

* Code for processing a bad medium error starts here

"

“

“

BAD_SECTOR_ERROR

* Code for processing a bad sector error starts here

"

“

“

Obviously, a similar mechanism can be used with any number of error returns (including zero or one).

Complete details of the vectored routines are given in section 16.0, including information about the behaviour of each routine when an error occurs.

2.2.3 Atomic Actions-

In general, system calls are treated as atomic: while one job is in supervisor mode, no other job in the system can take over the

processor. This provides for resource table protection without the need for complex procedures using semaphores. If ajob needs to execute some action other than a single system call into which no other job must be allowed to intervene, it should enter supervisor mode before entering the code which performs this action. Supervisor mode is entered using TRAP #0. The stack pointer only is changed by this trap.

A job should only use 64 bytes on the supervisor stack, and all of the space used on this stack must be released before exiting supervisor mode. In general, there should be nothing on the supervisor stack when a manager trap is made.

Some system calls are only partially atomic, that is, when they have completed their primary function, some other job may gain a share of CPU time before control returns to the calling job. These partially atomic system calls must not be made from a job in supervisor mode. All of the scheduler calls (ie, TRAP #1 with D0=4, 5, 8, 9, $A, $8) fall into this category, as do all the I/O calls (TRAP #3), unless immediate return (timeout<>0) is specified.

A piece of code in supervisor mode can be interrupted by the frame (50/60 Hz) or external interrupts, so care must be taken, when writing interrupt servers, that the system's internal data structure is not modified, directly or indirectly, by system calls. In practice, since	 interrupt servers tend only to be moving data into or out of queues, this is not a serious limitation.

2.3 Exception Processing

There are three categories of exception traps on the 68008: user traps, traps for software error conditions, and traps for hardware interrupts. There is also one special hardware trap called "bus error', which can be used to trap bad conditions on the address bus: this trap is not supported by the QL hardware.

User traps 0 to 4 inclusive are treated as defined in sections 13.0 through 15.0.

User traps 5 to 15 inclusive, together with the software error traps for "address error", "illegal instruction", "divide by zero", "check array", "trap on overflow", "privilege violation" and "trace" are redirectable by the user on a per-job basis: see the entry for MT.TRAPV in section 13.0.

Traps and exception vectors which are not used by Qdos may be redirected through a table which is set up by a particular job.

If a job has set up a table of trap vectors for itself, then that table will automatically	be used when that particular job is being executed. The vector tables used by other jobs will not be affected. A job set up by, even if not owned by, a job which has set up a table of trap vectors, will use the same table as that job, until it is redefined.

If the job ID is a negative word, then the table will be set up for the calling job.

The table is in the form of a long word address for each trap or exception. They are in the following order:

$00	address error

$04	illegal instruction

$08	zero divide

$0C	CHK

$10	TRAPV

$14	privilege violation

$18	trace

$1C	interrupt level 7

$20	trap #5

$24	trap #6

$28	trap #7

$2C	trap #8

$30	trap #9

$34	trap #10

$38	trap #11

$3C	trap #12

$40	trap #13

$44	trap #14

$48	trap #15

$4C	end of table

All interrupts on the QL are auto-vectored, therefore there is no treatment of the 68008 vectored interrupt traps. Interrupts generated by the QL internally are level 2 auto-vectors: the interrupt handling mechanism includes the facility for detecting an interrupt on the EXTINTL (external interrupt, active low) line in the QL's expansion port. (See section 11.1 for details of the interface to the relevant hardware.)

It is also possible to generate a level 7 (non-maskable) interrupt: the treatment of this can also be redirected on a per-job basis. Pressing CTRL-ALT-7 on the keyboard generates a level 7 interrupt and also resets all communications	with the IPC: a suitable interrupt handler could be written to perform a warm start on the system to allow partial recovery from a crash.

2.4 Start-up

The first thing that Qdos does when the system is reset is to execute a

RAM test. This test determines the amount of contiguous RAM present, and if there is any RAM failure, hangs up the machine.

Qdos then initialises the system variables, the system management tables, and the SuperBASIC area.

The address $COOO is then checked by Qdos for the characteristic longword $4AFB0001: if this is found, Qdos links in the SuperBASIC procedures contained in the ROM, prints out the name of the ROM, and performs a JSR to its initialisation point (details of the correct format of the ROM are found in section 8.0 on ROM device drivers). It is perfectly in order for the code in this ROM to take over the machine completely and never return to the system, for example if another operating system were being booted.

Qdos then does the same for the other ROMs in the expansion slots.

If all of these ROMs return control to Qdos, the next action is to try to open a device driver "BOOT": if this is found, its contents are loaded as a SuperBASIC program and executed. If no device driver "BOOT" has been linked in, Qdos attempts to find a file "MDV1_BOOT" and load and execute its contents as a SuperBASIC program. If both of these attempts fail, Qdos starts up the SuperBASIC interpreter with an empty program memory.

3.0 Machine Code Programming on the QL

Four types of machine code are available to program the QL, each being used to perform quite different operations: jobs, SuperBASIC procedures and functions, tasks, and the operating system or extensions to it. Thus there are several differences in both the form in which they are written, and the way in which they are treated by Qdos.

3.1 Jobs

Most application programs written in machine code or compiled code will be in the form of jobs. A job is an entity which has a share of machine resources: it has a priority which allows it to claim time-slots of CPU activity, and it has a fixed-size area of memory where data and code can be stored: code normally starts at the bottom of the area, and data at the top. This area is located somewhere in the transient program area.

Note that the command interpreter is itself a job but with the exceptional characteristic that its data area is expandable.

A job also has the ability to own I/O channels or other jobs. There is no protection between jobs under Qdos, so that channels are available for use by all jobs. Ownership simply implies that when the owner of a channel or job is deleted, the owned channel or job is deleted also (this process continues recursively).

Jobs have three well-defined states: they are active, sharing CPU resources with other jobs; suspended, for example, waiting for I/O or another job; or inactive, occupying memory but not capable of using CPU resources.

The priority of a job can be zero, in which case it is suspended, and does not consume CPU time. It can in fact be suspended for its entire lifetime and never execute at all, which would be the case if it was simply used as a means of obtaining some memory into which data could be loaded. A job at any other priority level is active.

When a job is started, two parts of its area of memory have defined meanings: the bottom of the code area, and the stack, which is at the top of the data area. It is the programmer's responsibility to set up the

bottom of the code area, which should be in the following form for use

by Qdos utilities:

JMP.L	JOB_START DC.IN	$4AFB

DC.IN	JOB_NAME_LENGTH

DC.IN	'Nameofjob'

JOB_START

* Code begins execution here (assuming that the start address defined when the job was created was zero)

On the first occasion that a job is activated, (A6) points to the base of the job area, (A6,A4) points to the bottom of the data space, and (A6,A5) points to the top of the job area. There may be some information on the stack, which will be in the following form: (A7) points to the number of channels which have been opened for the jobbefore it was activated; above this is a sequence of longwords holding the channel IDs, and above these are a command string which may have been passed to the job. It is the programmer's responsibility when starting a job to set up this information: the SuperBASIC EXEC, EXEC_W commands and any utilities produced by Sinclair are compatible with this form.

Note that the normal sequence in Qdos is as follows:

1. reserve space for a job;

2. load its code in;

3. open its channels;

4. activate it.

Execution begins at an address specified when the job was created.

This is normally specified as zero, which is why the first thing in a job is normally a JMP.L instruction to the entrypoint of the code.

Since Qdos cannot give guarantees as to where a job will be loaded, it is usual to write jobs as position-independent code, although it is possible to avoid this constraint if a special relocating loader is used after the space for the job has been allocated.

The system job table holds information about the jobs within the system. The system variable SV_JBBAS  points to the base of the job table, and SV_JBTOP points to the top. The table is a series of longwords each of which points to a job control block: the contents of this are described in section 18.5. The job is identified to the system by its Job ID: this is a longword consisting of a word giving its position in the job table (in the least significant word), and a word of tag allocated by the operating system when the job is created (in the most

significant word).

The traps that may be called relating to jobs are as follows:

MT.lNF	returns the current job ID, plus miscellaneous information

MT.JINF	returns the status of a job

MT.CJOB	creates a job

MT.JOB	returns information	on a job

MT.RJOB	removes an inactive job

MT.FRJOB	forces removal of a job (whether inactive or not) MT.FREE	finds the largest space available for a job MT.TRAPV	sets the trap-vector table for a job

MT.SUSJB	suspends a job MT.REUB	releases a job MT.ACTIV	activates a job

MT.PRIOR	changes the priority of a job

A job terminates itself by calling MT.FRJOB with its own job ID (or -1,

which always refers to the current job).

3.2 SuperBASIC Procedures and Functions

The SuperBASIC command interpreter is job number zero. It behaves

like all other jobs in most respects, with the important exception that it

owns a special data area which is expandable, and may be moved without the knowledge of the interpreter. This area is located immediately below the transient program area.

Machine code procedures and functions which are added to SuperBASIC appear to the user to be identical to those which are built into the ROM. From the user's point of view they are routines which are executed from within job number zero, but which have certain constraints on the way they are coded.

The most important constraint is that A6 is used to point to the (moveable) base of the SuperBASIC data area. The system may move the area and change the value of A6 between instructions without the knowledge of the interpreter, therefore A6 must not be modified within the procedure or function, and its value must not be stored or used in calculation. This constraint may be side-stepped by entering supervisor mode, but A6 must then be restored on exit back to user mode (the processor is in user mode when a procedure or function is entered). The stackpointer A7 must of course be restored to its original value before exiting from the procedure.

On exit from the procedure, an error key is passed to the interpreter in DO.L: this must be setto zero if there was no error. The procedure or function can then be exited using an RTS statement.

If machine code procedures or functions are to be used either recursively or in recursive SuperBASIC procedures, they must obey the usual constraints of having no local variables and no self-modifying code.

Machine code procedures and functions are normally loaded into the

resident procedure area above the transient program area. This area can only be expanded or deleted when the transient program area is

empty, which is normally immediately after the machine is booted.

Trap #4 is the one special trap which relates to SuperBASIC procedures and functions. This trap is used to make the addresses passed to an I/O trap relative to A6, which is necessary when working with the SuperBASIC variables area. It only affects the following trap, and must therefore be called before each trap whose addresses are to be modified.

Details of parameter passing, function returns and other useful information about the SuperBASIC interface are given in section 9.0.

3.3 Tasks

Tasks are special pieces of code invoked under interrupt, usually as part of the physical layer of a device driver. They obey special rules according to the precise conditions under which they are called: these rules are described in the sections on device drivers (sections 6.0-8.0). The important restriction on tasks is that they must not allocate or release machine resources: this should only be done from within a job, or within the access layer of a device driver.

3.4 Operating System Extensions

Some parts of user-defined device drivers do not fit into any of the above categories: they are special routines called from within a job via the Qdos Input/Output sub-system (see section 6.0). These routines have their own rules, and these are described in the sections on device drivers (sections 6.0-8.0).

4.0 Memory Allocation

Memory is allocated differently in each area of the Qdos memory map.

• Memory in the resident procedure area is allocated using the traps

MT.ALRES and MT.RERES.

• Memory in the transient program area is allocated by the mechanisms described in section 13.0 for creation and deletion of jobs. The vectored routines MM.ALLOC and MM.LNKFR may be used within a job to perform primitive heap allocation inside that job's own data area.

• Memory in the SuperBASIC area is allocated by various mechanisms. The traps MT.ALBAS and MT.REBAS are used by the interpreter to change the size of the entire area, but are not normally used by anything else. The vectored routine BV.CHRIX is used to allocate space on the arithmetic stack: the interpreter itself cleans up this space on return from a procedure or function. Space in the remaining parts of the SuperBASIC area is usually allocated by the vectored routines being used to perform the operations that require the space, so that this allocation is invisible to the user, except that it

usually results in a modification of the value of A6.

• Memory in the free memory area is not allocated or deallocated by the user, except by the slave block mechanisms defined in section 7.0 on directory device drivers.

• Memory in the common heap is allocated and released by the traps MT.ALCHP and MT.RECHP. The area allocated in this way by a job is released when that job is deleted. The same mechanisms can be accessed from within device drivers via the vectored routines MM.ALCHP and MM.RECHP.

4.1 Heap Mechanism

The mechanisms for allocating and releasing heap space are common to various routines. They are as follows:

A heap is an area of memory which contains a linked list of used heap items, and a linked list of free heap items. Each heap item is an area of memory (which is a multiple of 8 bytes long), together with a pair of longwords: the first is the length of the heap item, while the second is a pointer (relative to itself) to the next heap item in the list. The use of relative pointers ensures that heaps may be moved.

A heap is set up by linking an area of ram(memory into a non- existent heap (free space pointer=0). A heap is expanded by linking an area of ram-e rnernory, preferably but not necessarily, contiguous with the current top of the heap, into the heap.

Provided the user code can remember the length of a heap item, all of the memory in it may be used by the code. On allocation of the heap item, the first long word holds its length, and so, if desired, this may be retained by the user code.

The user code requires to keep one pointer to the first free space item in the heap. This is a long word, and is relative. When the heap has no free space, either because it does not exist, or because it is full, this pointer is zero.

Releasing a heap item adds it to the list of free space items within the heap, and consolidates it with adjacent free spaces where appropriate.

5.0 Input/Output on the QL

A QL program uses I/O by accessing the Qdos. The IOSS in turn accesses the device driver for the appropriate device. The device driver is a piece of code which can perform low-level I/O routines for a particular device: that device may correspond to a piece of hardware, such as a serial port, or it may be some notional device occupying a piece of memory, such as a pipe, which is a communication channel between jobs.

QL I/O is performed through the IOSS using an I/O channel. The applications program opens a channel by passing a device name to the IOSS, which returns a channel/D. The IOSS and the built-in device drivers have the ability to recognize qualifiers appended to the actual name of the device which can direct the open operation in particular ways, such as identifying a file name, or selecting some hardware option. The program then uses the channellD to identify to the IOSS which channel it wishes to access when performing read or write operations on it. It can also close the channel, passing the channel lD to the IOSS. There may be several channels open which use the same device driver, such as multiple screen windows, or Microdrive files. For this reason, all the built-in drivers are re-entrant, as must be the user-defined drivers if they are to have the same capability.

The QL ROM contains drivers for several devices such as screen windows, serial ports, pipes, microdrives, and so on. The user can add his own device drivers for pieces of add-on hardware, or simply for additional functions with the existing hardware.

Note that a channel lD is not the same thing as a SuperBASIC channel number (denoted by #expression): the latter is the index of an entry in the SuperBASIC channel table which includes a channel lD. See sections 18.4 and 18.7 for details of the channel table.

5.1 Serial I/O

All device drivers have, at the very least, the capability to perform serial I/O: that is, the operations of reading bytes, writing bytes, and testing for pending input. Serial I/O is completely byte-oriented - unlike many operating systems there is no inbuilt record structure, which means that the user is free to superpose his own record maintenance in whatever form he wishes. I/O which is purely serial is completely redirectable: when different devices are being used, the device name passed to the channel open trap is the only thing that changes.

The IOSS supports one control character only, this being the newline

character, which is ASCII 10 ($0A). Whilst this has the disadvantage

that one cannot directly store files of graphics commands which can be retrieved by a simple copy, it does have the advantage that files containing arbitrary sequences of bytes cannot do irretrievable damage to the system by being copied to a device for which they were not intended. The serial driver has the option of supporting ASCII 13 as a newline, and ASCII 26 (CTRL -Z) as an end of file marker.

All serial I/O calls support a time-out feature, which may be zero (return immediately), indefinite (wait until the operation is complete), or finite (wait until the operation is complete, or for a set time, whichever is the sooner). This last feature makes it very easy to write code which, for example, puts up a menu only if the user hesitates.

The IOSS supports the following calls for serial I/O:

IO.OPEN	opens a channel IO.CLOSE	 closes a channel IO.PEND	tests for pending input IO.FBYTE	fetches a single byte

IO.FLlNE	fetches a line of bytes terminated by newline (ASCII 10)

IO.FSTRG	fetches a string of bytes IO.SBYTE	sends a single byte IO.SSTRG	sends a string of bytes

The fetch and send traps have several special meanings when used in conjunction with screen or console channels: for a more detailed description of these, see section 15.0 on I/O Traps.

For the fetch byte and fetch string traps, characters read from the keyboard are not echoed in the associated window, and cursor handling is left to the applications program.

5.2 File I/O

Qdos files appear to the applications program as arrays of bytes on a physical device, with an associated file pointer which gives the "current position" in a file. A file also has a header, which is normally 64 bytes long containing information about the file such as its name, length, etc. Further details concerning the format of the file header are given in section 7.0 on Directory Device Drivers.

The open call to a file system device supports several modes: old (exclusive), old (shared), or new (exclusive). New (overwrite) mode has a slot allocated in the open keys, but is not currently supported for Microdrives.	In addition, a special open key indicates that it is desired to open the directory of the medium for reading rather than a particular file; the directory cannot be explicitly written, but is maintained by the device driver when open calls and deletions are made.

Qdos supports a system of slaving, whereby 512-byte blocks of data are buffered in the free memory area (see section 4.0): all unused memory being taken for this area. The filing system may return from a write operation when that operation has only been performed on the slave block concerned; Qdos will later force the system to convert that slave block into a true copy of the data on the physical device. As a result of this mechanism, add-on filing devices normally support 512- byte logical blocks: however this blocking system is transparent to the applications program. A single slave block table is shared by all the directory drivers which want to use it to improve their performance.

In addition to the serial I/O operations described above, Qdos supports the following operations for file-system devices:

IO.FORMT IO.DELET FS.CHECK FS.FLUSH FS.POSAB FS.POSRE FS.MDINF FS.HEADS FS.HEADR FS.LOAD FS.SAVE

formats a sectored medium deletes a file

checks all pending operations on a file flushes buffers for a file

positions the file pointer absolutely

positions the file pointer relatively

gets information about the mounted medium

sets the file header

reads the file header

loads a file into memory saves a file from memory

The FS.FLUSH and FS.CHECK command are subtly different: FS.FLUSH ensures that all write operations are complete, whereas FS.CHECK ensures that all write and read operations (including prefetches) are complete.

5.3 Screen and Console I/O

The keyboard and screen devices are treated in a special way by Qdos, and have a large number of functions in addition to those available for purely serial I/O devices. Two types of device are supported: scr (for screen), which is a screen window, and con (for console), which is a screen window with an associated keyboard channel. The three channels #0, #1 and #2 which are opened by SuperBASIC are all console channels.

5.3.1 Display Modes -

The QL has two display modes (see the Concepts manual for details). The display mode can be set or read using the MT.DMODE trap, but

as this trap clears all screen windows, it should be used with great care. A program can also find out whether the user selected TV or monitor

at switch-on by inspecting the value of the system variable

SV_TVMOD.

There are two main coordinate systems used for screen I/O: these are the graphics coordinate system and the pixel coordinate system (see the Concepts manual for details). Note that in 256-pixel mode and for several commands in 512-pixel mode, the least significant bit of a dimension in the x-direction is ignored, so that a given pixel address refers to the same location in both modes. Some traps refer to character coordinates: these are based on the pixel coordinate system but are scaled by the current character spacing for the window.

5.3.2 Window Properties and Operations -

A window is an area of screen which may be in any position on the screen, subject to the restriction that its x-position must be an even number. A window may be of any size that does not run off the edge or bottom of the screen, subject to the same restriction. Windows may overlap, but the system does not store or retrieve the area of overlap, it being the user's responsibility to ensure that any information is not lost or garbled.

Each window will have its own particular set of characteristics: a border width, a border colour, a paper colour, a strip colour, an ink colour, a cursor position, a cursor increment, a flag which says whether the cursor is suppressed, a pair of font pointers, information about newline treatment, and graphics information. Details of the window definition block are given in the section 15.0.

The special traps for dealing with windows are as follows:

SD.PXENQ SD.CHENQ SD.BORDR SD.WDEF SD.CURE SD.CURS SD.SCROL SD.SCRTP SD.SCRBT SD.PAN SD.PANLN SD.PANRT SD.CLEAR SD.CLRTP SD.CLRBT SD.CLRLN SD.CLRRT SD.RECOL SD.SETPA SD.SETST SD.SETIN SD.FILL SD.SETMD

returns window information  in pixel coordinates

returns window information in character coordinates

sets the border width and colour

redefines a window

enables the cursor suppresses the cursor scrolls a whole window

scrolls the top part of a window

scrolls the bottom part of a window pans a whole window

pans the line the cursor is on

pans the right-hand end of the line the cursor is on clears a whole window

clears the top part of a window

clears the bottom part of a window clears the line the cursor is on

clears the right-hand end of the line the cursor is on recolours a window

sets the paper colour sets the strip colour sets the ink colour

fills a rectangular block in a window

sets the character writing or plotting mode

5.3.3 Screen Character Output Operations-

Newline characters receive slightly different treatment when bytes are being sent to a screen or console channel rather than to any other

device. In addition to being caused by a newline character, a newline is

automatically inserted when the cursor reaches the right-hand side of

the window; when this happens during an IO.SBYTE trap, the error code ERR.OR (for out of range) is also returned.

If the cursor is suppressed, the newline is held pending. It can be cleared by any call to position the cursor, or activated by any of the following events:

sending another byte or string;

changing the character size; activating the cursor; requesting the cursor position.

This feature allows the right-hand character squares to be used without generating stray blank lines.

The following additional operations apply to screen character output:

SD.FOUNT SD.SETFL SD.SETUL

SD.SETSZ

sets or resets the character fount

sets or resets hardware flash (256-pixel mode only)

sets or resets underlining

sets the character size and spacing

5.3.4 Graphics Operations-

The QL can perform line, arc or ellipse drawing on a window basis in

scaled coordinates. It also provides a primitive area flood routine. The traps are as follows:

SD.POINT SD.LlNE SD.ARC SD.ELlPS SD.SCALE SD.GCUR

SD.FLOOD

draws a point draws a line draws an arc draws an ellipse sets the scale

moves the graphics cursor

set or reset area filling

5.3.5 Special Properties of Console Channels-

For the console device, the IO.FLlNE trap behaves in a particular fashion: the characters typed are echoed in the console window, and the left and right cursor keys (with or without CTRL) are used to edit the line in the standard way. In addition, the cursor is automatically enabled.

An additional trap, IO.EDLlN, is provided for console channels, which invokes the line editor on a pre-defined string. The line-editor may be exited by typing ENTER, or by typing either the cursor-up or the cursor-down character.

The user can temporarily suspend screen output to a console channel by typing the freeze screen character (CTRL-F5). Output is resumed when any character is typed, but the character is ignored for all other purposes. If a non-indefinite time-out has been set for the suspended operation, it may return non-complete if the screen is frozen past the time-out period.

5.3.6 Special Keyboard Functions-

Several console channels may be open at the same time. If they are used by different jobs, it may be that more than one console channel is expecting input at a given time. When this occurs, the user may cycle round the list of console channels currently expecting input by typing the change queue character on the keyboard. The cursor in the console window to which keyboard input is currently directed will flash if it is enabled. Any enabled cursors in other windows will be steady.

The change queue character is normally CTRL-C (ASCII 3). It can be changed by modifying the system variable SV_CQCH.

The keyboard maintains a type-ahead queue of seven characters in the

8049 processor which controls it. In addition to this, there may be

more type-ahead in the queue for each console channel.

The keyboard auto-repeats on all keys except the keyboard change queue character, CTRL-Space (the SuperBASIC break) or CTRL-F5 (the freeze screen character). However, auto-repeat will not occur unless the type-ahead queue for the console channel to which input is currently directed is empty. The delay before auto-repetition begins is held in the system variable SV_ARDEL, and the interval between repetitions is held in SV_ARFRQ (both in multiples of 1/50th or 1/6Oth of a second). These can be altered by a program.

When CAPSLOCK is pressed, the system will jump to a user-supplied routine whose absolute address is held in the system variable SV_CSUB if the value of this is non-zero. This routine should restore all registers to their initial state before returning.

5.3.7 Extended Operations-

A special trap SD.EXTOP is provided to allow a program to invoke a user-supplied routine using the same environment that is passed to the routines in the screen driver. See the description in section 15.0 (I/O Traps) for a more detailed discussion of this trap.

6.0 QDOS Device Drivers

A user-supplied Qdos device driver is a collection of routines which allow an applications program to perform IOSS functions on a user- supplied device in the same way as such functions are performed on the devices built into the system. As these routines are linked into the system's lists in front of the corresponding system routines, they may be used to replace the system routines. At the very least, the device driver contains a set of routines for opening a channel, closing a channel, and performing serial I/O on that channel: these routines are called via the IOSS as part of the job that is performing the I/O. The driver may also include one or more tasks, that is, routines performed asynchronously with the calling job, usually under interrupt.

Such tasks, which are known as the physical layer of the device driver, normally communicate with the rest of the device driver, which is known as the access layer, using asynchronous queues. These queues are usually polled by the task at regular intervals, either on every occasion the scheduler is entered, or on every 50/60 Hz polling interrupt.

Drivers for file system devices use a slightly different, and more general, mechanism: this is described in section 7.0.

Both drivers and tasks are linked in to lists provided by the operating system. The following traps are used to add and remove items from

those lists:

MT.LXINT MT.LPOLL MT.LSCHD MT.LlOD MT.LDD

links in an external interrupt service task links in a 50/60 Hz polling service task links in a scheduler loop task

links in a device driver to the 110 system

links in a directory device driver to the file system

MT.RXINT, MT.RPOLL, MT.RSCHD, MT.RIOD and MT.RDD remove these links.

The QL provides several utility routines which are useful for various actions commonly performed in device drivers, such as decoding a

device name, performing queue operations, etc.

6.1 Device Driver Memory Allocation

Device drivers allocate memory in two areas: the device driver definition block and the channel definition block. The device driver definition block belongs to the driver itself, and is allocated by the code which sets up the driver when it is initialised and linked into the various lists. The channel definition block belongs to each I/O channel, and is allocated by the driver itself when a channel is opened. Various parts of the channel definition block are thereafter used by the lOSS for its own purposes.

In theory, the access layer can allocate space on the heap at other times: in practice this is not usually required. The whole system can be made re-entrant to allow several channels to be open with the same device driver and the same device driver definition block, but with different channel definition blocks.

Note that the system will certainly crash if the area of a channel definition block is deallocated and used for something else before the channel is closed, or if the area of a device driver definition block is deallocated and used for something else before the device driver is removed from the system's lists, for example if the device driver definition block is in a transient program which is force-removed.	This possibility can be obviated by allocating the block in the common heap with a job number of zero, or by allocating it in the resident procedure area.

Tasks must not allocate or release memory: this must be done for them by the access layer, or by the device driver initialisation code.

6.2 Device Driver Initialisation

The code to initialise a device driver must first allocate the space for the device driver definition block, usually by allocating some space in the resident procedure area, although any of the normal allocation mechanisms may be used.

The device driver definition block will normally have the following structure, assuming that A3 has been made to point to it:

$00(A3)

$04(A3)

$08(A3)

$0C(A3)

$10(A3)

$14(A3)

$18(A3)

$1C(A3)

$20(A3)

$24(A3)

$28(A3)

Link to next external interrupt routine Address of external interrupt routine

Link to next poll interrupt routine

Address of poll interrupt routine

Link to next scheduler loop routine

Address of scheduler loop routine

Link to access layer of next device driver

Address of input/output routine Address of channel open routine Address of channel close routine

Any further workspace required for the device driver

The initialisation code should fill in the addresses of the open, close and I/O routines, together with those of any of the routines for tasks that it will be employing. It should also fill in any preset data required in the remainder of the workspace.

Finally, the link routines described above should be called to include the driver in the operating system's lists.

Note that the structure of the first 24 bytes of the device driver definition block is not mandatory; however, it is desirable from the point of view of consistency that it be kept the same. The comments in later sections about the base of the device driver definition block being passed to the driver are only valid if the above structure has been used.

6.3 Physical Layer

The physical layer tasks are normally the ones which perform actual I/O under interrupt or polled control. They usually take data out of queues or put data into queues, the other end of such queues being maintained by the access layer.

When the operating system calls one of the tasks in the physical layer, it passes the task a standard set of values in some of the registers. These values are as follows:

D3	Number of 50/60Hz interrupts since last scheduler call

(scheduler loop only)

A3	Pointer to base of device driver definition block

A6	Pointer to system variables

A7	Supervisor stack - routines may use up to 64 bytes

6.3.1 External Interrupt Tasks-

An external interrupt task must check its own hardware to determine whether the interrupt was for itself or for some other driver. It may also need to clear the source of the interrupt at that point. If the interrupt was not for itself, it should return.

6.3.2 Polling Interrupt Tasks-

Polling interrupt tasks should only be used when critical timing operations are required. In common with the external interrupt tasks, they can interrupt atomic operations in the rest of the system, such as access layer calls to the same driver, so they should be used with great care.

6.3.3 Scheduler Loop Tasks-

Calls from the scheduler loop do not interrupt atomic tasks. This means that operations such as allocating or releasing memory can be performed safely. Note that it is quite common for the same routine to be included both in the scheduler loop and in the external interrupt list.

Scheduler loop tasks are called at around 50/60Hz when the machine is busy, and more frequently if the machine is idle.

All physical layer calls return with RTS. D0 to D7 and A0 to A6 inclusive may be smashed.

6.4 The Access Layer

The access layer consists of three routines: the channel open, the channel close, and the Input/Output routine. These routines are called for the appropriate driver by the IOSS in response to a user's trap instruction. In the case of the channel open, the routine is called in turn for each device driver in the machine until a driver's open routine returns correctly to indicate that it has recognised the device name. Due to this mechanism, an incorrect open routine may crash the whole system when an open to any device is attempted, whereas the other routines are only invoked in response to the particular device being used.

For all access layer calls, the values of A3, A6 and A7 are the same as) for the physical layer. The other registers have different meanings, as described below in the sections for the individual types of call.

All access layer calls return using RTS.

6.4.1 The Channel Open Routine-

When the channel open routine is called via the lOSS, the following registers are set in addition to A3, A6 and A7 which are as described above:

A0	address of the device name

D3	access code as defined in the IO.OPEN trap

The open routine should perform the following operations:

First, decode the name; the utility IO.NAME, which is described in section 16.0, will normally be used for this purpose. Return with ERR.NF in D0 if the name was not recognised by this driver, or with ERR.BN if the name was recognised, but some of the additional information was incorrect in value or format.

Then, if the device cannot be shared, check whether the device is in

use and prevent another channel from being opened to it. If the device is in use, return ERR.IU.

Finally, allocate some space for the channel definition block. Any buffers or working area required for each channel are normally allocated in the common heap. Return with ERR.OM if there was not enough memory to do this.

On return from the open routine, the following should be set:

A0	address of channel definition block

A7	stackpointer returned to its value at entry

D0	error return code (zero for a successful open)

The remaining registers may be smashed.

6.4.2 The Channel Close Routine-

When this routine is entered, in addition to the usual values of A3, A6 and A7, AO points to the base of the channel definition block.

The function of the close routine is simply to release the memory taken up by the channel definition block and to ensure that everything in the device driver definition block is tidy.

Under some circumstances, it may not be possible to close the channel immediately because there are bytes waiting to be transmitted by the physical layer. In this case, the physical layer must contain a scheduler loop task, and the close routine should set a flag for the physical layer to complete the release of the memory on the next invocation of that task in which it is possible to do so. When this happens, it is usually necessary to build in a special mechanism to cope with the undesirable event of a program closing a channel to a particular device, and then re-opening it immediately only to receive an "in use" error because the closed channel has not yet been cleared.

The close routine should return with zero in D0, as it is assumed that a close routine cannot fail. Only registers D0 to D3 and A0 to A3 may be smashed.

6.4.3 The Input/Output Routine -

The I/O routine is called once when an I/O call is made, and then, unless the time-out was set to zero, on every subsequent scheduler loop until the operation is complete or the time-out has expired.

In addition to the usual values of A3, A6 and A7, the following registers are set:

D0	The trap code passed to the lOSS (0 in top three bytes)

D1	Additional information as defined in the trap calls in section 15.0

D2	Additional information as defined in the trap calls in section 15.0

D3	Zero on the first entry for a given trap call, -1 thereafter

A0	Base of channel definition block

A1	Additional information as defined in the trap calls in section 15.0

A2	Additional information as defined in the trap calls in section 15.0

The I/O routine should return ERR.NC (not complete) if it cannot complete the operation immediately. If a string operation has been partially completed, the values in D1 and A1 (number of bytes transferred and buffer pointer) should be set appropriately so that the operation can continue on the next try. D0 should be zero on return if the operation has been completed correctly. Registers D2 to D7 may be smashed.

Since most of the code for handling serial I/O is common to all device drivers, the I/O routine usually calls one of the utility routines IO.SERQ or IO.SERIO (which are described in section 16.0). IO.SERQ assumes that the only function ofthe access layer is to move bytes in and out of a pair of queues pointed to by fixed positions in the channel definition block, while IO.SERIO assumes that the operations required of it can all be made up out of three primitive routines for sending one byte, fetching one byte, and checking for pending input, such routines being supplied by the writer of the device driver.

Note that channels are assumed to be bidirectional; it is the responsibility of the I/O routine to trap an operation in a direction that is not allowed.

Note also that output operations which appear to the user as complete have merely completed the access layer call correctly: there being no general way in which the user can ascertain whether the physical layer has in fact completed the operation.

7.0 Directory Device Drivers

Drivers for devices which have a directory and form part of the filing system have a somewhat extended set of functions. For directory device drivers, there are three blocks in which memory is allocated, rather than two: these are the directory driver linkage block, the physical definition block and the channel definition block.

There is one directory driver linkage block for each directory driver: it is an extended form ofthe device driver definition block as found in a non-directory device driver. The block contains information about how to use the driver, together with the links in the operating system's lists.

Each directory driver may control up to 8 drives (numbered 1 to 8). Each drive has one physical definition block: this contains the drive number and information about the medium.

For each I/O channel that is open, there is an open channel definition block.

The file system is assumed to be composed of 512-byte blocks: thus a

byte within a file is addressed by the lOSS by a block number and a byte number within that block. It is of course possible to have a different physical block size, but the mapping ofthe lOSS structure onto the physical structure will be less convenient.

Each file is assumed to have a 64-byte header (the logical beginning of file is set to byte 64, not byte zero). This header should be formatted as follows:

$00

$04

$05

$06

$0E

$34

$38

$3C

long byte

byte

8 bytes

2+36 bytes long

long long

file length

file access key (not yet implemented - currently always zero)

file type

file type-dependent	information filename

reserved for update date (not yet implemented)

reserved for reference date (not yet implemented)

reserved for backup date (not yet implemented)

The current file types allowed are: 2, which is a relocatable object file;

1, which is an executable program; 255 is a directory; and 0 which is anything else. In the

case of file type 1,the first longword of type-dependent information holds the default size of the data space for the program.

7.1 Initialisation of a Directory Driver

The initialisation routine should firstly allocate room for the directory driver linkage block, and then write into it the information aboutthe driver routine addresses, the length ofthe physical definition block required for each drive, and the drive name. Note that for directory drivers, the decoding of the device name is performed by the lOSS, not by the open routine in the device driver as in non-directory drivers: the function of the open routine is to search for the file name within the given drive. The linkage block may be allocated in the resident procedure area if the driver is resident there, but will usually be in the common heap. The system will crash if the linkage block is overwritten without the driver being unlinked.

When this has been done, the traps MT.LXINT, MT.LPOLL, MT.LSCHD and MT.LDD can be called to link the driver and any associated tasks into Qdos.

The format of the directory driver linkage block is as follows (assuming that A3 has been made to point to it):

$00(A3)	link to next external interrupt routine

$04(A3)	address of external interrupt routine

$08(A3)	link to next 50/60 Hz interrupt routine

$0C(A3)	address of 50/60 Hz interrupt routine

$10(A3)	link to next scheduler loop routine

$14(A3)	address of scheduler loop routine

$18(A3)	link to access layer of next directory driver

$1C(A3)	address of input/output routine

$20(A3)	address of channel open routine

$24(A3)	address of channel close routine

$28(A3)	address of entry for forced slaving

$2C(A3)	reserved

$30(A3)	reserved

$34(A3)	address of entry to format medium

$38(A3)	length of physical definition block

$3C(A3)	word-length of drive name characters of drive name

(e.g. MDV)

Note that a directory driver must have at least 40 bytes of RAM for the linkage block.

7.2 Access Layer

The access layer of a directory driver contains five routines: the channel

open/file delete routine, the close routine, the I/O routine, the forced

slaving routine and the format routine.

For all directory device driver access layer calls (including open), A0 points to the base of the channel definition block when each routine is called. However, the format of the block is somewhat different:

The first $18 bytes are reserved for the lOSS.

$18(A0)  FS_NEXT	long

$1C(A0)  FS_ACCES	byte

$10(A0)  FS_DRIVE	byte

$1E(A0)  FS_FILNR	word

$20(A0)  FS_NBLOK	word

$22(A0)  FS_NBYTE	word

$24(A0)  FS_EBLOK	word

$26(A0)  FS_EBYTE	word

$28(A0)  FS_CBLOK	long

$2C(A0) FS_FNAME	2+36 bytes

$58(A0) FS_SPARE	72 bytes

link to next file system channel access mode (03 on open call,

-ve on delete)

drive ID

number of file on drive

block number containing next byte next byte from block

block number containing byte after EOF

byte after EOF

pointer to slave block table for current slave block which may hold current/next byte

file name

spare

A1 points to the physical definition block, which is formatted as follows:

The first $10 bytes are reserved for the lOSS.

$10(A1)    FS_DRIVR	long

$14(A1)    FS_DRIVN	byte

$16(A1)	FS_MNAME	2+10 bytes

$22(A1)    FS_FILES	byte

pointer to access layer link for driver

drive number medium name

number of files open on this medium

7.2.1 The Channel Open/File Delete Routine-

The function of the open routine depends on the access mode. This may have been passed to the lOSS in D3 if the open routine was called as a result of an IO.OPEN trap, or it may be a negative number, which would be the case if the routine has been entered as a result of an IO.DELET trap.

In order to understand the open routine, it is necessary first to understand the way in which Qdos handles device names. When a device name is passed to the lOSS as a result of an open or delete call, the lOSS looks for a match in its lists of device drivers and directory device drivers. The matching mechanism for non-directory device drivers is defined within the open routine for that driver. The matching mechanism for directory device drivers is as follows. The first characters of the name are checked against the drive name in the directory driver linkage block (which is put there when the driver is initialised), and these are expected to be followed by a drive number between 1 and 8, followed by an underscore, followed usually by the filename. If a match is found, the file system looks to see if there is a physical definition block for that drive already in existence. If there is not, a physical definition block is created in the system's table of physical definition blocks (the drive ID in the channel definition block is an index to this table). Note that the file system has no knowledge of whether a drive is actually connected, and will set up the definition block regardless.

The lOSS then checks to see if this is the second or subsequent open to a shared file: if this is the case it generates the complete channel definition block itself, setting FS_NBYTE to $40, and copies the remaining information from the channel definition block for the first open. The directory driver's open routine is not called. Otherwise, the lOSS calls the open routine, passing it the file name in the channel definition block.

On entry to the open routine, the following registers are set:

A0	base of channel definition block

A1	base of physical definition block

A3	base of directory driver linkage block

A6	base of system variables

The channel and physical definition blocks are all set to zero except for the following, which are filled in by the lOSS:

FS_NEXT FS_ACCES FS_DRIVE FS_FNAME FS_DRIVR

FS_FILES

link to next file system channel access mode

drive ID

file name

pointer to directory driver access layer

number of files open on this drive (maintained by lOSS)

In the case of a device with removable media, the open routine should find out the name of the medium and install it in FS_MNAME. It should also look at the access mode to find out which operation is required. If the required operation is delete, it should perform that operation and return, but if the required operation is another sort of open, then it should fill in the appropriate portions of the channel definition block, namely FS_FILNR, FS_EBLOK, FS_EBYTE, FS_NBLOK and FS_NBYTE. FS_CBLOK is a pointer to the slave block table which may be filled in as an indication to the I/O routine that the block it is looking for may be slaved there. The I/O routine must check this however, normally by searching the slave) table.

The lOSS will free the channel definition block on exit from the open routine if the action was a delete or if the open routine returns an error key in D0.

The maintenance ofthe directory structure of the medium is the responsibility of the open and close routines - the lOSS plays no part in this. Equally, the open routine is responsible for understanding the meaning of the access mode and reacting accordingly.

The open routine may smash registers D1 to D7 and A1 to A5 inclusive before returning. D0 isthe error key, and the remaining registers should be preserved.

7.2.2 The Channel Close Routine-

As far as the lOSS is concerned, this routine behaves in the same way as for a non-directory device driver. It is of course necessary for the close routine to maintain the directory structure of the medium, so its operation will normally be rather more complicated.

The close routine for a directory device driver has two additional functions: it must unlink the channel from the list of files open, and must decrement the FS_FILES field in the physical definition block, which gives the number of files open on the medium. Suitable code for performing these operations and ending the close routine isas follows:

*get address of physical definition bLock into A2

| MOVEQ | #O,DO | top three bytes must be be clear |  |
| --- | --- | --- | --- |
| MOVE.B | FS_DRIVE(AO),DO | get the drive ID |  |
| LSL.B | #2,DO | convert it to a table |  |
|  |  | offset |  |
| LEA.L | SV _FSDEF(A6),A2 | getbaseofPDBtable |  |
| MOVE.L | (A2,DO.W),A2 | get address from |  |

* now decrement the file count

SUBQ.B    #1,FS_FILES(A2)

*now unlink the file

LEA	 FS_NEXT(A0),A0

LEA	SV_FSLST(A6),A1

(base+offset)

get address of link pointer

…and pointer to start of linked list

MOVE.W

JSR LEA

UT.UNLNK,A4

(A4)

-FS.NEXT(A0),A0

routine to unlink an item

restore A0 to base of channel def

MOVE.W	MM.RECHP,A4

JMP	(A4)

routine to release channel def space

call it, and exit from the close

The close routine must also initiate the process of tidying up any slave blocks remaining for that channel. It need not force the slave blocks to be made into true copies itself, but it must be guaranteed that the copying will happen without further intervention by the calling program.

7.2.3. The Input/Output Routine _

This routine also appears to the IOSS to be identical for both directory and non-directory device drivers, though once again the routine is usually rather more complex for most normal file system devices. The main difference is that the I/O routine for a random access file system device must take into account the current block and position as provided by the IOSS, since these may have been updated by the IOSS as a result of a file pointer positioning trap.

7.3 Slaving

The area of memory between SV_FREE and SV_BASIC is used by the

filing system as temporary storage for file slave blocks and for the slave

block table. A slave block is a block of 512 bytes of data. The slave block table is a table of 8 entries whose start point is held in the system variable SV_BTBAS and whose top is held in the system variable SV_BITOP; the system variable SV_BTPNT points to the most recently allocated slave block table entry. The address of a slave block, relative to the base of system variables, is equal to 512/8 times the offset of the corresponding entry in the slave block table from the beginning of that table.

Currently, only the first byte of each slave block table entry is used by Qdos itself: the remaining bytes are available for use by the driver. This byte is divided into two four-bit nibbles. The most significant nibble contains the drive identifier (0 ..15), and the least significant nibble is a code indicating the status of the block. The byte is formatted as follows:

$00	unavailable to filing system

$01	empty block

$x3	block is true representation of file

$x7	block is updated, awaiting write

$x9	block is awaiting read

$xB	block is awaiting verify

x is the drive ID for this file

For Microdrives, the remaining space in each slave block table entry is laid out as follows:

BT_PRIOR BT_SECTR BT_FILNR BT_BLOCK

01	byte

02	word

04	word

06	word

available for slaving algorithms physical sector number*2

file number

block number within the file

It is left to the device driver to decide what the slave blocks are used for but it must be prepared to release a slave block if requested to do so by the memory manager. This is done by calling the driver's forced slaving routine with the following parameters:

A1	points to the base of the offending slave block

A2	points to the physical definition block

A3	points to the base of the directory driver linkage block

Registers D0 to D3 and A0 to A4 inclusive may be smashed. There may not be an error return to this routine.

Typically the slave blocks are used to buffer data being written to a device, the actual writing being carried out by an asynchronous task.

Searching for an empty slave block involves performing a linear search through the slave"block table, usually starting from SV_BTPNT or SV_BTBAS. The status of each entry in the table must be checked and only those blocks which are empty or true representations should be taken. When a new block is allocated SV_BTPNT should be updated to point to the allocated block. Allocating slave blocks is a form of memory allocation and should only be carried out by access layer or scheduler loop calls.

This position in memory of a slave block which corresponds to a slave block table entry may be calculated using the following code:

MOVE.L	A4,DO	A4 is pointer	to slave block	table	entry

*

*form	offset	into	slave	block	table,	gives

*slave block no.*8; entries are 8 bytes wide in table

*

SUB.L   SV_BTBAS(A6),D0

LSL.L   #6,D0                multiply by 64 (8*64=512)

MOVE.L  D0,A5

ADD.L   A6,A5                add offset to system

variable base

* A5 now has base address of slave block

7.3.1 The Format Routine

This routine is to a large extent independent of the other routines. It is called with the drive number in D1, a pointer to the medium name in A1, and a pointer to the directory driver linkage block in A3.

It should return the error code in D0, the number of good sectors in D1 and the total number of sectors in D2. Registers D3 to D7 and A0 to A5 inclusive may be smashed.

8.0 Built-in Device Drivers

The following devices are built in to the QL ROM:

CON_wXhaxXy_k	Console I/O

window area "w" by "h" pixels, top left hand corner at pixel position "x", “y”

keyboard type-ahead buffer length "k" characters.

The size and position are defined in terms of pixels on a 512 x256 display map (position 256x128 is the centre of the screen in both display modes).

Default CON_448x180a32x16_128

SCR_wXhaxXy	Screen output

window definition is as for CON. Default SCR 448x180a32x16

SERnpz	RS232 serial I/O

port "n",

"p" indicates parity: E,O,M,S for even, odd, mark or space parity,

"z" indicates protocol: R indicates raw data,

Z or C indicates that ctrl-Z is used as an EOF marker,

C indicates that ASCII 13 is to be exchanged with ASCII 10.

Default SER1R no parity.

NETI_nn	Serial network output

link from node "nn"

NETO_nn	Serial network input

link to node"nn"

PIPE_n	Job connection and synchronisation

if "n" given it is an output pipe of length n bytes,

otherwise it is an input pipe connected to the channel lD passed in D3.

MDVn_name	Microdrive file

MDV1 refers to Microdrive "1".

Within device names, no distinction is made between upper and lower case letters.

9.0 Interfacing to SuperBASIC

When writing SuperBASIC procedures or functions in machine code, there are several things that an applications programmer may want to do: he may wish to look at or modify the information held in SuperBASIC variables and arrays, he may wish to access or modify the SuperBASIC list of I/O channels, and he may wish to reserve and use space on the arithmetic stack. He will also, of course, wish to access the list of parameters passed to the routine and return values either to those parameters or in a function return. In order to do this, it is

necessary to understand the data structures used by the interpreter and to emulate the interpreter's techniques for manipulating them.

9.1 Memory Organisation within the

SuperBASIC Area

The SuperBASIC area contains twelve distinct areas:

the job header,

the SuperBASIC work area, the name table,

the name list,

the variable values area, the channel table,

the arithmetic stack, the token list,

the line number table, the program file,

the return list, the buffer.

There are also various other stacks used by the interpreter.

The job header is located at the bottom of the SuperBASIC area, and looks just like any other job header (see section 18.5). Immediately above this is the SuperBASIC work area; this is an area of fixed storage used for the working variables of the interpreter. Included in these working variables are pointers to the other areas: the interpreter can not only shuffle these areas around, but may ask Qdos to change the size of the whole SuperBASIC area.

The organisation of this area is shown in section 18.3. Throughout normal operation of the interpreter, A6 points to the base of the SuperBASIC work area, the whole of which may move between instructions, with a corresponding change in A6. All the pointers are, of course, relative to A6, so that their values need not be changed when the SuperBASIC area is moved.

The name table, the name list and the variable values area are required by the applications programmer in order to access and/or modify SuperBASIC variables and parameters. The channel table is required in order to access SuperBASIC I/O channels, and the arithmetic stack (usually abbreviated to RI stack) is a convenient area in which to reserve storage, and is also where parameters are passed. The remaining areas are not described in this document.

9.2 The Name Table

All variables, procedure names, parameters and even expressions are handled through the name table. This is a regular table of eight byte entries, but the entries hold different information according to the type of entry.

The entries may be as follows:

Byte 0 of the name table has an additional usage during parameter passing: see section 9.8.

The Name pointer is a pointer to an entry in the name list (see the following section). A name pointer of -1 indicates a nameless item

such as the value of an expression; any other negative pointer indicates a pointer to another entry in the name table of which this entry is a copy.

The Value pointer is a pointer to an entry in the variable values area (see section 9.4). A value pointer of -1 indicates that the value is undefined.

Since all these areas may move during execution, the pointers are offsets from the base of each area. For the RI stack, the base is at the high address; for the others it is at the bottom.

Note that functions written in SuperBASIC are typed according to whether the name ends in % ,$ or neither. Functions written in machine code, in common with procedures written in SuperBASIC or machine code, have no type.

The entries for expressions and substrings are for use within the expression evaluator: the applications programmer would not normally use them.

9.3 Name List

The names in the name list are stored as a byte character count followed by the characters of the name. Note that this format is different from all other uses of strings in Qdos in which a word character count is used.

9.4 Variable Values Area

This area is a heap in which the values are stored. The format for each type of data item is given in the following sections.

I

9.5 Storage Formats

9.5.1. Integer Storage

An integer is a 16-bit two's complement word.

9.5.2 Floating Point Storage

A floating point number is stored as a two-byte exponent followed by a four-byte mantissa.

The most significant four bits of the exponent are zero, whilst the remaining twelve bits are an offset from -$800. The mantissa is two's complement and fractional, with bit 31 of the mantissa representing -1, and bit 30 of the mantissa representing +1/2. There are no implicit bits in the mantissa, so either bit 31 or bit 30 will be set for a normalized number, except in the special case of zero.

The value of the number is thus mantissa*2 to the power (exponent -$800). If the mantissa is viewed as two's complement absolute (as opposed to fractional), the value of the number is given by: mantissa *2 to the power (exponent-$81F). The $1 F corresponds to 31 decimal the length of the mantissa minus one.

Examples of floating point storage are as follows:

Hex	Decimal

0804

0801

07FF

07FF

0800

0000

50000000

40000000

40000000

80000000

80000000

00000000

10.00

1.00

0.25

-0.50

-1.00

0.00

9.5.3 String Storage

A string is stored as a word character count, followed by the characters of the string. The string storage always takes a multiple of two bytes.

Examples are as follows:

9.5.4 Array Storage

An array descriptor has a header which consists of a longword offset of the array values from the base of the variable value area, followed by the number of dimensions (word), followed by a pair of words for each dimension. The first word is the maximum index, the second word is the index multiplier for this dimension.

The storage of floating point and integer arrays is entirely regular. A floating point array takes 6 bytes per element, an integer array 2 bytes per element.

A string array is stored as an array of characters; except that the zeroth element of the final dimension is a word containing the string length. The final dimension defines the maximum length of the string. This is always rounded up to the nearest even number.

A substring is the result of internal slicing operations; this is a regular array of characters; the base of the indexing is one rather than zero.

Examples of Floating Point Storage

Floating point variables (in hex)

0000	0000	0000

0801	4000	0000

0800	8000	0000

0804	5000	0000

0.0

1.0

-1.0

10.0

Floating point arrays

base,2,3,3,2,1	DIM A(3,2)

Examples of String Storage	(Numbers are in decimal) String variable

4;65,66,67,68	"ABCD"

String array

base,2,3,12,10,1	DIM A$(3,10)

4;65,66,67,68,x,x,x,x,x,x	"ABCD"

9;49,50,51,52,53,54,55,56,57,x	"123456789"

O;x,x,x,x,x,x,x,x,x,x

1;32,x,x,x,x,x,x,x,x,x,

Substring array base, 1,3,1

65,66,67

""

""

A$(0,1 TO 3) as above

"ABC"

9.6 Code Restrictions

There is a simple set of rules for writing procedures in machine code for

SuperBASIC.

1. As the SuperBASIC program area is liable to move at any time while the execution is in user mode, all refererences to this area must be indexed by A6 or A7. A6 and A7 must never be saved, used in arithmetic or address calculations, and must never be altered, except by pushing or popping the A7 stack. In extreme circumstances it is possible to enter supervisor mode (Trap #0) to make the following action atomic. If this is done, A6 and User stack pointer must not be saved or manipulated	before entering supervisor mode, and they must be restored before exiting.

2. Not more than 128 bytes must be used on the user stack.

3. D0 must be returned as an error code (long).

4. D1 to D7 and A0 to A5 inclusive may be treated as volatile.

9.7 Linking in New Procedures and

Functions

New SuperBASIC procedures and functions written in machine code may be linked into the name table using the vectored routine BP.lNIT (see section 16.0). When the procedures and functions are in a ROM in the suitable format (see section 11.4), BP.INIT is called automatically. If the procedures and functions are to be stored in RAM, they should be loaded into the resident procedure area as, once added, they may not be removed except by re-booting the machine. It is usually convenient to load the code for calling BP.INIT to make the linkage into the same area, although this is not necessary.

9.8 Parameter Passing

The SuperBASIC interpreter passes parameters using a substitution

mechanism, which operates as follows. The interpreter first evaluates

any of the parameters that are expressions. A new entry is then created at the top of the name table for each actual parameter. In the case of a procedure or function written in SuperBASIC, this is followed by a null entry for any formal parameter that is missing from the actual

parameter list. The interpreter then swaps the new name table entries with the old name table entries corresponding to the actual parameters. In the case of a procedure or function written in machine code, the code is then called with A3 pointing to the name table entry for the first parameter in the list, and A5 pointing to the last ((A5-A3)/8 is the number of parameters).

If a local statement is encountered, the entry in the name table is copied to a new position at the top of the table, and an empty entry put in its place.

At the end of a SuperBASIC procedure or function, the parameter entries are copied back and local variables are removed. The parameter entries in the name table together with any temporary storage in the variable value table are then removed for all procedures and functions.

Byte 0 of the name table entry for a parameter has an additional meaning to that associated with a normal name table entry. The bottom four bits have the usual indication of type (0=null, 1=string etc.), but the top four bits are used to indicate the separator that was present after the parameter in the actual parameter list, together with information as to whether the actual parameter was preceded by a hash (#).

Thus the format of byte 0 is as follows:

h sss tttt

type: 0=null, 1=string, 2=floating point, 3=integer

type of following separator: 0=none, 1=comma,

2=semi-colon, 3=backslash, 4=exclamation mark,

5=TO

1 if the parameter was preceded by hash, otherwise 0

9.9 Getting the Values of Actual Parameters

For the purpose of using scalar (as opposed to array) parameters locally in the same way as "call by value" parameters in other high-level languages, it is expedient to use one of a set of four vectored routines which place the values of actual parameters on the arithmetic stack. Each routine assumes that all the parameters will be of the same type. It is passed the values of A3 and A5 which point to the name table entries for the parameters; it returns the number of parameters fetched

in the least significant word of D3, and the values themselves in order on the arithmetic stack with the first parameter at the top (lowest address) of the stack. These routines smash the separator flags. They are as follows: CA.GTINT gets 16-bit integers, CA.GTFP gets floating point numbers, CA.GTSTR gets strings, and CA.GTLIN gets floating point numbers but converts them to 32-bit long integers.

These routines may still be used when processing parameters of mixed type or when wishing to inspect the separators. To begin with, the values of A3 and A5 should be saved; then, for each parameter in succession, the separator flags are inspected, and the appropriate routine is called with A3 pointing to the parameter and A5 equal to A3+8, thus getting one parameter.

These routines smash D1, D2, D4, D6, A0 and A2. The error codes are returned in D0 and the condition codes.

A special technique is provided for use in those routines in which it is necessary for the user to be able to type in a string without quotes, as it's required for SuperBASIC commands involving device names. Firstly, the name is inspected to see if it is a valid set string variable. If it is, the string is fetched using CA.GTSTR; if it is not, the parameter's name itself is fetched from the name list, and converted to string form by changing its word count from byte to word, realigning the string if necessary. If a string is to be input without quotes, it must of course follow the rules for SuperBASIC names, as described in the Concepts manual.

9.10 The Arithmetic Stack Returned Values

The top of the arithmetic stack is usually pointed to by A1. Space may be allocated on the stack by calling the vectored routine BV.CHRIX: the number of bytes required is given in D0.L; D0 to 03 are smashed by the call. Since both the stack within the SuperBASIC area and the SuperBASIC area itself may move during a call, the stack pointer should be saved in BV_RIP(A6) before the call, and restored from BV_RIP(A6) after the call has been completed. The routine ensures that the restored value will be correct.

The vectored routines for getting parameters reserve their own space on the arithmetic stack.

The arithmetic stack is automatically tidied up both after procedures, and after errors in functions. To make a good return from a function, the returned value should be at the top (lowest address) of the stack with nothing below it (that is with both (A6,A1.L) and BV_RIP(A6) pointing to it) when the routine is exited. The type of the returned value should be in D4 (1 =string, 2=floating point number, 3=integer). Since SuperBASIC has no long integer type, long integers must be converted to floating point before returning.

Values can also be returned to parameters or, indeed, global variables, by putting the value on the arithmetic stack in the same way, pointing A3 to the appropriate name table entry and calling the vectored routine BP.LET. D0 is an error return, and D1, D2, D3, A0, A1 and A2 are smashed. If the actual parameter was an expression, no error will be given, but the value returned will be lost. The type of the returned parameter is determined by the name table entry, and the information on the arithmetic stack must be in the correct form.

Note that strings must be aligned on the arithmetic stack so that the character count is on a word boundary. All entries on the stack must be a multiple of two bytes long, so that a string of odd length has one byte at the end which contains no information.

9.11 The Channel Table

A channel number (#n) is an index to an entry in the SuperBASIC channel table. This is a table of items which are each of length CH.LENCH (currently $28) bytes. The base of the table is at BV_CHBAS(A6), and the top is at BV_CHP(A6); thus the base of the entry for channel #n is given by:

(n*CH.LENCH+BV_CHBAS(A6)) (A6)

The format of each table entry is as follows:

| $00 | long | the channellD |
| --- | --- | --- |
| $04 | float | current graphics cursor (x) |
| $0A | float | current graphics cursor (y) |
| $10 | float | turtle angle (degrees) |
| $16 | byte | pen status |
| $20 | word | character position on line for PRINT and INPUT |
| $22 | word | WIDTH of page |

If a channel entry is off the top of the channel table, or if the channel

ID is negative, there is no channel open to that # number.

10.0 Hardware-related Programming

10.1 Memory Map

The 68008 has one megabyte of address space. Although an unexpanded QL uses only the bottom 256 kbytes of this, the allocation for the remainder is determined and should be adhered to when designing add-on hardware. This is how it is made up:

$FFFFF    ______________

$EOOOO   _______________

$C0000  ___________

$40000  ___________

$28000   ___________

$20000   ___________

$10000   ___________

$0C000  ___________

$00000   ___________

The registers in the on-board I/O area are partially decoded: the details of this decode may vary according to different versions of the QL hardware - some versions will recognise any address in the entire area.

However, the address map normally used is the same for all QLs:

The display control registers are in the ZX8301 "Master chip", and the others are in the ZX8302 "Peripheral chip". The details of the QL hardware are rather obscure, and it is strongly recommended that these registers should not be used by applications programs, and should only be accessed via Qdos traps or vectored routines.

10.2 Display Control

The display format in memory is explained below: this format is specific to the QL and may change on future Sinclair products. It is, therefore, strongly advised that screen output be performed using only the standard screen driver, together with the MT.DMODE trap.

In 512-pixel mode, two bits per pixel are used, and the GREEN and BLUE signals are tied together, giving a choice of four colours: black, white, green and red. On a monochrome screen, this will translate as a four level greyscale.

In 256-pixel mode, four bits per pixel are used: one bit each for Red, Green and Blue, and one bit for flashing. The flash bit operates as a toggle: when set for the first time, it freezes the background colour at the value set by R, G and B, and starts flashing at the next bit in the line; when set for the second time, it stops flashing. Flashing is always cleared at the beginning of a raster line.

Addressing for display memory starts at the bottom of dynamic RAM and progresses in the order of the raster scan - from left to right and from top to bottom of the picture. Each word in display memory is formatted as follows:

High byte (A0=0)

D7 D6 D5 D4 D3 D2 D1 D0

G7 G6 G5 G4 G3 G2 G1 G0 G3 F3 G2 F2 G1 F1 G0 F0

Low Byte (A0=1)	Mode

D7 D6 D5 D4 D3 D2 D1 D0

R7 R6 R5 R4 R3 R2 R1 R0  512-pixel

R3 B3 R2 B2 R1 B1 R0 B0  256-pixel

R, G, Band F in the above refer to Red, Green, Blue and Flash. The numbering is such that a binary word appears written as it will appear on the display: ie R0 is the value of Red for the rightmost pixel, that is the last pixel to be shifted out onto the raster.

10.3 Display Control Register

This is a write-only register, which is at $18063 in the QL .

One of its bits is available through the Qdos MT.DMODE  trap: bit 3,

which is 0 for 512-pixel mode and 1 for 256-pixel mode.

The other two bits of the display control register are not supported by Qdos, these being bit 1 of the display control register, which can be used to blank the display completely, and bit 7, which can be used to switch the base of screen memory from $20000 to $28000. Future versions of Qdos may allow the system variables to be initialised at $30000 to take advantage of this dual-screen feature: the present version does not.

Bits 0,2,4,5 and 6 of the display control register should never be set to anything other than zero, as they are reserved and may have unpredictable results in future versions of the QL hardware.

10.4 Keyboard and Sound Control

The keyboard and loudspeaker are controlled by the QL 's second processor, which is an 8049 single-chip microcomputer: this is known in the QL as the Intelligent Peripheral Controller or IPC. The MT.IPCOM trap provides a set of commands that the CPU can send to the IPC over the serial link that connects them. This trap is discussed in greater detail in section 13.0.

When the keyboard is accessed via the console driver, the usual functions of debounce and conversion to ASCII are performed, in addition to the functions described in section 15.0. The other way of accessing the keyboard is to use the MT.lPCOM trap to monitor the instantaneous state of the keys directly: this is the only way of detecting multiple key presses (necessary for joystick input), or of detecting the state of the SHIFT, CTRL and ALT keys when no other key has been depressed. See the SuperBASIC Keywords entry on the KEYROW function for an example of the use of this technique.

The same trap, with different parameters, is used for sound generation.

10.5 Serial I/O

The QL's serial I/O should only be accessed via the serial driver, except for setting the baud rate, which is performed by the MT.BAUD trap. The only other function that can safely be performed by the user independently of the operating system is the checking of the transmit handshake lines (DTR on channel 1 and CTS on channel 2), which can be looked at by monitoring bits 4 and 5 of the microdrive status register respectively. Note that if the connector is rewired to use these pins as data lines, this function could be used to perform RS-232-C reception entirely in software, which would make it possible to perform XON-XOFF handshaking or split baud rate operation.

10.6 Real-time Clock

The QL's real-time clock is a 32-bit seconds counter. The three traps MT.RCLCK, MT.SCLCK and MT.ACLCK are used to read, set and adjust the clock. The vectored routines CN.DATE and CN.DAY are used to convert the time obtained to a string.

10.7 Network

This should not be accessed other than by the built-in device driver.

10.8 Microdrives

Normally, these should not be accessed other than by the built-in device driver. However, it is possible to write routines to access microdrive sectors directly in order to perform such functions as fast medium-to-medium copying or recovery of data from a damaged medium.

There are four vectored routines provided for this purpose: MD.READ, MD.WRITE, MD.VERIN and MD.SECTR. Use of these routines requires a detailed understanding of the microdrive hardware and format, and is probably beyond the scope of most users.

However, to use these routines the following code example shows how a microdrive is selected or de-selected. In later versions of the operating system it will be a vectored entry.

sys_wser

move.b	dO,-(sp)

wait

subq.w	#1,sv_timo(aO)

blt.s	set.mode

move.w	#(2OOOO*15-82)/36,dO

delay1

dbra	dO,delay1

bra.s	wait

set_mode

clr.w	sv_timo(aO)

and.b	#pc.notmd,sv_tmode(aO)

move.b	(sp)+,dO

or.b	dO,sv_tmode(aO)

and.b	#OFFh-pc.maskt,sv_pcint(aO)

exit

move.b	sv_tmode(aO),pc_tctrel

rts sys_rser

;save operation

;decrement timeout

;done?

;time= 18*n+42 cycles

;delay

;repeat until timeout expires

;clear wait

;not RS232

;either mdv or net

;disable transmit interrupt

;set pc

bclr or.b

bra.s

md_desel

moveq

moveq

bra.s

#pc..serb,sv_tmode(aO)

#pc.maskt,sv_pcint(aO)

exit

#pc.desel,d2

#7,d1

sedes

;set RS232 mode

;enable transmit

interrupt

;clock in deselect bit first

;deselect all

md_selec

moveq   #pc.selec,d2 subq.w	#1,d1

sedes

clk_loop

move.b	d2,(a3)

moveq	#(18*15-40)/4,d0

ror.l	d0,d0

bclr	#pc..sclk,d2 move.b	d2,(a3)

moveq	#(18*15-40)/4,d0

ror.l	d0,d0

moveq	#pc.desel,d2

dbra	d1,clk_loop

;clock in select bit first

;and clock it through n

;times

;clock high

;time=2*n+20 cycles

;clock low

;... clocks d2.0 into first

;drive

;time=2*n+ 20 cycles

;clock high - deselect bit

;next

rts

drive

bsr.s	startup

bsr.s	wind_dwn rts

; Routine to start up a microdrive.

; NB: RETURNS IN SUPERVISOR MODE (if d3 = 1 to 8)

; d1

; d2

; d3	number of microdrive

; a0

; a3

d1 smashed d2 smashed d3 preserved a0 SV_BASE

a3 mdctrl (= 18020h)

;	errors:

; OR: microdrive out of range

startup

cmp.l

blt.s

cmp

bgt.s

move.l

moveq trap

#1,d3 ill_drve

#8,d3

ill_drve

(sp)+,a3

#mt.inf,d0

#1

;Iegal microdrive?

;jump if not

;Iegal microdrive?

;jump if not

;a3=return address

;select MT.INF

;a0= 'to system

;variables

trap	#0

move.l	a3,-(sp)

moveq	#10h,d0

bsr	sys_wser

;supervisor mode

;'return' (geddit?) the

;return address

;microdrive mode

;wait for RS232 to

;complete

| or move.l | #0700h,sr d3,d1 | ;shut out rest of world ;d1 is microdrive to be ;started |
| --- | --- | --- |
| move.l | #mdctrl,a3 | ;a3= "control register |
| bsr | md_selec | ;start it up |
| moveq | #0,d0 | ;no problems |
| rts ill_drve |  | ;return |
| moveq | #-4,d0 | ;error=out of range |

rts

Routine to wind down (al!!) microdrives

N.B. MUST BE CALLED IN SUPERVISOR MODE

; d1	d1 smashed

; d2	d2 smashed

; a0	a0 SV_BASE

; a3	a3 ^instruction after call to here(!!)

wind_dwn

moveq	#mt.inf,d0	;select MT.INF

trap	#1	;a0= ^to system

;variables

move.l	  #mdctrl,a3	;a3= ^control register

bsr.s	md_desel		;wind it down

bsr

sys_rser

;re-enable RS232

move.l	  (sp)+,a3	;a3=return address move		#0,sr	;interrupts off

move.l	  a3,-(sp)	;'return' (it's a killer!)

;return addr. rts	;return

11.0 Adding	Peripheral Cards

to the QL

Peripheral cards may be plugged into the expansion connector on the left-hand side of the QL , or into one of the connectors in the QL expansion module: a unit which allows several add-on cards to be connected to the QL in parallel. The QL expansion module consists of a power supply and a card cage containing a specially wired backplane. The backplane is connected to the QL via a ribbon cable and buffer card.

There are two general categories of peripheral card for the QL : pure add-on memory cards, and other peripheral cards.

It is intended that only one pure add-on RAM card be plugged into the machine at anyone time. It is allocated the address area between $40000 and $BFFFF; the add-on memory should be contiguous from $40000 upwards. This allows for an add-on memory size of up to 512 kbytes.

There is also room for an add-on ROM card of up to 128 kbytes, which is allocated the addresses $E0000 to $FFFFF.

Other peripheral cards contain electronics for the devices being added, a small ROM containing the drivers for the devices being added together with a code allowing the QL to detect that the card is present, and a 4-bit comparator which is used to select the card as explained below.

Note that the convention adopted in this document for an active low signal is to append the letter "L" to the end of the signal name, as in DTACKL, VPAL etc. This takes the place of the overbar indication used in the data sheets from most vendors.

11.1 Expansion Connector

The expansion connector allows extra peripherals to be plugged into the QL. Details of the connections available at the connector may be found in the QL Concepts manual.

The connector inside both the QL and the expansion module is a 64- way male DIN-41612 indirect edge connector, as found on standard Eurocard modules. The connector on each add-on card should be the inverse version of this.

The VIN supply is in the region of +9V DC: the trough never falling below 7V. Up to 500 mA may be drawn from this to power the card.

No add-on card should load any pin on the edge connector by more than two LSTTL loads. All add-on card data bus output drivers should be a 74LS245 or equivalent, in terms of drive ability, and being tri-state.

When the expansion module is connected, RESETCPUL is held low until power is applied to the expansion module. Switching off the expansion module also forces RESETCPUL low.

11.2 CPU Interface

The CPU interface is totally memory-mapped onto the 68008's bus, control of the bus for use with the video display controller being obtained by using the DTACKL signal to arbitrate the bus. Memory access is entirely controlled by DSL, with ASL left unused. ASL should not be used to gate any add-on hardware.

An unexpanded QL does not look at address lines A19 and A18. In peripheral cards which are to be added to the QL, it is necessary for each card to disable the circuitry on the QL itself when that peripheral card recognises its own address.This is achieved by pulling signal DSMCL high before DSL goes low including buffering times. This is done typically by using a fast NPN switching transistor (such as an MPS2369) connected as an emitter follower with the emitter connected to DSMCL, the collector to +5V and the base to a logic Signal. Note that the timing for this operation is the most critical in most hardware interfaces to the QL, especially when the necessary signals have been buffered.

Add-on cards must supply DTACKL or VPAL as required, to notify the

CPU that they have recognised their address.

All 68008 signals are available both on the expansion connector and in the expansion module to allow expansion to include coprocessors or other peripherals.

The following signals are outputs only: A0-A19, RDWL, ASL, DSL, BGL, CLKCPU, E, RED, BLUE, GREEN, CSYNCL, VSYNCH, ROMOEH, FC0-2 , RESETCPUL.

The following lines are inputs only, and should only be driven from open collector outputs: DTACKL, BRL, VPAL, IPL0L, IPL1L, BERRL, EXTINTL, DBGL.

The data bus, D0-D7, is bidirectional.

When using the QL expansion module, the data bus buffers in the module are enabled whenever A18 or A19 is high, or if the Data Bus Grab Signal (DBGL) is asserted by any add-on card on pin 25A of the edge connector. If DBGL is to be used, it should be driven by an open collector buffer.

The EXTINTL pin may be used to generate a level 2 external interrupt, which can be linked to a user task (see section 6.3). Note thatthe EXTINTL pin must not be negated until the Qdos start-up mechanism is complete, or there is a risk of the system hanging up.

11.3 Peripheral Card Addressing

Peripheral cards (other than pure add-on memory cards) are allocated the address space between $C0000H and $DFFFFH. Each peripheral card, when selected, must disable DSMCL and assert VPAL or DTACKL as required, for its own use. This address space is split into eight slots of

16 kbytes each; each peripheral card should normally take only one block if a full set of eight peripheral cards is to be allowed to operate concurrently.

There is a set of four select lines, SP0-SP3, appearing on the edge connector. The first card in the QL expansion module, or a single card directly plugged into the QL, receives a value of zero on these four lines. Each slot in the expansion module has a value one different from that in the other slots: this means that each card isallocated 16 kbytes of address space. The card select logic compares the values on A17-A14 against the number coming in on the select lines in order to determine whether that card is selected. For the card to be selected it must be the case that A14=SP0, A15=SP1, A16=SP2 and A17=SP3.

If there is a ROM containing device drivers for the peripheral card, it should sit in the bottom addresses of the 16 kbyte block. The format of the lowest part of this ROM is specified in the next section.

I '

11.4 Add-on Card ROMs

When the machine is booted, the operating system checks for plug-in

ROM drivers by looking forthe characteristic longword flag $4AFB0001 at the base of each location in which a ROM might be present. The beginning of a plug-in ROM should be in the following format:

00	$4AFB0001 (flag to indicate ROM is present)

04	pointer to list of BASIC procedures and functions

06	pointer to initialisation routine

08	string identifying the ROM

The pointers are relative to the base of the ROM. If the list pointer is zero then there will be no attempt to link routines into SuperBASIC.

The list of BASIC procedures and functions is in the form used by BP.lNIT (see section 16.0).

At start-up the machine will link in the additional BASIC procedures from the ROM, then call the initialisation routine (in user mode) which must not modify A6, and finally must restore A0 (the initial window ID), and A3, the pointer to the ROM, on exit. Up to 128 bytes may be used on the user stack.

The description should be in the form of a character count (word) followed by the ASCII characters of the device description(s) ending with the newline character (ASCII 10). It is recommended that the number of characters should be limited to 36.

All code for device drivers must be position independent, since the addresses of the ROM and the devices on the card will be dependent upon the position at which it has been plugged into the QL expansion module. This allows multiple copies of the same add-on card to be used simultaneously.

12.0	Non-English QLs

There are three areas in which non-English QLs may differ from English

QLs: the video, the keyboard, and the character set for serial communications.

The version codes for non-English QL s are adjusted appropriately to contain a character identifying the country. In the version code returned by MT.lNF, this character replaces the decimal point; in the string returned by the SuperBASIC VER$ function, the character is added on at the end, producing a string three characters long for non-English QLs.

12.1 Video

This is different for countries where the television system is NTSC, which permits the use of fewer raster lines than PAL. In QLs for such countries, the following options are the defaults:

For monitor operation, a 50Hz 624-line non-interlaced system is used; this is the same system as is used on the English QL. The full 512x256 pixel display is available, and the default windows and character size are the same as for the monitor mode on an English QL .

For TV operation, a 60Hz 524-line non-interlaced system is used in which the number of raster lines available is limited to 192. In order to ease the task of software conversion, an alternate display font is provided which allows a 6x8 character square instead of the usual 6x10. This ensures approximately the same number of visible rows of text on both PAL and NTSC QL s, at the cost of true descenders and reduced vertical spacing. The default windows and graphics scaling for TV operation are different from those of the English QL .

It is to be expected that a different version of any applications software (or at least different options) will be required for NTSC operation on domestic televisions.

12.2 Non-English-language Keyboards

The keyboard layout for most European countries will be different from the English layout. This difference should be largely transparent to applications software, since the "QL ASCII" codes contain all the characters necessary for the European countries in question, and the codes generated are independent of the keyboard layout and hence of the actual key depressions required to generate them.

However, there are a few subtleties, the following being the most obvious:

1. A program which draws pictures of keys in certain places will certainly produce an incorrect drawing if the location of those keys has changed between countries.

2. The keyrow function (or MT.IPCOM trap) refers to the physical position of the keys, not to their logical meaning. For example, a test on an English QL for the letter "0" using keyrow will turn into a test for the letter "A" on a French QL which has an AZERTY keyboard.

3. An instruction to "hit any key" will not be strictly accurate for a country which employs non-spacing diacriticals, where the keypress of an accent character does not generate a code until the character to be accented is pressed. The length of the type-ahead buffer in the IPC will be apparently reduced in such cases.

12.3 Character Set

The English character set is available in all countries. However, in non-English countries, the character set for serial communications may (optionally) be translated into a "local" character set, this being chosen by the Sinclair distributor for that country as being a commonly used interface standard. A further option allows the user to specify his own translation table, since it is anticipated that a number of countries will have several standards (i.e., no standards at all).

12.4 Special Alphabets

Languages with non-Roman alphabets, such as Hebrew, Greek, Thai, Arabic, etc., require special treatment. No general scheme has been devised for making software transportable to these countries, and the implementation means will be specific to each country.

13.0 Manager Traps

The special trap #0 is used to enter supervisor mode. The user should store the status register somewhere before calling this trap, so that he can return to user mode by restoring it to its previous value.

TRAP #1 D0=$15	MT.ACLCK

Adjust the clock

Call parameters	Return parameters

D1.L adjustment in seconds

D2

D3

AO A1

A2

A3

D1.L time in seconds

D2	 ??? D3	??? AO	 ???

A 1	preserved

A2	preserved

A3	preserved

As setting the clock takes a significant time, no adjustment is made if a call is made to adjust the clock and D1 =0.

Time starts at 00:00 1 January 1961.

TRAP #1 D0=$A

Activate a job

Call parameters

D1.L	job ID

D2.B   priority (0 to 127) D3.W  timeout (0 or -1) AO

A1

A2

A3

Error returns:

NJ  job does not exist

NC job already active

MT.ACTIV

Return parameters

D1.L  job ID

D2	preserved

D3	preserved

A0	base of job ctrl area

A1	preserved

A2	preserved

A3	preserved if D3 =0

This activates a job in the transient area. Execution commences at the start address defined when the job was created.

If the timeout is zero then the execution of the current job continues, otherwise the current job will be suspended until the job activated has

completed. The trap will then return with the error code from that job.

TRAP #1 D0=$16

Allocate BASIC program area

MT.ALBAS

Call parameters

D1.L number of bytes required

D2

D3

A0 A1

A2

A3

A6	base address

A7	user stack pointer

Error returns:

OM out of memory

Return parameters

D1.L  nr. bytes allocated

D2	 ??? D3	??? A0	??? A1	??? A2	??? A3	???

A6	new base address

A7	new stack pointer

TRAP#1 D0=$18

Allocate common heap area

Call parameters

D1.L nr. bytes required

D2.L owner job ID

D3

A0 A1

A2

A3

Error returns:

OM out of memory

NJ job does not exist

MT.ALCHP

Return parameters

D1.L nr. bytes allocated

D2	???

D3	???

A0	base address of area

A1	??? A2	??? A3	???

This trap is a specific example of the general heap allocation mechanism described in section 2.1.4 and accessible using MT.ALLOC.

Trap #1 D0=$C	MT.ALLOC

Allocate an area in a heap

Call parameters	Return parameters

D1.L  length required	D1.L length allocated

D2	D2	???

D3	D3	???

A0     ptr to ptr to free space	A0	base of area allocated

A1	A1	??? A2	A2	??? A3	A3	???

A6	base address	A6	preserved

Error returns:

OM no free space large enough

Two trap entries are provided for user heap management where this is required to be atomic. A6 is used as a base address for both this call and for MT.LNKFR so that A0 (and A1) is an address relative to A6.

See section 2.1.4 for details of the heap mechanism.

TRAP #1 D0=$E

MT.ALRES

Allocate resident procedure area

Call parameters

D1.L number of bytes reqd.

D2

D3

A0 A1

A2

A3

Error returns:

Return parameters

D1	???

D2	???

D3	???

A0	base address of area

A1	??? A2	??? A3	???

OM out of memory

NC unable to allocate (TRNSP area not empty)

This trap, in common with its partner MT.RERES (release resident procedure area) should only be invoked when the transient program area is empty.

TRAP #1 D0=$12

Set the baud rate

Call parameters

D1.W baud rate

D2

D3

A0 A1

A2

A3

BP non recognised baud rate

MT.BAUD

Return parameters

D1	???

D2	 preserved D3	preserved A0	preserved A1	preserved A2	preserved A3	preserved

TRAP #1 D0=$1	MT.CJOB

Create a job in transient program area

Call parameters

D1.L  owner job ID

D2.L  length of code (bytes) D3.L  length of data space AO

A1	start address or 0

A2

A3

Error returns:

Return parameters

D1.L  job ID

D2	preserved

D3	preserved

A0	base of area allocated

A1	preserved A2	preserved A3	preserved

OM   out of memory

NJ	no room in job table or D1 is not a job

This trap allocates space in the transient program area, and sets up a job entry in the scheduler tables. This does not invoke the job and the only initialisation is that two words of 0 are put on the stack. The program itself would normally be loaded, by another job, into the space allocated, after this system call. The stack pointer saved in the job control area points initially to two zero words on the stack (at the highest addresses in the job's data area); if channels are to be opened for the job, or a command string is to be passed to the job, then this can be done before the job is activated.

If D1 is negative, the new job is independent, otherwise it is owned by the calling job.

TRAP #1 D0=$10	MT.DMODE

Set or read the display mode

Call parameters	Return parameters

D1.B key -1 read mode	D1.B display mode

0 mode is 4 colour

8 mode is 8 colour

D2.B key -1 read display	D2.B display type

0 monitor

1 625-line TV

2 525 line TV

D3	D3	preserved A1	A0	preserved A1	A1	preserved A2	A2	preserved A3	A3	preserved

A4	???

This call is used to set or read the current display mode. It is treated as a manager trap as it affects all the displayed windows. If a call is made to set the screen mode, then all the windows on the screen are cleared and the character sizes may be adjusted. Obviously, there are serious risks involved in calling this trap to set the mode when there are jobs in the machine accessing the screen.

TRAP #1 D0=$6	MT.FREE

Find largest contiguous free space that may be allocated in the transient program area

Call parameters	Return parameters

D1	D1.L  length of space found

D2	 D2	 ??? D3	D3	??? AO	AO	 ??? A1	A1	 ??? A2	A2	 ??? A3	A3	???

TRAP #1 D0=$5	MT.FRJOB

Force remove job from transient program area

Call parameters	Return parameters

D1.L  job	ID D2

D3.L  error code

A0

A1

A2

A3

D1	??? D2	??? D3	??? A0	??? A1	??? A2	??? A3	???

Error returns:

NJ  job does not exist

This inactivates a complete job tree and deletes all jobs in it. If D1 is a negative word then the job is the current job.

Neither of the traps MT.FRJOB or MT.RJOB to remove jobs can remove job 0.

Neither of these traps are guaranteed atomic.

If there is a job waiting on completion of any job removed, this is released with 00 set to the error code (see MT.ACTIV D0=$A).

TRAP #1 D0=$0	MT.lNF

System information

Call parameters	Return parameters

D1	D1.L   current job 10

D2	D2.L   ASCII version (n.nn)

D3	D3	preserved

A0	A0	pointer to system vars

A1	A1	preserved A2	A2	preserved A3	A3	preserved

TRAP #1 D0=$11	MT.lPCOM

Send a command to the IPC

Call parameters	Return parameters

D1

D2

D3

A0

A1

A2

A3	pointer to command

D1.B return parameter

D2	preserved

D3	preserved

D5	???

D7	???

A0	preserved A1	preserved A2	preserved

A3	preserved

This trap sends a command to the IPC.

A command sent to the IPC is a nibble followed by a stream of nibbles or bytes being the parameters of the command; some information may then be returned from the IPC. The command format for MT.lPCOM is a header describing the command to be sent, followed by the parameters to be sent, followed by a byte indicating whether a reply is expected. The IPC communication is completely unprotected and the command must not contain any errors or else the entire machine will hang up. IPC communications	is a very slow process and excessive use of the IPC, for example: polling all rows of the keyboard - the cursor keys have been organised to all be in one row, will cause very high processor overheads.

The command format allows 0, 4 or 8 bits to be transferred from each byte in the parameter block. This is encoded in 2 bits:

00	send least significant 4 bits

01	send nothing

10	send all 8 bits

11	send nothing.

The complete command format is:

1 byte

1 byte

1 long word

n bytes

1 byte

the IPC command nibble in the LS 4 bits; the number of parameter bytes to follow; containing the codes for the amount of each parameter byte to be sent in reverse order: bits 1,0 the amount of the first byte to send bits 3,2 the amount of the second byte etc.:

the parameter bytes

length of reply encoded in bits 1,0.

Most of the IPC commands are for use by the operating system and any attempt by application programs to use these is liable to cause loss of data or worse. There are three commands for the IPC which may be used by applications programs:

$9	read a row of the keyboard, 1 parameter

4 bits	the row number

8 bits reply

$A	initiate sound, 8 parameters

8 bits	pitch 1

8 bits	pitch2

16 bits	interval between steps

16 bits	duration

4 bits	step in pitch

4 bits	wrap

4 bits	randomness of step

4 bits	fuzziness no reply

$B	kill sound, no parameters, no reply.

TRAP #1 D0=$2	MTJINF

Information on a job

Call parameters	Return parameters

D1.L  job 10

D2.L  job at top of tree

D3

A0 A1

A2

A3

Error returns:

D1.L next job in tree

D2.L owner job

D3.L MSB -ve if suspended

LSB priority

A0	base address of job

A1	???

A2	preserved

A3	preserved

NJ job does not exist

This trap returns the status of a job.

This trap may be used to check the status of a tree of jobs. On each call

02 should be the 10 of the job at the top of the tree; to scan a complete tree the trap is made with 01 being the return value of the previous call. When the tree has been completely scanned 01 is returned equal to zero.

MT.LDD See the entry for MT.LXINT for details.

MT.LlOD See the entry for MT.LXINT for details.

Trap #1 D0=$0	MT.LNKFR

Link a free space (back) into a heap

Call parameters	Return parameters

| D1.L | length to link in | D1 | ??? |
| --- | --- | --- | --- |
| D2 |  | D2 | ??? |
| D3 |  | D3 | ??? |
| A0 | base of new space | A0 | ??? |
| A1 | ptr to ptr to free space | A1 | ??? |
| A2 |  | A2 | ??? |
| A3 A6 | base address | A3 A6 | ??? preserved |

A6 is used as a base address for this call and for MT.ALLOC so that A0 (and A1) is an address relative to A6.

MT.LPOLL See the entry for MT.LXINT for details.

MT.LSCHD See the entry for MT.LXINT for details.

TRAP#1     D0=$1A

D0=$1C

D0=$1E

D0=$20

D0=$22

MT.LXINT MT.LPOLL MT.LSCHD MT.LlOD MT.LDD

Link  an external interrupt service routine

a polling 50/60 Hz service routine

a scheduler loop task an I/O device driver

or a directory device driver into the operating system

Call parameters	Return parameters

D1

D2

D3

A0	address of link

A1

A2

A3

D1	preserved

D2	preserved

D3	 preserved A0	 preserved A1	???

A2	preserved

A3	preserved

TRAP #1 D0=$B	MT.PRIOR

Change job priority

Call parameters	Return parameters

D1.L  job ID

D2. B priority (0 to 127)

D3

A0 A1

A2

A3

D1.L  job ID

D2	preserved

D3	preserved

A0	base of job ctrl area

A1	preserved A2	preserved A3	preserved

Error returns:

NJ job does not exist

This call is used to change the priority of a job. If D1 is a negative word it will change the priority of the current job. Setting the priority to 0 will cause inactivation. This call re-enters the scheduler and so a job setting its own priority to zero will be immediately inactivated.

TRAP #1 D0=$13	MT.RCLCK

Read the clock

Call parameters	Return parameters

D1	D1. L time in seconds

D2	D2	???

D3	D3	preserved

A0	A0	???

A1	A1	preserved	 A2	A2	preserved

A3	A3	preserved

MT.RDD See the entry for MT.RXINT for details.

TRAP #1 D0=$17

Release BASIC program area

MT.REBAS

Call parameters		Return parameters

D1.L nr. of bytes to release

D2

D3

A0 A1

A2

A3

A6	base address

A7	user stack pointer

TRAP #1 D0=$19

Release common heap area

D1.L nr. bytes released

D2	???

D3	???

A0	???

A1	???

A2	???

A3	???

A6	new base address

A7	new stack pointer

MT.RECHP

Call parameters	Return parameters

D1	D1	???

D2	D2	???

D3	D3	???

TRAP #1 D0=$9	MT.RELJB

Release a job

Call parameters	Return parameters

D1.L  job ID

D2

D3

A0 A1

A2

A3

D1.L  job ID

D2	preserved

D3	preserved

A0	base of job ctrl area

A1	preserved

A2	preserved

A3	preserved

Error returns:

NJ not a valid job ID

After this call all jobs are rescheduled.

The activity of jobs can be controlled by activation or by modification of the priority levels. A job at priority level 0 is inactive, at any other priority level it is active.

TRAP #1 D0=$F	MT.RERES

Release resident procedure area

Call parameters	Return parameters

D1	D1	???

D2	D2	???

D3	D3	???

A0	A0	??? A1	A1	??? A2	A2	??? A3	A3	???

Error returns:

NC unable to release (TRNSP area not empty)

This trap, in common with its partner, MT.ALRES (allocate resident procedure area), should only be invoked when the transient program area is empty.

MT.RIOD	See the entry for MT.RXINT for details.

TRAP#1 D0=$4	MT.RJOB

Remove job from transient program area

Call parameters

Return parameters

D1.L  job10

D2

D3.L error code

AO

A1

A2

A3

D1	???

D2	???

D3	 ??? A0	??? A1	??? A2	??? A3	???

Error returns:

NJ job does not exist

NC job not inactive

This trap removes a job (and its subsidiaries) from the transient program area. Only inactive jobs may be removed.

MT.RPOLL See the entry for MT.RXINT for details.

MT.RSCHD See the entry for MT.RXINT for details.

TRAP #1    D0=$1B D0=$1D D0=$1F   D0=$21

D0=$23

MT.RXINT MT.RPOLL MT.RSCHD

MT.RIOD

MT.RDD

Remove an external interrupt service routine a polling 50/60 Hz service routine

a scheduler loop task an IO device driver

or a directory device driver from the operating system

Call parameters	Return parameters

D1

D2

D3

A0	address of link

A1

A2

A3

D1	 preserved D2	preserved D3	preserved A0	 preserved A1	???

A2	preserved

A3	preserved

TRAP #1 D0=$14	MT.SCLCK

Set the clock

Call parameters	Return parameters

D1.L time in seconds

D2

D3

A0

A1

A2

A3

D1.L time in seconds

D2	???

D3	 ??? A0	 ???

A1	preserved

A2	preserved

A3	preserved

TRAP #1 D0=$8	MT.SUSJB

Suspend a job

Call parameters	Return parameters

D1.L	job ID D2

D3.W  timeout period

A0

A1	address of flag byte

A2

A3

D1.L  job ID

D2	preserved

D3	preserved

A0	base of job ctrl area

A1	preserved A2	preserved A3	 preserved

Error returns:

NJ  not a valid job ID

A job may be suspended for an indefinite period, or until a given time has elapsed. The timeout period is up to ($7FFF times the frame time).

If the job ID is a negative word, then the current job is suspended. The flag byte is cleared when the job is released. If there is no flag byte, then A 1 should be o. If the timeout period is specified as -1, then the suspension is indefinite; no other negative value should be used. If the job is already suspended, the suspension will be reset. All jobs are rescheduled.

TRAP #1 D0=$7	MT.TRAPV

Set the per-job pointer to trap vectors

Call parameters	Return parameters

D1.L job ID D2

D3

A0

A1	pointer to table

A2

A3

D1.L  job ID

D2	 preserved D3	preserved A0	base of job A1	???

A2	preserved

A3	preserved

Note: When a routine in the table is entered as a result of an exception, the CPU is in supervisor mode. The routine should return with an RTE command (not RTS). Any registers used must be saved and restored.

14.0 I/O Management Traps

TRAP #2 D0=$2

Close a channel

Call parameters

D1

D2

D3

A0   channel lD

A1

A2

A3

Error returns:

NO channel is not open

IO.CLOSE

Return parameters

D1	 preserved D2	 preserved D3	 preserved A0	???

A1	???

A2	preserved

A3	preserved

TRAP #2 D0=$4	IO.DELET

Delete a file

Call parameters	Return parameters

| D1.L job | ID (as file open!!) | D1 ??? |
| --- | --- | --- |
| D2 |  | D2 | preserved |
| D3 |  | D3 | ??? |
| A0 | address of channel name | A0 | ??? |
| A1 |  | A1 | ??? |
| A2 |  | A2 | preserved |
| A3 |  | A3 | preserved |

Error returns:

NO	not opened -too many channels open

OM   out of memory

NF	file or device not found

BN     bad file or device name

TRAP #2 D0=$3

Format a sectored medium

Call parameters

D1

D2

D3

A0	ptr to medium name

A1

A2

A3

Error returns:

OM  out of memory

NF   drive not found

IU	drive in use

FF	format failed

IO.FORMT

Return parameters

D1.W   number of good sectors

D2.W   total nr of sectors

D3	preserved

A0	???

A1	???

A2	preserved

A3	preserved

The medium name is in the form of a character count (word) followed by the ASCII characters of the drive name, the drive number, underscore then up to 10 characters for the medium name. For example, MDV1_November.

TRAP #2  D0=$1	IO.OPEN

Open a channel

Call parameters	Return parameters

D1.L  job ID	D1	job ID

D2	D2	preserved

D3.L code	D3	preserved

0 old (exclusive) file or device

1 old (shared) file

2 new (exclusive) file

3 new (overwrite) file

4 open directory

A0	address of channel name	A0	channel lD

A1	A1

A2	A2

A3	A3

??? preserved preserved

Error returns:

NO   not opened - too many channels open

NJ	job does not exist

OM   out of memory

NF	file or device not found

EX	file already exists

IU	file or device in use

BN	bad file or device name

If the job ID is passed as a negative word (for example -1) then the channel will be associated with the current job.

The file or device name should be a string of ASCII characters. This string is preceded by a character count (word), the pointer should point to this word (on a word boundary).

The error return "BN" indicates that the name of the device has been recognised but that the additional information is incorrect, for example CON_512y240.

The code is usually ignored for access to any non-shared device: in practice, this is anything other than a file store. If the error code is non- zero then no channel has been opened.

Note that New (overwrite) is not currently supported for Microdrive files.

15.0 I/O Traps

TRAP#3 D0=$40	FS.CHECK

Check all pending operations on a file

Call parameters

D1

D2

D3.W  timeout A0	channel lD A1

A2

A3

Error returns:

NC not complete

NO channel not open

Return parameters

D1	???

D2	preserved

D3. L preserved A0	 preserved A1	???

A2	preserved

A3	preserved

This trap is used to check whether all of the pending operations have completed.

TRAP  #3  D0=$41				FS.FLUSH

Flush buffers for this file

Call  parameters			Return parameters

D1					D1     ???

D2					D2     preserved

D3.W   timeout			D3.L  preserved

A0        channel   ID			A0     preserved

A1					A1     ???

A2					A2     preserved

A3					A3     preserved

Error  returns:

NC  not complete

NO  channel not open

When a write operation to a file is complete, the data written may still be in the  slave blocks rather than on the file. For further details please see Section 5.2  on File I/O. This call may be used to check that a file is in a known state.

TRAP  #3  D0=$47

Read file header

Call  parameters

D1

D2.W   buffer   length

D3.W   timeout

A0	channel lD

A1	base of read buffer

A2

A3

Error  returns:

NC  not complete

NO  channel not open

BO  buffer overflow

FS.HEADR

Return  parameters

D1.W   length of header read

D2	preserved

D3.L	preserved

A0	preserved

A1	top  of  read  buffer

A2	preserved

A3	preserved

The read header call is provided so that a job can allocate the space for a load call as well as determining the characteristics of a file. The buffer provided must be at least 14 bytes long. In the case of a trap to a pure serial device, then the length of the header returned in D1 will be spurious.

The file pointer is such that position zero is the first byte after the header. Thus block boundaries on standard directory driver files are at positions 512*n-64.

TRAP#3  D0=$46

Set file  header

Call  parameters

D1

D2

D3.W   timeout

A0	channellO

A1	base of  header  def

A2

A3

Error  returns:

NC  not  complete

NO  channel   not  open

FS.HEADS

Return  parameters

D1.W   length  of  header  set

D2	preserved

D3.L    preserved

A0	preserved

A1	end  of  header  def

A2	preserved

A3	preserved

This call sets the first 14 bytes of the header. The length of file will normally be overwritten by the filing system. When a header is sent over a pure serial device, then the 14 bytes of the header are preceded by a byte $FF.

TRAP  #3  D0=$48

Load  file  into  memory

Call  parameters

D1

D2.L	length  of  file

D3.W   timeout

A0	channellD

A1	base address  for  load

A2

A3

Error  returns:

NO channel   not  open

FS.LOAD

Return  parameters

D1	???

D2	preserved

D3.  L preserved

A0	preserved

A1	top  address  after  load

A2	preserved

A3	preserved

Files may be loaded into memory in their entirety with the file load trap. If the transient program area is used for this, a trap # 1 must have been invoked to reserve the space before the file load trap is invoked.

D3 should be set to -1 before both this trap, and FS.SAVE, and the base address in A1 must be even.

TRAP#3  D0=$45

Get information about medium

FS.MDINF

Call  parameters

D1

D2

D3.W timeout

A0	channel ID

A1	ptr to 10 byte  buffer

A2

A3

Error returns:

Return  parameters

D1.L empty/good sectors

D2	preserved

D3.L preserved

A0	preserved

A1	end of medium name

A2	???

A3	???

NC  not complete

NO  channel not open

The name of the medium, its capacity, and the available space may be obtained for a file or directory that is open.

The medium name is 10 bytes long and left justified. Any remaining bytes are filled with the space character ($20).

The number of empty sectors is in the most significant word (msw) of

D1, the total available on the medium is in the least significant word

(lsw).

A sector is 512 bytes.

TRAP#3  D0=$42

Position file pointer absolute

Call parameters

D1.L   file position

D2

D3.W  timeout

A0	channel lO

A1

A2

A3

Error  returns:

NC  not complete

NO  channel not open

EF   end of file

FS.POSAB

Return parameters

D1.L  new file position

D2	preserved D3.L  preserved A0	preserved A1	???

A2	preserved

A3	preserved

TRAP  #3   DO=$43

Position file pointer relative

Call  parameters

D1.L	offset to	file  pointer

D2

D3.W   timeout

A0	channel lD A1

A2

A3

Error  returns:

NC  not complete

NO  channel not open

EF   end of file

FS.POSRE

Return  parameters

D1.L  new  file  position

D2	preserved D3	preserved A0	preserved A1	???

A2	preserved

A3	preserved

If a file positioning trap returns an off file limits error, then the pointer is set to the nearest limit, this being 0 or end of file. The relative file positioning may, of course, be used to read the current file position.

TRAP#3  D0=$49

Save file from memory

Call  parameters

Return  parameters

FS.SAVE

D1

D2.L	length   of  file

D3.W   timeout

A0	channel lO

A1	base address of  fiIe

A2

A3

Error  returns:

NO  channel not open

OF   drive full

D1	???

D2	preserved

D3.L  preserved

A0	preserved

A1	top address of file

A2	preserved

A3	preserved

In common with FS.LOAD, D3 should be set to -1 before this trap, and the base address in A1 must be even.

TRAP  #3  D0=$4	IO.EDLIN

Edit a line of characters (console driver only)

Call parameters

D1	cursor/line length

D2.W   length of buffer

D3.W   timeout

A0	channel ID

A1	pointer to end of line

A2

A3

Error  returns:

NC  not complete

NO  channel not open

BO  buffer overflow

Return parameters

D1	cursor/line length

D2	preserved

D3	preserved

A0	preserved

A1	pointer to end of line

A2	preserved

A3	preserved

This is similar to the fetch line trap, except that the pointer A 1 is always to the end of the line, D1 contains the current cursor position in the msw and the length of the line in the Isw and the line (from the current cursor position) is written out to the console when the call is made. The line should not have a terminating character when the trap is made, but the terminating character will be included in the character count on return. Enter (ASCII 10), up cursor or down cursor are all acceptable terminating	characters.

TRAP#3  D0=$1

Fetch  a byte

Call  parameters

D1

D2

D3.W timeout

A0	channel lD A1

A2

A3

Error  returns:

NC  not complete

NO  channel not open

EF    end of file

IO.FBYTE

Return  parameters

D1.B  byte  fetched

D2.L  preserved

D3.L	 preserved A0	 preserved A1	???

A2	preserved

A3	preserved

TRAP  #3   DO=$2   or  3	IO.FLlNE

IO.FSTRG

D0=$2

D0=$3

IO.FLlNE  fetch  a line  of  characters  terminated by ASCII  <LF> ($A)

IO.FSTRG  fetch  a string  of  bytes

Call  parameters	Return  parameters

D1

D2.W   length of buffer

D3.W   timeout

A0	channel lD

A1	base of  buffer

A2

A3

D1.W   nr. of  bytes  fetched

D2.W   preserved D3.L	preserved A0	preserved

A1	updated ptr to buffer

A2	preserved

A3	preserved

Error returns:

NC not complete

NO channel not open

EF end of file

B0 buffer overflow (fetch line only)

The character count of a fetch a line trap includes the linefeed character if found.

IO.FSTRG See the entry for IO.FLlNE for details.

TRAP  #3   D0=$0

Check for pending input

Call parameters

D1

D2

D3. W  timeout

A0	channel lD A1

A2

A3

Error  returns:

Return parameters

D1	???

D2.L  preserved D3.L  preserved A0	preserved A1	 ???

A2	preserved

A3	preserved

IO.PEND

NC  not complete (no pending input)

NO  channel not open

EF   end of file

This trap is used to check for pending input on a channel. It does not read  any data or modify the input channel in any way. This only works on the  console device if D3=0 and the keyboard queue is already connected to the  console.

TRAP #3  D0=$5

Send a byte

Call parameters

D1.B   byte to be sent

D2

D3.W  timeout

AO	channellD A1

A2

A3

Error returns:

NC  not complete

NO channel not open

DF  drive full

OR off  window/paper etc

IO.SBYTE

Return parameters

D1	???

D2.L  preserved D3.L  preserved AO	preserved A1	???

A2	preserved

A3	preserved

TRAP#3   D0=$7

Send a string  of  bytes

Call parameters

D1

D2.W   nr of bytes to be sent

D3.W   timeout

A0	channel ID

A1	base of  buffer

A2

A3

Error  returns:

NC  not complete

NO  channel not open

OF   drive full

IO.SSTRG

Return parameters

D1.W  nr. of bytes sent

D2.W   preserved

D3.L   preserved

A0	preserved

A1	updated ptr to buffer

A2	preserved

A3	preserved

Please refer to section 5.3.5 for details of the special treatment afforded to  newlines on the console or screen device.

SD.ARC  See the  entry  for  SD.POINT  for  details.

TRAP  #3   D0=$C

Set the border width and colour

SD.BORDR

Call  parameters

Return  parameters

D1.B    colour D2.W   width D3.W   timeout

A0	channel lD

A1

A2

Error returns:

D1

D2.L D3.L A0 A1

A2

??? preserved preserved preserved preserved preserved

NC  not complete

NO  channel not open

This call redefines the border of a window. By default this is of no width. The width of the border is doubled on the vertical edges. The border is inside the window limits. All subsequent screen traps (except this one) use the reduced window size for defining cursor position and window limits.

As a special case, the colour $80 defines a transparent border so that the border contents are not altered by the trap.

If the call changes the width of the border, then the cursor is reset to the home position (top left hand corner).

SD.CHENQ See the entry for SD.PXENQ for details.

TRAP  #3   D0=$20   to  24

Clear part or all of a window

SD.CLEAR SD.CLRBT SD.CLRLNSD.CLRRT SD.CLRTP

D0=$20

D0=$21

D0=$22

D0=$23

D0=$24

Call parameters

D1

D2

D3.W  timeout

A0	channellD A1

A2

Error returns:

SD.CLEAR SD.CLRTP SD.CLRBT SD.CLRLN SD.CLRRT

clear all of window clear top of window

clear bottom of window clear cursor line

clear right hand end of cursor line

Return  parameters

D1	???

D2.L  preserved

D3.L  preserved

A0	preserved

A1	???

A2	preserved

NC  not complete

NO  channel not open

The clear window traps can clear all or part of a window. To clear a part of a window the cursor is used as a reference. The clear operation consists of overwriting all the pixels in the designated area with paper colour.

The division between the top of the window and the bottom of the window is the cursor line. The cursor line is in neither the top nor the bottom ofthe window.

The cursor line is the whole height of the current character fount (either 10 or 20 rows). The right hand end includes the character at the current cursor  position.

SO.CLRBT  See the  entry  for  SO.CLEAR for  details.

SO.CLRLN  See the  entry  for  SO.CLEAR for  details.

SO.CLRRT  See the  entry  for  SO.CLEAR for  details.

SO.CLRTP  See the  entry  for  SO.CLEAR for  details.

TRAP  #3   D0=$E	SD.CURE

Enable the cursor

Call parameters	Return  parameters

D1

D2

D3.W  timeout

A0	channel lD A1

A2

D1	???

D2.L  preserved D3.L preserved A0	preserved A1	???

A2	preserved

Error returns:

NC  not complete

NO  channel not open

The cursor is automatically enabled when a read line or edit line trap is issued to a console window.

TRAP  #3   D0=$F	SO.CURS

Suppress the cursor

Call parameters	Return  parameters

D1

D2

D3.W  timeout

A0	channellD

A1

A2

D1	???

D2.L  preserved D3.L  preserved A0	preserved A1	???

A2	preserved

Error returns:

NC  not  complete

NO  channel not open

The calls to suppress or enable the cursor do not return an error if the cursor is already suppressed or enabled (respectively), as they merely ensure that the cursor is in the desired state.

SD.ELlPS See the entry for SD.POINT for details.

.

TRAP #3  D0=$9	SD.EXTOP

Call an extended operation

Call  parameters	Return  parameters

D1	parameter

D2	parameter

D3.W   timeout

A0	channel lD A1	parameter

A2	start  address  of  routine

D1	parameter

D2	preserved

D3.L  preserved A0	preserved A1	parameter A2	preserved

Error  returns:

NC  not complete

NO  channel not open

and anything from the operation routine

This trap invokes an externally supplied routine as if it were part of the standard screen driver. D1, D2 and A1 are passed to the routine, while only D1 and A1 are returned. The code within the routine is executed in supervisor mode with A0 pointing to the channel definition block (see Section 7.2) and A6 pointing to the system variables as for standard device drivers.

TRAP #3  DO=$2E	SO.FILL

Fill rectangular  block in window

Call parameters	Return  parameters

D1.B	colour

D2

D3.W   timeout

A0	channel  ID

A1	base of  block  definition

A2

D1	???

D2.L  preserved

D3.L  preserved A0	preserved A1	???

A2	preserved

Error returns:

NC  not  complete

NO  channel  not  open

OR  block  falls outside  window

This trap fills a rectangular block of a window with the current ink colour, taking into account the mode set by SD.SETMD.

The block definition is in the same form as the window definition. It is 4 words long: width, height, X origin and Y origin. The origin is referred to the window origin.

This is a fast way of drawing horizontal or vertical lines.

TRAP #3  D0=$35

Turn area flood on and off

Call parameters

SD.FLOOD

Return parameters

D1.L	key  0=end  flood	D1	???

1= start or restart flood

D2

D3.W  timeout

A0	channel ID

A1

A2

A3

Error returns:

NC  not complete

NO channel not open

D2	preserved

D3.L  preserved A0	 preserved A1	???

A2	preserved

A3	preserved

TRAP  #3  D0=$25	SD.FOUNT

Set or reset the fount

Call  parameters	Return  parameters

D1

D2

D3.W   timeout

A0	channel ID

A1	base of fount

A2	base of second fount

D1	???

D2.L   preserved

D3.L   preserved A0 	   preserved A1	???

A2	preserved

Error  returns:

NC  not complete

NO  channel not open

The character fount is a 5x9 array of pixels in a 6x1 0 rectangle. A default fount and a second fount are built into the ROM, although alternative founts may be selected.

If the fount address is given as zero the default fount will be used.

The structure of the fount assumes that up to a certain value characters are invalid (default $1E), from the next value (default $1F) a known number of characters are valid (default $61). Thus the structure is as follows:

$00 lowest valid character (byte)

$01 number of valid characters-1 (byte)

$02 to $0A 9 bytes of pixels for the first valid character

$08 to $13 etc.

Each byte of pixels has the pixels in bit 6 to bit 2 (inclusive) of the byte. The top row of any character is implicitly blank.

If a character, which is to be written, is found to be invalid in the first fount, it is written using the second fount. If it is also invalid in the second fount, then the lowest valid character of the second fount is used.

The default fount extends from $20 to $7F.

SD.GCUR See the entry for SD.POINT for details.

SD.LINE See the entry for SD.POINT for details.

SD.NCOL See the entry for SD.POS for details.

SD.NL See the entry for SD.POS for details.

SD.NROW	See the entry for SD.POS for details.

TRAP  #3   D0=$1B, 1E and 1F

SD.PAN SO.PANLN SO.PANRT

Pan part or all of a window

D0=$1B D0=$1E

D0=$1F

SD.PAN SD.PANLN

SD.PANRT

pan all of window pan cursor line

pan right hand end of cursor line

Call parameters	Return parameters

D1.W   distance to pan

D2

D3.W   timeout

A0	channel lD A1

A2

D1	???

D2.L  preserved D3.L  preserved A0	 preserved A1	???

A2	preserved

Error  returns:

NC  not  complete

NO  channel   not  open

The whole of a window, or the whole of the cursor line, or the right hand end of the cursor line may be panned by any number of pixels to the right or to the left. A positive distance implies that the pixels will move to the right. The space left behind will be filled with paper colour.

The cursor line is the whole height of the current character fount

(either 10 or 20 rows). The right hand end includes the character at the current cursor position.

S0.PANLN		See the entry for SD.PAN for details. S0.PANRT See the entry for SD.PAN for details. S0.PCOL	   See the entry for SD.POS for details.

TRAP  #3   D0=$17	SD.PIXP

Position cursor using pixel coordinates

Call  parameters	Return  parameters

D1.W   X-coordinate D2.W   V-coordinate D3.W    timeout

A0         channel lD

A1

A2

D1     ???

D2.L  preserved D3.L  preserved A0	 preserved A1	???

A2	preserved

Error returns:

NC  not complete

NO  channel not open

OR  off window

The cursor position is the top left hand corner of the next character rectangle referred to the top left hand corner of the window. This trap clears the pending newline in the window.

TRAP  #3  D0=$30

D0=$31

D0=$32

D0=$33

D0=$34

D0=$36

SD.POINT SD.LlNE SD.ARC SD.ELlPS SD.SCALE SD.GCUR

SD.POINT SD.ARC SD.ELlPS SD.GCUR

SD.LINE SD.SCALE

Plot a point, line, arc, ellipse, set scale or graphics cursor position. Expects parameters on the arithmetic stack pointed to by (A1)

Call  parameters

D1

D2

D3.W   timeout

A0	channel lD

A1	arithmetic stack pointer

A2

Error  returns:

NC  not  complete

NO  channel not open

Return  parameters

D1	???

D2.L  preserved

D3.L  preserved A0	preserved A1	???

A2	preserved

These four traps draw various lines and arcs in the window. Any point on these lines which falls outside the window will not be plotted.

The format of the parameters required is as follows:

SO.POINT	$00(A1)

$06(A1)

SO.LINE	$00(A1)

$06(A1)

$0C(A1)

$12(A1)

y-coordinate x-coordinate

y-coord of finish of line x-coord of finish of line y-coord of start of line

x-coord of start of line

SD.ARC	$00(A1)	angle subtended by arc

$06(A1)	y-coord of finish of line

$0C(A1)	x-coord of finish of line

$12(A1)	y-coord of start of line

$18(A1 )	x-coord of start of line

SD.ELlPS	$00(A1)	rotation angle

$06(A1)	radius of ellipse

$0C(A1)	eccentricity of ellipse

$12(A1)	y-coord of centre

$18(A1)	x-coord of centre

SD.SCALE	 $00(A1)	 y position of bottom line of window

$06(A1)	x position of left hand pixel of window

$0C(A1)	length of Y axis (height of window)

SD.GCUR	$00(A1)	graphics x-coordinate

$06(A1)	graphics y-coordinate

$0C(A1)	pixel offset to right

$12(A1)	pixel offset down

For all the graphics traps, the parameters on the A1 stack are floating point, and coordinates are referred to an arbitrary origin (default is 0,0) with an arbitrary scale (default is height of window = 100 units).

The calling program must allocate at least 240 bytes on the A1 stack.

TRAP #3  D0=$10 to 16

Cursor positioning  by character intervals

SD.POS

SD.NCOL

SD.NL

SD.NROW

D0=$10	SD.POS

D0=$11	SD.TAB

D0=$12	SD.Nl

D0=$13	SD.PCOl

D0=$14	SD.NCOl

D0=$15	SD.PROW

D0=$16	SD.NROW

absolute position tabulate

newline

previous column next column previous row next row

SD.PCOl SD.PROW SD.TAB

Call parameters	Return parameters

D1.W  column  number (D0=10,11)

D2.W  row  number (D0=10)

D3.W  timeout

A0	channel ID A1

A2

D1	???

D2.L   preserved

D3.L   preserved A0	 preserved A1	???

A2	preserved

Error returns:

NC not complete

NO channel not open

OR  position would  be out of window

In the case of an error return, the cursor position is not changed. The cursor position is the top left hand corner of the next character rectangle referred to the top left hand corner of the window. These traps clear the pending newline in the window.

SD.PROW Seethe entry for SO.POS for details.

TRAP  #3   D0=$A or B	SD.PXENQ

SD.CHENQ

Return the current window size and cursor position

D0=$A D0=$B

SD.PXENQ   enquiry in pixel coordinates

SD.CHENQ   enquiry in character coordinates

Call parameters	Return parameters

D1

D2

D3.W  timeout

A0	channel   10

A1	base of  enquiry   block

A2

D1	preserved

D2	preserved

D3.L  preserved

A0	preserved A1	???

A2	preserved

Error  returns:

NC  not complete

NO  channel not open

The window size (X,Y) and cursor position (X,Y) are put into a 4 word enquiry block. The top left hand corner of the window is cursor position 0,0. These traps activate the newline if pending in the window.

TRAP#3   D0=$26	SD.RECOL

Recolour  a window

Call  parameters	Return  parameters

D1

D2

D3.W   timeout

A0	channel lD

A1	pointer to colour list

A2

D1	???

D2.L  preserved

D3.L  preserved A0	preserved A1	???

A2	preserved

Error  returns:

NC  not  complete

NO  channel   not  open

A window may be recoloured without changing the information in it. This allows the same sort of effects as resetting the attributes of an attribute based screen, but it is very much slower.

The colour list is 8 bytes long and should contain the new colours required for each of the 8 colours in the window. Each of the new colours must be in the range 0 to 7. For 4 colour mode, only bytes 0,2,4 and 6 need to be filled in.

SD.SCALE See the entry for SD.POINT for details.

SD.SCRBT See the entry for SD.SCROL for details.

TRAP  #3   D0=$18 to 1A	SD.SCROL

SO.SCRBT

Scroll part or all of a window

D0=$18	SD.SCROL D0=$19	SD.SCRTP D0=$1A	SD.SCRBT

Call  parameters

D1.W   distance  to  scroll

D2

D3. W  timeout

A0        channel lD A1

A2

Error  returns:

NC  not  complete

NO  channel   not  open

SO.SCRTP

scroll all of window scroll top of window scroll  bottom of window

Return  parameters

D1	 ???

D2.L  preserved D3.L  preserved A0	 preserved A1	 ???

A2	 preserved

Part or all of a window may be scrolled; for partial scrolling the cursor is used as a reference. These traps cause pixels to be transferred from one row to another. Vacated rows of pixels are filled with paper colour. A positive scroll distance implies that the pixels in the window will be moved in a positive direction, ie, downwards.The space left behind will be filled with paper colour.

The division between the top of the window and the bottom of the window is the cursor line. The cursor line is included in neither the top nor the bottom of the window. The cursor is not moved.

SD.SCRTP See the entry for SD.SCROL for details.

TRAP  #3   D0=$2A   and  2B	SD.SETFL

SD.SETUL

Set flash and underscore

| DO=$2A | SD.SETFL | set flash |
| --- | --- | --- |
| DO=$2B | SD.SETUL | set underscore |

Call parameters	Return parameters

D1.B    0 attribute off	D1	???

else attribute on

D2		D2.L  preserved D3.W   timeout	D3.L  preserved A0	channel lD	A0	preserved A1		A1	???

A2	A2	preserved

Error  returns:

NC  not complete

NO  channel not open

SD.SETIN   See the entry for SD.SETPA for details.

TRAP  #3   D0=$2C	SD.SETMD

Set the character writing or plotting mode

Call parameters	Return parameters

D1.W   mode	D1	???

-1       ink is exclusive ored into the background

0	    character background is strip colour

1	    character background is transparent

0 or 1  plotting is in ink colour

D2

D3.W   timeout

A0	channel ID

A1

A2

Error  returns:

NC  not complete

NO  channel not open

D2.L   preserved

D3.L   preserved A0	 preserved A1	 ???

A2	 preserved

TRAP  #3   D0=$27   to  29	SO.SETPA

SO.SETIN

Set screen  colours

DO=$27	SD.SETPA DO=$28	SD.SETST

DO=$29	SD.SETIN

set paper colour set strip colour set ink colour

SO.SETST

Call  parameters	Return  parameters

D1.B    colour

D2

D3.W   timeout

A0	channel lD A1

A2

D1	 preserved D2	 preserved D3.L   preserved A0	 preserved A1	 ???

A2	preserved

Error returns:

NC  not complete

NO  channel not open

The screen driver uses three colours. There is the background colour of a window: referred to as paper colour; this is the colour which is used by the scroll, pan and clear operations. There is the colour which is used by the character generator to provide a highlighting background for individual characters or words: referred to as strip colour. Finally, there is the colour used for writing characters and drawing graphics: referred to as ink colour.

SO.SETST See the entry for SO.SETPA for details.

TRAP#3  D0=$20

Set character size and spacing

Call parameters

D1.W character width/spacing

0 single width, 6 pixel spacing

1 single width, 8 pixel spacing

2 double width, 12 pixel spacing

3 double width, 16  pixel spacing

D2.W  character height/spacing

1 single  height, 10 pixel  spacing

1 double height, 20 pixel  spacing

D3.W  timeout

A0	channel ID A1

A2

Error returns:

NC  not complete

NO  channel not  open

SD.SETST

Return parameters

D1	???

D2.L  preserved

D3.L  preserved A0	preserved A1	???

A2	preserved

The character generator supports two widths and two heights of character. In 8 colour mode, only the double width characters may be used. In addition the spacing between characters is entirely flexible, but for simplicity of use only two additional spacings are supported directly: these are 8 pixel and 16 pixel, in single and double width respectively.

Calls with D1=0 or 1 in 8 colour mode will operate as though a call had been made with D1 equal to 2 or 3.

SD.SETUL See the entry for SD.SETFL for details.

SD.TAB See the entry for SD.POS for details.

TRAP  #3   D0=$0

Redefine a window

Call  parameters

D1.B    border colour

D2.W   border width

D3.W   timeout

A0	channel lD

A1	base of window block

A2

Error returns:

SD.WDEF

Return  parameters

D1	???

D2.L  preserved

D3.L  preserved A0	 preserved A1	???

A2	preserved

NC  not complete

NO  channel not open

OR  window does not fit on page

This call redefines the shape or position of a window: the contents are not moved or modified, but the cursor is repositioned at the top left hand corner of the new window. The window block is 4 words long and is the width, height, X origin and Y origin.

16.0 Vectored Routines

Vector $110	BP.INIT

All addresses passed to this routine must be relative to A6.

BP.lNIT is used to link in a list of procedures and functions to be added to the SuperBASIC name table. Once added, the functions can be called from SuperBASIC in the same way as the procedures and functions built into the ROM.

On entry, A1 should point to a table in the following form:

word	approximate number of procedures (see below)

for each procedure

(word	pointer to routine - here

(byte	length of name of procedure

(characters

word	0

word	approximate number of functions (see below)

for each function

(word	pointer to routine - here (byte	length of name of function (characters

word	0

The "approximate	number" of procedures or functions is used to reserve internal table space. It should be exactly equal to the number

of procedures or functions unless the average length of the procedure

or function names exceeds 7, in which case it should be:

(total number of characters + number of functions or procedures + 7) /8

The pointers to the routines are relative to the address of the pointer

(e.g. DC.W ENTRY- *)

All registers except A 1, and D2 are preserved by BP.INIT and no more than 48 bytes are used on the user stack.

Vector   $120	BP.LET

All addresses passed to this routine must be relative to A6.

BP.LET assigns a value to be associated with an entry in the SuperBASIC name table. On entry, (A6,A3) should point to the name table entry, and (A6,A1) should point to the value to be assigned (see section 9.5 for details of the storage format for the various types of data). A1 and A3 should be on word boundaries.

The type of the entity to be assigned (and hence its length) is determined by the type in the name table entry.

On exit, D0 is an error code, and D1, D2, D3, A0, A 1 and A2 are smashed.

Vector  $11A	BV.CHRIX

All addresses passed to this routine must be relative to A6.

BV.CHRIX is used to reserve space on the arithmetic stack (A6,A1). On entry, the number of bytes required should be in D1.L: D0 to D3 are smashed.

Since not only the stack but the whole SuperBASIC area may move during the call, the arithmetic stack pointer should be saved in BV_RIP(A6), whence it should be retrieved after the call has been completed.

CA.GTFP  See the entry for CA.GTINT for details.

Vector   $112

$114

$116

$118

CA.GTINT CA.GTFP CA.GTSTR

CA.GTLlN

All addresses passed to these routines must be relative to A6.

These routines are used to get the values of actual parameters to SuperBASIC procedures or functions onto the arithmetic stack. Each routine assumes that all the parameters will be of the same type, as follows:

CA.GTINT CA.GTFP CA.GTSTR

CA.GTLlN

16-bit integer floating point

string

floating point: convert to 32-bit long integer

On entry, (A6,A3) points to the name table entry for the first parameter in the list, and (A6,A5) points to the entry for the last.

The number of parameters fetched is returned in the least significant word of D3. The values themselves are returned in order on the arithmetic stack (A6,A 1) with the first parameter at the top (lowest address) of the stack.

These routines smash D1, D2, D4, D6, A0 and A2. D0, and also the condition codes, give the error code. The separator flags in the name table entries are also smashed.

CA.GTLlN See the entry for CA.GTINT for details.

CA.GTSTR See the entry for CA.GTINT for details.

CN.BTOIB See the entry for CN.DTOF for details.

CN.BTOIL See the entry for CN.DTOF for details.

CN.BTOIW See the entry for CN.DTOF for details.

Vector	$EC CN.DATE	get date and time

$EE CN.DAY	get day of week

CN.DATE

CN.DAY

Call parameters	Return parameters

D1.L  date  (internal value) D2

D3

A0

A1	pointer to stack

A2

A3

D1	 preserved D2	 preserved D3	preserved A0	 preserved

A1	pointer to stack

A2	preserved

A3	preserved

All addresses passed to these routines must be relative to A6.

There are two date conversion routines: CN.DATE returns the date in the form yyyy mmm dd hh:mm:ss, CN.DAY returns a three letter day of the week. The result is put on the A 1 stack in string format. At least 22 bytes are required by CN.DATE and at least 6 bytes by CN.DAY. CN.DAY See the entry for CN.DATE for details.

Vector   $100  CN.DTOF	 floating point

$102  CN.DTOI	integer

&$104   CN.BTOIB	binary (byte)

&$106   CN.BTOIW	binary (word)

&$108   CN.BTOlL	binary (long)

&$10A   CN.HTOIB	hex (byte)

&$10C   CN.HTOIW	hex (word)

&$10E  CN.HTOlL	hex (long)

CN.DTOF

CN.BTOlL

CN.BTOIW

CN.DTOI

CN.HTOIB CN.HTOlL CN.HTOIW

Call parameters	Return parameters

D1	D1

???

D2	D2	???

D3

D7	0 or ptr to end buffer

A0	pointer to buffer A1	pointer to stack A2

A3

D3	???

D7	preserved

A0	 pointer to buffer A1	 pointer to stack A2	???

A3	???

Error returns:

XP error in conversion (eg 1..0 as floating pt.

or no digits or too many hex or binary digits)

All addresses passed to these routines must be relative to A6. Utilities marked & are non-functioning in V1.03 and earlier.

These routines convert from ASCII characters in a buffer (pointed to by

A0) to a value on the stack (pointed to by A1).

The hex and binary conversions from ASCII to number, always put a

long word on the A1 stack. A1 is set to point to the least significant

byte or less significant word for the byte and word conversions.

The decimal conversions may use up to about 30 bytes on the A1 stack.

If there is an error then A0 and A1 are both unchanged. Otherwise, on return, A1 points to the return value (floating point, long word, word or byte) and AO points to the next character in the buffer.

CN.DTOI  See the entry for CN.DTOF for details.

Vector	$F0   CN.FTOD	floating point		    CN.FTOD

$F2   CN.ITOD	integer				CN.ITOBB

$F4   CN.ITOBB	binary (byte)			CN.ITOBL

$F6   CN.ITOBW	binary (word)			CN.ITOBW

$F8   CN.ITOBL	binary (long)			CN.ITOD

$FA   CN.ITOHB	hex (byte)			CN.ITOHB

$FC   CN.ITOHW	hex (word)			CN.ITOHL

$FF   CN.ITOHL	hex (long)			CN.ITOHW

Call parameters			Return parameters

D0   ???

D1					D1   ???

D2					D2   ???

D3					D3   ???

A0   pointer to buffer			A0   pointer to buffer

A1   pointer to stack			A1   pointer to stack

A2					A2   ???

A3					A3   ???

All addresses passed to these routines must be relative to A6.

These routines convert a value on the stack (pointed to by A1) to a set of ASCII characters in a buffer (pointed to by A0).

CN.HTOIB See the entry for CN.DTOF for details. CN.HTOIL See the entry for CN.DTOF for details. CN.HTOIW	See the entry for CN.DTOF for details. CN.lTOBB See the entry for CN.FTOD for details.

CN.lTOBL   See the entry for CN.FTOD for details. CN.ITOBW    See the entry for CN.FTOD for details. CN.ITOD    See the entry for CN.FTOD for details. CN.ITOHB    See the entry for CN.FTOD for details. CN.lTOHL   See the entry for CN.FTOD for details.

CN.ITOHW	See the entry for CN.FTOD for details.

Vector   $122

Decode a device name

Call  parameters

D1

D2

D3

A0	pointer to name

A1

A2

A3	pointer to parameters

Error  returns:

IO.NAME

Return  parameters

D1	??? D2	??? D3	???

A0	preserved

A1	???

A2	???

A3	preserved

ERR.NF not recognised

ERR.BN name recognised - but bad parameters

This routine parses a device name. Given a device name and a description of the syntax of the name to be checked against and for the possible parameters to be appended to it, the routine determines·) whether the name is recognised, and extracts the parameters if it is. The device name is formed using four components:

Name Separator Number

Code

ASCII characters, normally letters. Case is ignored. Single ASCII character. Case is ignored.

Decimal number in the range 0 to 32767

One of a list of ASCII characters

On entry to the routine, AO must point to the device name (which is in the usual Qdos string format), A3 must point to an area of memory which is sufficient to hold the decoded parameter values, and A6 must point to the base of system variables. The device description starts 6 bytes after the call, and is in the following format:

word	 number of characters in the device name to be checked for words	the characters of the device name to be checked for

word	number of parameters

For each parameter, one of the following options:

byte space, byte separator, word default value (numeric with separator)

word negative number, word default value (numeric with no separator)

word positive number of possible codes, bytes for the ASCII

codes

Note that all letters must be in upper case.

For each numeric parameter value in the description, the utility will return either the value given in the device name, or the default. For each list of codes in the description the utility will return the position of the code in the list, or zero.

Examples:

The CON description is:

DC.W DC.W DC.W DC.W

DC.W

3,'CON'

5

'_',448,'X',180

'A',32,'X',16

‘_',128

console

five parameters window size window position

keyboard queue length

Device  name	Parameters

CON			       448,180,0,0,128

CON_256		       256,180,0,0,128

con_60			       448,180,0,0,60

cona0x12		       448,180,0,12,128

con_256x64a64x128_20	       256,64,64,128,20

The SER description is:

DC.W	 3,'SER' DC.W	4

DC.W	-1,1

DC.W	4,'OEMS' DC.W	2,'IH'

DC.W	3.’RZC’

RS232 serial device four parameters

port number (default 1)

parity (odd/even/mark/space) ignore/use handshaking Raw/use CTRLZ/use CR

Device  name	Parameters

SER SERE

ser2miZ

1,0,0,0

1,1,0,0

2,3,1,2

If the name is not matched, the routine returns immediately after the call with ERR.NF in D0. If the name is matched but the additional information is incorrect, it returns 2 bytes after the call with ERR.BN in D0. If a match is found, it returns 4 bytes after the call with D0=0.

IO.QEOF   See the entry for IO.QSET for details. IO.QIN     See the entry for IO.QSET for details. IO.QOUT	See the entry for IO.QSET for details.

Vector   $DC  IO.QSET	set up a queue

$DE  IO.QTEST   test status of queue

$E0   IO.QIN	put byte into queue

$E2   IO.QOUT	extract byte from queue

IO.QSET

IO.QEOF IO.QIN

IO.QUOT

$E4   IO.QEOF	put end of file marker into queue

IO.QTEST

Call parameters

D1.L  queue length or data

D2

D3

A0 A1

A2	pointer to queue

A3

Return  parameters

D1	data

D2	preserved/free space

D3	preserved A0	preserved A1	preserved A2	preserved

A3	modified by QIN, QOUT,

QTEST,QSET

Error returns:

ERR.NC  queue is full (QIN) or empty (QOUT, QTEST)

ERR.EF  end of file reached (QOUT, QTEST)

The data length should be less than 32767

IO.QTEST  See the entry for IO.QSET for details.

IO.SERIO   See the entry for IO.SERQ for details.

Vector  $E8  IO.SERQ	direct queue handling

$EA IO.SERIO	general IO handling

IO.SERQ

IO.SERIO

Call parameters	Return parameters

D1	 standard IOSS value D2	standard IOSS value D3	standard IOSS value A0	standard IOSS value A1	standard IOSS value A2

A3

D1	standard IOSS value D2	standard IOSS value D3	???

A0	preserved

A1	standard IOSS value

A2	???

A3	???

Error returns:

ERR.BP undefined action

or errors returned from supplied routines

These routines must be called from supervisor mode, with A6 pointing to the base of system variables. It may not be called from a task which services an interrupt.

IO.SERQ is a direct queue handling routine. When the channel definition block is set up for simple serial I/O then the 7th and 8th long words should be set to point to the queues for input and output respectively. If either input or output is prohibited, then the corresponding pointer should be zero.

IO.SERQ should be called with standard 1055 values in D0, D1, D2, D3,A0 and A1.

For serial I/O where the operations for byte input and output are not so simple, the routine IO.SERIO may be called. The call instruction should be followed by three long words, these being the entry addresses for

testing for pending input, (next byte in D1)

fetch byte, (byte in D1)

send byte. (byte in D1)

The use of absolute addresses for these may prove awkward;   so the entry  to this routine  is best included  in the  physical definition   block for the driver:

at $28(A3) or similar	or

387800E8	MOVE.W	$E8,A4	DC. L	TEST

4E94	JSR	(A4)	DC. L	FETCH

DC.L	TEST	DC. L	SEND

DC.L	FETCH	4E75	RTS

DC.L	SEND

4E75	RTS

invoked by	or

JSR	$28(A3)	PEA	$28(A3) MOVE.W	$E8,A4

JMP       (A4)

For the calls to the three service routines D0 should be returned as the error code,  D1 to D3 and A1 to A3 inclusive are volatile.

Both of these calls treat actions 0,1,2,3,5 and 7, the header set and read actions and load and save: for undefined actions they return ERR.BP.

Vector   $124  MD.READ

$126  MD.WRITE

$128  MD.VERIN

$12A  MD.SECTR

read a sector write a sector verify a sector

read a sector header

MD.READ

MD.SECTR

MD.VERIN

MD.WRITE

Call  parameters

D1

D2

D7

A0

A1	pointer to start of bufr

A2

A3	$18020

Error  returns: MD.WRITE

MD.READ, MD.VERIN

MD.SECTR

Return  parameters

D1	file nr (read/verify)

D2	 block nr (read/verify) D7	sector nr (read headr) A0	 ???

A1	pointer   to  end  of  bufr

A2	???

A3	$18020

none

normal - failed

return+2 OK

normal - bad  medium

return+2 - bad sector header return  +4  -  OK

The microdrive support routines are vectored to simplify the writing of file recovery programs. On entry A3 must point to the microdrive control register, and the interrupts must be disabled. All registers except A3 and A6 are treated as volatile.

These routines do not set D0 on return but have multiple returns.

Before calling MD.WRITE the stack pointer must point to a word: the file number and the block number of the sector to be written are in the high and low byte respectively.

These vectors point to $4000 bytes before the actual entry point. The following code may be used:

MOVE.W aa.aaaa,An

JSR    $4000(An)

MD.SECTR See the entry for MD.READ for details.

MD.VERIN See the entry for MD.READ for details.

MD.WRITE See the entry for MD.READ for details.

Vector   $C0	MM.ALCHP

Allocate common heap area

Call parameters	Return  parameters

D1.L   space required

D2

D3

A0

A1

A2

A3

D1.L  space allocated

D2	???

D3	???

A0	base of area allocated

A1	??? A2	??? A3	???

Error returns:

OM   out of memory

This routine must be called from supervisor mode, with A6 pointing to the base of system variables. It may not be called from a task which services an interrupt.

The space requested must include room for the heap entry header. For

simple heap entries this is 16 bytes long, for IOSS channels this is 24 bytes long.

The address of the heap area is the base of the area allocated, not the base of the area which may be used (contrast with trap #1 D0= $18 and $19).

The area allocated is cleared to zero.

Vector   $D8	MM.ALLOC

Allocate an area in a heap

Call parameters	Return parameters

D1.L  length required

D2

D3

A0	ptr to ptr to free space

A1

A2

A3

D1.L   length allocated

D2	???

D3	???

A0	base of area allocated

A1	??? A2	??? A3     ???

Error returns:

OM no free space large enough

See section 4.1 for details of the heap allocation mechanism.

Vector $DA				MM.LNKFR

Link a free space (back) into a heap

Call parameters

D1.L  length to link in

D2

D3

A0	base of new space

A1	ptr to ptr to free space

A2

A3

Return parameters

D1	 ??? D2	??? D3	??? A0	??? A1	??? A2	??? A3	 ???

Vector   $C2

Release common heap space

MM.RECHP

Call parameters

D1

D2

D3

A0	base of area to release

A1

A2

A3

Return parameters

D1	 ??? D2	??? D3	??? A0	??? A1	??? A2	??? A3	???

This routine must be called from supervisor mode, with A6 pointing to

the base of system variables. It may not be called from a task which services an interrupt. See entry for MM.ALCHP

Vector     $11C RI.EXEC    executes an operation	  RI.EXEC

$11E RI.EXECB  executes a list of operations	RI.EXECB

Call parameters	Return parameters

D0.W  operation (RI.EXEC) D1

D2

D3

A0

A1	pointer to arith stack

A2

A3	ptr to operation list

A4	ptr to base of var area

D0	error  code D1	preserved D2	preserved D3	preserved A0	preserved A1	updated

A2	preserved

A3	preserved

A4	preserved

Error returns:

OV  arithmetic overflow

All addresses passed to these routines must be relative to A6. The arithmetic package is available for general use through two vectors: the first executes a single operation; the second executes a list of operations.

The package operates on floating point numbers on a downward stack pointed to by (A6,A1.L). lt operates on the top of the stack (TOS) which is pointed to by (A6,A1.L), and the next on stack (NOS) at 6(A6,A1.L).

See section 9.5 for details of the floating point format.

The interpreter takes two types of operation codes. The first is a true arithmetic operation with an operation code between $02 and $30 inclusive, the second is a negative code between $FFFF and $FF31 inclusive: this indicates a load or store operation of a floating point number to or from the location given by the calculation (A6.L +A4.L +opcode$FFFE). lf bit 0 of the opcode is clear the operation is a load (A1 decremented by 6, creating a new TOS), if it is set the operation is a store (A1 incremented by 6, NOS- ->TOS)

For RI.EXEC the operation code should be passed asa word. For RI.EXECB the operation codes are in a table of bytes pointed to by A3. The table isterminated by a zero byte.

Note: for the function EXP, D7 should be set to zero or an erroneous value will be returned.

The operation codes for the interpreter are asfollows:

CODE

function change to A1

$02	RI.NINT

$04	RI.INT

$06	RI.NLlNT

$08	RI.FLOAT

$OA	RI.ADD

$OC	RI.SUB

$OE	RI.MULT

$10	RI.DIV

$12	RI.ABS

$14	RI.NEG

$16	RI.DUP

$18	RI.COS

$1A	RI.SIN

$1C	RI.TAN

$1E	RI.COT

$20	RI.ASIN

$22	RI.ACOS

$24	RI.ATAN

$26	RI.ACOT

$28	RI.SQRT

$2A	RI.LN

$2C	RI.LOG10

$2E	RI.EXP

$30	RI.POWFP

nearest integer to TOS +4

truncate TOS to integer +4

nearest long integer to TOS +2 integerTOS  to floating  point -4

add TOS to NOS +6

subtract TOS from NOS +6

multiply  TOS by NOS +6

divide TOS into NOS +6 positive value of TOS  0 negate TOS  0

duplicate TOS -6

cosine

sine

tangent

cotangent

arcsine

arccosine

arctangent

arccotangent

square root

natural logarithm

logarithm to base 10

exponential

NOS to the power of TOS  + 6

)

)

)

)

)

) change TOS only

) A1 unchanged

)

)

)

)

)

UT.COM  See the entry fer UT.WINDW for details.

Vector  $E6

Compare two strings

Call parameters

D0.B comparison type

D1

D2

D3

A0	base of string 0 wrt A6

A1	base of string 1 wrt A6

A2

A3

A6	base address register

Return parameters

D1.L  -1, 0, or  +1

01	preserved

02	preserved

03	 preserved AO	 preserved A 1	 preserved A2	preserved A3	preserved

A6	preserved

UT.CSTR

All addresses passed to this routine must be relative to A6.

D0 (and the status register) is set negative if the string at (A6,A0) is less than the string at (A6,A 1) etc.

UT.ERRO

UT.ERR

Vector   $CA  UT.ERRO

$CC  UT.ERR

Call parameters

D0.1 error code

D1

D2

D3

A0    channel ID (UT.ERR  only) A1

A2

A3

write error message to channel 0 write error message to given channel

Return parameters

D0.1 preserved

D1	preserved

D2	preserved

D3	preserved A0    preserved A1    preserved A2	preserved A3	preserved

These routines must be called from user mode.

These routines exist for writing simple messages to a channel. They are

basic error message handlers which write a standard or device driver

supplied error message to either the command channel 0, or else to a

defined channel.

UT.LINK

UT.UNLINK

Vector   $02   UT.LINK

$04   UT.UNLNK

link an item into a list

unlink an item from a list

Call parameters	Return parameters

D1

D2

D3

A0	base of item (un)linked

A1	pointer to previous item

A2

A3

D1	preserved

D2	preserved

D3	 preserved A0	 preserved A1	updated A2	 preserved

A3	preserved

These two routines are provided for handling linked lists.

These routines are passed the base address of the item to be linked or unlinked, and a pointer which points to either the pointer to the first item in the list, or to an item in the list.

When an item is linked in, it will be linked in at the start of the list, or, if the pointer was to an item in the list, after that item.

When an item is removed, the pointer may point to the pointer to the

first item in the list, or to any item in the list before the item to be removed.

When starting a new list, the pointer to the first item in the list must be zero.

Each item in the list must have 4 bytes reserved at the start for the link pointer.

Vector   $CE	UT.MINT

Convert an integer to ASCII and send it to the defined channel

Call parameters

D1.W   integer   value

D2

D3

A0	channellD A1

A2

A3

Error returns:

All the usual IO

Return parameters

D1	??? D2	??? D3	???

A0	preserved

A1	???

A2	preserved

A3	preserved

This routine ought usually to be called from user mode.

Vector   $D0	UT.MTEXT

Send a message to a channel

Call parameters	Return parameters

D1	D1

???

D2	D2	???

D3

A0	channellD

A1	base of  message

A2

A3

D3	???

A0	preserved

A1	???

A2	preserved

A3	preserved

Error  returns:

All the usual IO

This routine ought usually to be called from user mode.

The above routines (UT.MINT and UT.MTEXT)  are provided to write parts of more complex messages to a defined channel.

The message is in the form of a text string: number of characters (word) followed by the characters in ASCII. If a new line is required at the end of the message, this should be included in the message. If the channel is 0 then D3 will be returned 0, otherwise D3 will be returned -1. In version V1.03 and earlier, DO is set to the error return but is not tested so the condition codes will not be correct. As a special concession, interrupt servers and other supervisor mode routines can call these routines with A0=0. If the command channel is in use, they will attempt to use channel 1. This operation is not recommended,	but it does seem to work!

UT.SCR See the entry for UT.WINDW for details.

UT.UNLNK See the entry for UT.LlNK for details.

UT.WINDW

Vector   $C4  UT.WINDW

$C6  UT.CON

$C8  UT.SCR

set up a window using a supplied name

set up console window

set up screen window

UT.CON

UT.SCR

Call parameters	Return parameters

D1	D1	???

D2	D2	???

D3	D3	???

A0	ptr to name (WINDW only)       A0	channel  ID

A1	ptr to parameter block	A1	??? A2		A2	??? A3		A3	???

Error returns:

BN   bad device name (WINDW only) OM   out of memory

NO   out of channels

OR   window is off-screen

The above three routines, which must be called in user mode, set up console or screen windows using a parameter list which follows the call statement. In the first case, the window is opened using a name which has been supplied, a block of parameters defining the border, and the paper, strip and ink colours. The window is set up and cleared for use.

The second and third routines define the window using an additional block of four words.

The parameter block is as follows:

$00	border colour (byte)

$01	border width (byte)

$02	paper/strip colour (byte)

$03	ink colour (byte)

$04	width (word)		)

$06	height (word)		)

$08	X origin (word)		)

$0A	Y origin (word)		)

not required for UT.WINDW

17.0 Qdos System Standards

In order to make best use of the third-party work, both software and hardware, currently going on on the QL, a number of Sinclair standards have been produced.

1. Floppy disc standard - This covers the physical layout, formatting, directory structure and disk handling of floppy disks under Qdos.

2. Relocatable object file standard - To allow the linking of separately compiled modules, potentially written in different languages.

These standards are available on application to Sinclair Research at the address in the introduction.

18.0 Qdos Keys

The following sections contain keys for various features of Qdos. These

keys provide a definition for several of the data structures within Qdos.

18.1  Error Keys

The following keys indicate error messages already defined in the system. A positive error code istaken as an address of a user-supplied error message. See the Concepts manual for a fuller description ofthe way in which these are used by the procedures built into SuperBASIC.

ERR.NC ERR.NJ ERR.OM ERR.OR ERR.BO ERR.NO ERR.NF ERR.EX ERR.IU ERR.EF ERR.DF ERR.BN ERR.TE ERR.FF ERR.BP ERR.FE ERR.XP ERR.OV ERR.NI ERR.RO ERR.BL

-1	operation not complete

-2     not a valid job

-3     out of memory

-4	out of range

-5	buffer overflow

-6	channel not open

-7	file or device not found

-8	file already exists

-9	file or device in use

-10   end of file

-11    drive full

-12    bad device name

-13   transmission error

-14   format failed

-15   bad parameter

-16   file error

-17   error in expression

-18   arithmetic overflow

-19   not implemented (yet)

-20   read only

-21   bad line (syntax error in BASIC)

18.2  System Variables

The following list gives the offset of each system variable from the base

of the system variables (whose position can be found using the MT.lNF

trap), together with the length of the variable.

SV_IDENT	$00 word	identification word

The following variables are the pointers which define the current state of the Qdos memory map.

SV_CHEAP	$04  long	 base of common heap area

SV_CHPFR	$08  long	first free space in common heap area SV_FREE	$0C  long	base of free area

SV_BASIC	$10  long	base of basic area

SV_TRNSP	$14  long	base of transient program area

SV_TRNFR	$18  long	first free space in transient program area

SV_RESPR	$1C  long	base of resident procedure area

SV_RAMT	$20  long	top of ram (+1)

SV_RAND	$2E  word	random number

SV_POLLM	$30  word	count of poll interupts missed

SV_TVMOD	$32  byte	0 if not TV display

SV_SCRST	$33  byte	screen status  (0= active)

SV_MCSTA	$34  byte	current value of display control register

SV_PClNT	$35  byte	current value of interrupt control/mask register

SV_NETNR	$37  byte	network station number

The following system variables are pointers to the list of tasks and drivers.

SV_I2LST SV_PLlST SV_SHLST SV_DRLST SV_DDLST

$38   long

$3C  long

$40   long

$44   long

$48   long

pointer to list of interrupt 2 drivers pointer to list of polled tasks

pointer to list of scheduler tasks pointer to list of device drivers

pointer to list of directory device drivers

SV_KEYQ	$4C  long

SV_TRAPV	$50   long

pointer to a keyboard queue

pointer to the trap redirection table

The following system variables are pointers to the resource management tables. The slave block tables have 8 byte entries, whilst the others have 4 byte entries.

SV_BTPNT

$54	long	pointer to most recent slave block entry

SV_BTBAS	$58	long	pointer to base of slave block table

SV_BTTOP	$5C	long	pointer to top of slave block table

SV_JBTAG	$60	word	current value of job tag

SV_JBMAX	$62	word	highest current job number SV_JBPNT	$64	long	pointer to current job table entry SV_JBBAS	$68	long	pointer to base of job table SV_JBTOP	$6C	long	pointer to top of job table

SV_CHTAG	$70	word	current value of channel tag SV_CHMAX	$72	word	highest current channel number SV_CHPNT	$74	long	pointer to last channel checked SV_CHBAS	$78	long	pointer to base of channel table SV_CHTOP	$7C	long	pointer to top of channel table

The following variables contain information about how to treat the keyboard, and about other aspects of the IPC and serial port communications. SV_CAPS, SV_ARDEL, SV_ARFRQ and SV_CSUB can safely be poked.

|  | SV_MDRUN | $EE | byte | which drive is running? |
| --- | --- | --- | --- | --- |
|  | SV_MDCNT | $EF | byte | microdrive run-up run-down counter |
|  | SV_MDDID | $F0 | 8 bytes | drive ID*4 of each microdrive |
|  | SV_MDSTA | $F8 | 8 bytes | status 0=no pending ops |
|  | SV_FSDEF | $100 | 16*long | pointers to file system physical definition |
|  | SV_FSLST | $140 | long | pointer to list offile channel definitions |

The following area, between $180 and $480 is reserved for the supervisor stack. There is no explicit stack protection in the code, although the stack should be of sufficient size for most normal purposes.

18.3  SuperBASIC Variables

Note that the system variable SV_BASIC points to the bottom of the SuperBASIC area, where its job header, which is $68 bytes long, is located. The value of A6 used during the interpreter points to the address immediately above the job header, which contains a set of variables formatted as shown in this table.

The first part of the area holds the pointers to the various areas of memory used by the interpreter: it defines the partitioning of

SuperBASIC's own area of memory.

BV_START	0	start of pointers

| BV_BFBAS | $00 | long | buffer base |
| --- | --- | --- | --- |
| BV_BFP | $04 | long | buffer running pointer |
| BV_TKBAS | $08 | long | token list |
| BV_TKP | $OC | long |  |
| BV_PFBAS | $10 | long | program file |
| BV_PFP | $14 | long |  |
| BV_NTBAS BV_NTP | $18 $1C | long long | name table |
| BV_NLBAS | $20 | long | name list |
| BV_NLP | $24 | long |  |
| BV_VVBAS BV_VVP | $28 $2C | long long | variable values |
| BV_CHBAS | $30 | long | channel table |
| BV_CHP | $34 | long |  |
| BV_RTBAS | $38 | long | return table |

BV_RTP	$3C	long

BV_LNBAS	$40	long	line number table

BV_LNP	$44	long

BV_CHANGE   $48	change of direction marker

18.4  Offsets on BASIC Channel Definitions

The following section gives the format of an entry in the SuperBASIC

channel table, These entries can be monitored or modified by user-

defined SuperBASIC procedures which need to have a channel

attached using a '#n' construct.

| CH.ID | $00 |  | channel id |  |
| --- | --- | --- | --- | --- |
| CH.CCPY CH.CCPX | $04 $0A | float float | current cursor position, y current cursor position, x |  |
| CH.ANGLE | $10 | float | turtle angle |  |
| CH.PEN | $16 | byte | pen status (up or down) |  |
| CH.CHPOS | $20 | word | character position on line |  |
| CH.WIDTH | $22 | word | width of line in characters |  |
| CH.SPARE | $24 |  | ..spare .. |  |

CH.LENCH	$28	length of a channel definition block

18.5  Job Header and Save Area Definitions

The location of the job table can be found by looking at the system

variables SV_IBBAS and SV_IBTOP. Each entry in the table is a longword pointing to a block of $68 bytes in the format given here.

JB_LEN*	$00	long	total length of job area

JB_START	$04	long	 start address on activation (usually 0) JB_OWNER	$08	long	job ID of the owner of this job JB_HOLD	$0C long	 ptr to byte to be cleared when job

released

JB_TAG*	$10	word	tag for this job, allocated by MT.CJOB JB_PRIOR	$12	byte	current accumulated priority:

set to zero when the job is executing,

incremented on each scheduler call ifthe job isactive but not executing

JB_PRINC	$13	byte	priority increment (the actual priority of

the job) set to zero if the job is inactive

SuperBASIC activates jobs at priority $20

JB_STAT*	$14	word	job status

0 => not suspended

>0 => numberofframe times to release

-1 => suspended

-2 => waiting for another job to finish

|  | JB_RELA6 | $16 | byte | MSB set if next trap #2 or addressing relative to A6 | #3 has |
| --- | --- | --- | --- | --- | --- |
|  | JB_WFLAG | $17 | byte | set if there is a job waiting completion of this one | on |
|  | JB_WJOB | $18 | long | job Id of waiting job |  |
|  | JB_TRAPV | $1C | long | pointer to trap redirection | vectors |
|  | JB_00 | $20 |  | save offset of D0 |  |
|  | JB_01 | $24 |  | save offset | of D1 |  |
|  | JB_02 | $28 |  | save offset | of D2 |  |
|  | JB_03 | $2C |  | save offset | of D3 |  |
|  | JB_04 | $30 |  | save offset | of D4 |  |
|  | JB_05 | $34 |  | save offset | of D5 |  |
|  | JB_06 | $38 |  | save offset | of D6 |  |
|  | JB_07 | $3C |  | save offset | of D7 |  |
|  | JB A0 | $40 |  | save offset | of A0 |  |
|  | JB A1 | $44 |  | save offset | of A1 |  |
|  | JB A2 | $48 |  | save offset | of A2 |  |
|  | JB A3 | $4C |  | save offset | of A3 |  |
|  | JB A4 | $50 |  | save offset | of A4 |  |
|  | JB A5 | $54 |  | save offset | of A5 |  |
|  | JB A6 | $58 |  | save offset | of A6 |  |
|  | JB A7 | $5C |  | save offset | of A7 |  |
|  | JB_USP | $5C |  | save offset | of USP |  |
|  | JB_SR | $60 |  | save offset | of SR |  |
|  | JB_PC | $62 |  | save offset | of PC |  |
|  | JB_ENO | $68 |  |  |  |  |

Thus the job identified by <job-ID>  starts at ((SV_JBBAS) +4  * <job- ID>.W), and the  most  significant  word  of <job-ID> must match the tag held at 10H on from  this address (otherwise  that job no longer exists). A negative  <job-ID> implies that  the job no longer  exists, as does a value of <job-lD>.W which is greater  than  the length  of the job table held in SV_IBMAX.

Entries marked  by * should not be modified. Other entries may be modified   by a trap, or may be changed directly with caution.

18.6  Memory  Block Table Definitions

The following keys define the format of the start of a slave block.

BT_STAT BT_PRIOR BT_SECTR BT_FILNR BT_BLOCK BT_END

$00	byte

$01	byte

$02	word

$04	word

$06	word

$08

drive ID/status byte - see below block priority

sector number (Microdrive*2)

file number (Microdrive) logical

block number (Microdrive) location

The most significant 4 bits of the status byte contain the pointer to the physical device block SV_FSDEF, the least significant are the status

codes:

Status code masks:

| BT.ACTN | 00001100B | check for read or write request |
| --- | --- | --- |
| BT.INUSE | 00001110B | check if a file block in use |

Bits  of  status  codes:

| BT..FILE | 0 | 1 if a file block |
| --- | --- | --- |
| BT..ACCS | 1 | 1 if contents may be accessed |
| BT..WREQ | 2 | 1 if block required to be written |
| BT..RDVR | 3 | 1 if block required to be read/verified |

18.7  Channel Definitions

The position of a channel definition block corresponding to a given channel 10 can be found using a similar method to that used for finding the block for a job described in section 3.1. The relevant system variables are SV_CHBAS and SV_CHMAX.

Channel definition header for all channels:

CH_LEN	$00	long CH_DRIVR	$04	long CH_OWNER	$08	long CH_RFLAG	$0C	long CH_TAG	$10	word CH_STAT	$12	byte

CH_ACTN	$13	byte CH_JOBWT	$14	long CH_END	$18

length of definition  block address of driver

owner job

address to be set when space released

channel tag

status - 0 OK, negative waiting

-1   A1 abs, $80 A1  rel A6 stored action for waiting job ID of job waiting  on IO

Extended channel definition for plain serial queues:

CH_QIN CH_QOUT CH_QEND

$18	long

$1C    long

$20

pointer to input queue (or zero)

pointer to output  queue (or zero)

Device driver header:

CH_NEXT CH_INOUT CH_OPEN CH_CLOSE

$00	long

$04	long

$08	long

$0C    long

pointer to next driver entry for input and output entry for open

entry for close

The following are for directory devices (file system) only:

CH_SLAVE	$10	long

CH_RENAM	$14	long

entry for slaving blocks entry  reserved for rename

CH_FORMT	 $1C   	long	entry for format  medium CH_DFLEN	$20		long	length of physical definition  block CH_DRNAM	 $24	 2+n  bytes	drive name

18.8 File System Definition Blocks

File system channel definition block format:

FS_NEXT	$18	long	link to next file system channel

FS_ACCES	$1C	byte	access mode

FS_DRIVE	$1D	byte	drive ID

FS_FILNR	$1E	word	file number

FS_NBLOK	$20	word	block containing next byte

FS_NBYTE	$22	word	next byte in block

FS_EBLOK	$24	word	end of file (block)

FS_EBYTE	$26	word	end of file (byte in block)

FS_CBLOK	$28	long	pointer to table for current slave block

FS_UPDT	$2C	byte	set if file is updated

FS_FNAME	$32	2+36	file name

FS_SPARE	$58	72 bytes

FS_END	$A0

The common part of a physical definition block

FS_NMLEN	$24			max length of file name

FS_HDLEN	$40			length of file system header

FS_DRIVR	$10	long	pointer to driver

FS_DRIVN	$14	byte	drive number

FS_MNAME	$16	word+10 bytes  medium name

FS_FILES	$22	byte	number of files open

18.9  Screen Driver Data Block Definition

This is the format of the block handed to a screen driver operation.

SD_XMIN	$18	word	window top LHS

SD_YMIN	$1A	word

SD_XSIZE	$1C	word	window size

SD_YSIZE	$1E	word

SD_BORWD	$20	word	border width

SD_XPOS	$22	word	cursor position

SD_YPOS	$24	word

SD_XINC	$26	word	cursor increment

SD_YINC	$28	word

SD_FONT	$2A	2*long	font addresses

SD_SCRB	$32	long	base address of screen

SD_PMASK	$36	long	paper colour mask

SD_SMASK	$3A	long	strip colour mask

SD_IMASK	$3E	long	ink colour mask

SD_CATTR	$42	byte	character attributes

SD_CURF	$43	byte	cursor flag 0=suppressed, >0=visible

SD_PCOLR	$44	byte	paper colour byte

SD_SCOLR	$45	byte	strip colour byte

SD_ICOLR	$46	byte	ink colour byte

SD_BCOLR	$47	byte	border colour byte

SD_NLSTA	$48	byte	new line status (>0 implicit, <0 explicit)

SD_FMOD	$49	byte	fill mode (0=off, 1=on)

SD_YORG	$4A	float	graphics window y-origin

SD_XORG	$50	float	graphics window x-origin

SD_SCAL	$56	float	graphics scale factor

SD_FBUF	$5C	long	pointer to fill buffer

SD_FUSE	$60	long	pointer to user defined fill vectors

SD_LINEL	$64	word	line length in bytes

SD_END	$68

18.10  Queue  Header  Definitions

The following is the format of the header of a queue manipulated using the system's built-in queue handling routines.

| Q_EOFF | $00 | bit | end of file flag (MSbit) |
| --- | --- | --- | --- |
| Q_NEXTQ | $00 | long | link to next queue |
| Q_END | $04 | long | pointer | to end of queue |
| Q_NEXTIN Q_NXTOUT | $08 $0C | long long | pointer pointer | to next location to put byte in to next location to take byte |
|  |  |  | from |  |

Q_QUEUE	$10	start  of  queue

18.11  Arithmetic  Interpreter Operation

Codes

The following are the codes for the operations which can be performed on the QL through the vectored routines which access the arithmetic interpreter.

RLTERM RLNINT RI.INT RLNLlNT RLFLOAT RI.ADD RLSUB RLMULT RLDIV RLABS RI.NEG RLDUP RLCOS RLSIN RLTAN RLCOT RLASIN RLACOS RI.ATAN RLACOT

$00

$02

$04

$06

$08

$0A

$0C

$0E

$10

$12

$14

$16

$18

$1A

$1C

$1E

$20

$22

$24

$26

terminator byte

nearest integer to top of stack (tos)

truncate tos to integer

nearest long integer to tos integer tos to floating point

add tos to next on stack (nos) subtract tos from nos

multiply tos by nos divide tos into nos positive value of tos negate tos

duplicate tos

cosine sine tangent cotangent arcsine arccosine arctangent

arccotangent

RI.SQRT	$28

RI.LN	$2A

RI.LOG10	$2C 	RI.EXP		$2E RI.POWFP	$30

RI.MAXOP	$30

RI.LOAD	$00

RI.STORE	$01

square root natural log

logarithm to base 10 exponential

nos to power of tos

highest valid opcode load operation bit store operation bit

18.12 IPC Link Commands

These can be used with the MT.IPCOM trap.

RSET_CMD	0

STAT_CMD	1

OPS1_CMD	2

OPS2_CMD	3

CLS1_CMD	4

CLS2_CMD	5

RDS1_CMD	6

system  reset

report  input  status

open  RS232 channel   1 open  RS232  channel  2 close  RS232  channel   1 close  RS232  channel  2 read  RS232 channel   1

18.13	Hardware  Keys

The following are the addresses of the registers within the QL hardware.

PC_CLOCK

$18000

real time clock in seconds (long word)

PC_TDATA	$18022	transmit data

PC_TRAK1	$18022	Microdrive read track 1

PC_TRAK2	$18023	Microdrive read track 2

MC_STAT	$18063	display control

The  following is the format of the interrupt register.

| PC.INTRG | $01 | gap interrupt |
| --- | --- | --- |
| PC.INTRI | $02 | interface interrupt |
| PC.INTRT | $04 | transmit interrupt |
| PC.lNTRF | $08 | frame interrupt |
| PC.INTRE | $10 | external interrupt |
| PC.MASKG | $20 | gap mask |
| PC.MASKI | $40 | interface mask |
| PC.MASKT | $80 | transmit mask |

The following is the format of the transmit control register.

PC..SERN	3	serial port number PC..SERB	4	0=serial IO

PC..DIRO	7	direct output

PC.BMASK	00000111B	baud rate mask

PC.NOTMD	11100111B	all bits except mode control

PC.MDVMD	00010000B	Microdrive mode

PC.NETMD	00011000B	network mode

The following is the format of the Microdrive control/systems  register.

Write masks:

PC.READ PC.SELEC PC.DESEL PC.ERASE PC.WRITE

0010B

0011B

0010B

1010B

1110B

read (or idle) Microdrive select bit set

select bit not set

eraseon/write off eraseand write

The following  is the format  of the display control register.

| MC..BLNK | 1 | bit 1 blanks display |
| --- | --- | --- |
| MC..M256 | 3 | bit 3 sets 256 mode |
| MC..SCRN | 7 | bit 7 sets screen base |

18.14  Trap Keys

This section gives a summary of all of the Qdos traps, together  with their access keys passed in DO. All keys are in hex.

18.14.1   Trap  1 Keys (Manager Traps) -

MT.INF	$00	get system information

MT.CJOB	$01	create a job

MT.JINF	$02	get information on job

MT.RJOB	$04	remove a job

MT.FRJOB	$05	force remove a job

MT.FREE	$06	find out how much free spacethere is

MT.TRAPV	$07	set pointer to trap redirection vectors

MT.SUSJB	$08	suspend a job

MT.REL.lB	$09	release a job

MT.ACTIV	$0A	activate a job

MT.PRIOR	$0B	set a job priority

MT.ALLOC	$0C	allocate a bit of a heap

MT.LNKFR	$0D	releasea bit of a heap

MT.ALRES	$0E	allocate resident procedure area

MT.RERES	$0F	releaseresident procedure area

MT.DMODE	$10	set display mode MT.IPCOM	$11	send IPCcommand MT.BAUD	$12	set baud rate MT.RCLCK	$13	read clock MT.SCLCK	$14	set clock

MT.ACLCK	$15	adjust clock

18.14.2 Trap 2 Keys (I/O Management Traps)-

| IO.OPEN | $01 | open channel |
| --- | --- | --- |
| IO.CLOSE | $02 | close channel |
| IO.FORMT | $03 | format medium |
| IO.DELET | $04 | delete file |
| IO.OPEN | D3 | keys: |
| IO.OLD | 0 | open old (exclusive) file or device |
| IO.SHARE | 1 | open old (shared) file |
| IO.NEW | 2 | open new (exclusive) file |
| IO.OVERW | 3 | overwrite (or open new) file |
| IO.DIR | 4 | open directory |

18.14.3 Trap 3 Keys (I/O  Traps)-

| SD.WDEF SD.CURE SD.CURS SD.POS | $0D $0E $0F $10 | define window enable cursor suppress cursor absolute position |  |
| --- | --- | --- | --- |
| SD.TAB | $11 | tab (horizontal position) |  |
| SD.NL | $12 | newline |  |
| SD.PCOL | $13 | previous column |  |
| SD.NCOL | $14 | next column |  |
| SD.PROW | $15 | previous row |  |
| SD.NROW | $16 | next row |  |
| SD.PIXP | $17 | set pixel position |  |
| SD.SCROL | $18 | scroll whole window |  |
| SD.SCRTP SD.SCRBT SD.PAN SD.PANLN SD.PANRT SD.CLEAR | $19 $1A $18 $1E $1F $20 | scroll top of window scroll bottom of window pan window pan cursor line pan RHS of cursor line clear whole window |  |
| SD.CLRTP | $21 | clear top of window |  |
| SD.CLRBT | $22 | clear bottom of window |  |
| SD.CLRLN | $23 | clear cursor line |  |
| SD.CLRRT | $24 | clear to right of cursor |  |
| SD.FOUNT | $25 | set fount addresses |  |
| SD.RECOL | $26 | recolour a window |  |
| SD.SETPA | $27 | set paper colour |  |
| SD.SETST | $28 | set strip colour |  |
| SD.SETIN SD.SETFL SD.SETUL SD.SETMD SD.SETSZ SD.FILL SD.DONL SD.POINT | $29 $2A $28 $2C $2D $2E $2F $30 | set ink colour set flash on/off set underline on/off set write mode set character size fill block do pending newline set point in window |  |
| SD.LINE | $31 | draw line |  |
| SD.ARC | $32 | draw arc |  |
| SD.EllPS | $33 | draw ellipse |  |
| SD.SCALE | $34 | set graphics scale |  |
| SD.FLOOD | $35 | set fill mode/vectors |  |
| SD.GCUR | $36 | set text cursor using graphics coords coords |  |  |
| SD.ROP | $37 | rasterop |  |  |
| SD.DOT | $38 | points in pixel coords |  |  |

| SD.LIN | $39 | lines in pixel coords |
| --- | --- | --- |
| FS.CHECK | $40 | check all pending operations |
| FS.FLUSH | $41 | flush buffers |
| FS.POSAB | $42 | position file pointer (absolute) |
| FS.POSRE | $43 | position file pointer (relative) |
| FS.MDINF | $45 | information about medium |
| FS.HEADS | $46 | set file header |
| FS.HEADR | $47 | read file header |
| FS.LOAD | $48 | load file |
| FS.SAVE | $49 | save file |

18.15 List of Vectored Routines

The following  is a list of the vectored  routines, together  with the addresses of their associated vectors. All keys are in hex.

| CN.ITOHL CN.ITOHW | $FE $FC | long to ASCII hex word to ASCII hex |
| --- | --- | --- |
| IO.NAME | $122 | decode a device name |
| IO.QSET | $DC | set up a queue |
| IO.QTEST | $DE | test status of queue |
| IO.QIN | $E0 | put byte into queue |
| IO.QOUT | $E2 | extract byte from queue |
| IO.QEOF | $E4 | put EOF marker into queue |
| IO.SERQ | $E8 | direct queue handling |
| IO.SERIO | $EA | general IO handling |

The MD routines are indexed by $4000.

| MD.READ | $124 | read a sector |  |
| --- | --- | --- | --- |
| MD.WRITE | $126 | write a sector |  |
| MD.VERIN MD.SECTR | $128 $12A | verify a sector read a sector header |  |
| MM.ALCHP MM.ALLOC MM.LNKFR MM.RECHP | $CO $D8 $DA $C2 | allocate common heap space allocate an area in a heap link free space back into heap release common heap space |  |
| RI.EXEC RI.EXECB | $11C $11E | execute an operation execute a list of operations |  |
| UT.CON UT.CSTR | $C6 $E6 | set up console window compare two strings |  |
| UT.ERR | $CC | write error message to channel |  |
| UT.ERRO | $CA | write error message to channel zero |  |
| UT.LlNK | $D2 | link an item into a list |  |
| UT.MINT | $CE | convert integer to ASCII,put on chan |
| UT.MTEXT | $D0 | send message to channel |
| UT.SCR | $C8 | set up screen window |
| UT.UNLNK | $D4 | unlink an item from a list |
| UT.WINDW | $C4 | set up window using supplied name |

19.0 Doing Business with	Sinclair

The purpose of this section is to encourage those thinking of developing commercial software for the QL to consider offering it to Sinclair Research for publishing, promotion and distribution. There are various options offered to software houses, with varying degrees of Sinclair involvement	and support.

The first option is that of full publication and manufacture by Sinclair, whereby the new product is taken as a master with draft documentation, packaged in Sinclair packaging style and sold under the Sinclair logo in all the outlets stocking Sinclair hardware products. The software house is thereby released completely from the tasks of production, packaging, promotion, distribution and sale. For such a proposal to be financially viable, Sinclair has to obtain an exclusive licence for the product on Sinclair computers, and Sinclair will pay a percentage royalty on every unit sold. The software house remains free, of course, to develop the software for other computers, should it wish to do so.

The second option is for the software house to give Sinclair an exclusive licence to distribute the product in Sinclair packaging, but to sell the product to Sinclair as a fully packaged finished product to Sinclair specification. In this way the software house remains responsible for production and packaging, with Sinclair undertaking promotion, distribution and sale.

The third option is for the software house to retain responsibility for production, packaging, promotion, distribution and sale of the product, but allowing Sinclair to offer the product for sale in addition. This method provides the software house with an opportunity to increase its sales, as the product will be promoted in all Sinclair Mail Order literature. As orders are received, they will be passed to the software house, and Sinclair will require a percentage commission on orders generated in this way. Under this option, Sinclair packaging is not used for the product and so it remains very much the software house's 'own brand'.

Further details of the above options  are given later on in this section, but first, the procedure  for offering  software  to Sinclair is dealt with, together  with  Sinclair methods  of review and appraisal.

19.1	How to offer a Product to Sinclair

When a software house offers a product to Sinclair for publication, two main areas have to be examined.

The first of these areas is the product concept. Under this heading, answers must be provided to such questions as:

What is the product? What does it do?

For what type of market is it intended?

Does it exist?

If it exists:

How is it selling?

Methods of sale?

Volumes to date?

What machine does it run on?

If it does not exist:

What kind of sales are anticipated? Based on what kind of information?

Are there any other products like it and if so which?

Obviously, some of the questions listed above assume that the product does not already exist for the QL or any other Sinclair computer. However, if it does run on some other computers, the second area to be examined would be concerned with how the product might be adapted to make use of the QL's features.

Specifically:

How would the product change?

What kind of pricing structure is envisaged?')

What volume of sales are expected with respect to a low-cost computer such as the QL?

Would the target market change at all and if so, how?

Apart from considering the two areas described above, the product would need to be reviewed by Sinclair. For such a review to take place, the software house would need to send either:

1, The product itself, running on the QL, together with draft documentation,It need not be finished and completely bug free, so long as it is sufficiently complete to be able to be put out for review,

or

2, The product running on another machine, preferably on Apple II, Macintosh or an IBM Pc.

or

3. A detailed product proposal on paper if the product exists only as a design. Such a proposal should cover at the very least the product concept and the proposals for the QL version of it.

19.2 Where Software Products should be sent for Review

1. Business software or proposals should be sent to the Business Software Editor, at the address given in the introduction to this manual.

2. Educational software or proposals should be sent to the Educational

Software Editor, at the same address.

3. Anything that does not fall clearly into either of these two categories (e.g., games, compilers, utilities, expert systems etc.), should be sent to the Software Manager, at the same address.

19.3 How Products are reviewed and what

Sinclair are looking for

1. Games and entertainment software

Software of this type is generally reviewed by outside reviewers, often sixth formers. They are looking for originality, graphics, excitement, variety and pace. The software isjudged under these five categories. The reviewers also compare the software to other similar products, and finally try to identify any bugs which may require fixing together with any improvements which may be made.

As the computer games market is both extremely competitive and overcrowded, Sinclair can only consider absolutely top quality products for distribution. At the same time, the QL has expanded the range of possibilities in the context of entertainment software, thus any new ideas for using computers at home for entertainment and leisure activities would be reviewed with great interest.

2. Compilers and utilities

Technical products ofthis kind will be reviewed internally in the first instance by Sinclair software engineers. They will judge the product for its completeness, the adequacy of its documentation, the speed at which it runs on the QL and its technical competence. In some cases where the product is of a very specialist nature it would be put out for review by an independent consultant.

3. Educational software

Educational products, either for school, polytechnic, university or home use, will be reviewed internally at first, and possibly also by Sinclair educational consultants. The following categories are of particular interest to Sinclair:

1. Software which caters for specific university and polytechnic

markets.

2. Software which provides adult home education in fields previously uncatered for.

3. Software wh ich actually teaches rather than tests foreign

languages such as French, German or Spanish.

4. Software which teaches people how to expand their potential

for different employment markets, for example, teaching touch typing, word processing, how to understand accounts, how to program etc.

5. Expert systems and authoring systems, especially if they have application software running under them which can also be sold.

4.  Business software

Business software  will be reviewed  internally  unless it caters for a specific vertical  market  in which  case Sinclair may seek permission to have the product  reviewed  in detail by an independent

consultant.  When  possible business packages are being considered,

both the company  and the product  will be examined  very carefully.

Thus the following  are particularly  sought  after:

1. Established suppliers of business products  with  a respected name in the business market.

2.  Products which  would  benefit  from  distribution  in wider  markets and at a lower price than at present.

3. Suppliers who can, if necessary, provide  any direct support needed by their product  to Sinclair customers,  possibly at additional  cost.

4.  A secure financial  backing  which  will ensure that the company will not disappear after Sinclair have launched the product, leaving  no support  for it.

19.4 Contractual Options in dealing with

Sinclair Research

In the introduction to this section several possible contractual options were described, which will now be explored in more detail.

1. Distribution in Sinclair packaging

Royalty contract - every software house which offers a product to

Sinclair Research for distribution in Sinclair packaging under the

Sinclair name, will be asked to sign a Licence Agreement of the type

shown in Appendix A. This agreement allows for the grant of an exclusive licence to Sinclair Research for the distribution and sale of the specified software products, in return for a royalty which is normally 20% of the selling price.

2. Distribution of finished goods

Those software houses from whom Sinclair agree to buy a complete finished product packaged to Sinclair specifications, will be asked to sign a second contract in addition to the software licence contract described above. This second contract would provide for the supply and purchase of manufactured goods on an 'at cost plus' basis. In this way, a packaging specification would be agreed upon for the product, and Sinclair would nominate approved suppliers of each component of that packaging. The software house would then purchase these components from the nominated supplier at a price previously negotiated between Sinclair and the supplier. The cost of the product would then be passed on to Sinclair, the software house having added a fixed margin as their handling fee for controlling production.

3. Sinclair approved products

Under this option, the product would neither be sold in Sinclair packaging nor would it carry the Sinclair name. It would instead be packaged in the software house's own packaging under its own name. It would, however, be promoted as a Sinclair endorsed product in the Sinclair catalogue. Orders would be sent to a special PO box at Sinclair's despatching warehouse and would then be forwarded direct to the software house for fulfilment. Sinclair would, of course, expect to be paid a percentage commission on orders generated in this way, which would normally be equivalent to 15% of the retail selling price.

19.5 Promotion and Distribution

1. Sinclair packaged software

As might be expected, software carrying the Sinclair logo attracts the bulk of Sinclair promotional activities. In particular, all software carrying the Sinclair logo and name will:

1)   be offered initially to all Qlub members directly, possibly at a small discount as an introductory offer;

2)   be carried in a catalogue which will be included with every QL

shipped;

3)   be launched to the trade and specialist press, and included in advertising campaigns from time to time;

4)   be the subject of special promotions which will be considered for vertical market software;

5)   be offered the possibility of consideration for bundling contracts

from time to time. This can be a very lucrative way of ensuring that the software reaches the widest possible market;

6)   be offered to our local area offices and distributors all over the world, for translation into foreign languages;

7)   be similarly offered to our Boston Office for publication and distribution in the United States.

2. Sinclair endorsed products

Where a product is not distributed in the Sinclair packaging, but is being promoted and offered for sale through Sinclair, then it is likely to be promoted using methods 1.) and 2.) only, though from time to time, where appropriate, other methods of promotion and marketing will be considered. To attract the full range of Sinclair's marketing activities a product needs to be offered for distribution in both the Sinclair packaging and brand name.

19.6 Summary

Many software houses writing software for personal computers today are concerned about the possible dilution of effort that is entailed

when a product has to be packaged, promoted, marketed and sold as

well as developed. Sinclair Research are known for their ability to obtain media coverage and for their marketing and distribution capabilities.

In the case of the QL, Sinclair believe that software houses can be offered distribution opportunities without equal. The Qlub will enable direct contact to be retained with customers on a far larger scale than previously possible with other Sinclair computers. It is proposed to use the Qlub Newsletters as a method of informing customers of every new product launched in advance of the general public. Small discounts will be offered which will make the product attractive tothe customer, but will not begin to approach the kind of discounts Sinclair would need to give should the product be offered through a distributor or a retailer.

It is hoped that software houses will feel that to offer software to

Sinclair in one of the ways described above will prevent many of the problems previously associated with bringing their products onto the market place.

20.0	Bibliography

1. MC68000 16/32-bit microprocessor programmer's reference manual.

Published by Prentice-Hall for Motorola. ISBN 0-13-566795-X. Contains instruction set details for the MC68000 and MC68008,

including permissible addressing modes and bus cycle diagrams.

Some hardware detail is included, but no timing diagrams.

2. Motorola Semiconductors 16-bit microprocessors data manual -

1983.

Published by Motorola Ltd., York House, Empire Way, Wembley, Middlesex.

Contains the hardware reference for the MC68008.

21.0 Index

A1 stack see arithmetic stack

access layer

of device driver 31,32,34,37

of directory drive 38-45

add-on

card ROM  66

cards 63,66

hardware 56

peripherals 56

RAM 56,63

ROM 10,56,63,66

allocation

heap 8,23,147

memory 9-10,22,31

alphabets, special 69

area flood 119

arithmetic

interpreter operation codes 170-171

stack 47,54-55,135

array storage 51

atomic actions 13

auto-repeat 30

baud 59,75,173

blocks

physical 38

slave 9,44,166

BOOT

device driver 16

file 16

border 28,113

BP.INIT 52,69,134,176

BP.LET 55,135,176

buffer 47

bus error 14

business 178-185

BV.CHRIX 22,54,135,176

CA.GTFP 54,136,176              CA.GTINT 54,136,176

CA.GTLIN 54,136,176          CA.GTSTR 54,136,176

CAPSLOCK 30

change queue character 30

channel 24

close 24,30,35-36,42-3

console

definition block 32,38,166-167

ID 17,24

number 55

open 24,30,34-35,41-42

table 47,55

superBASIC 9,164

character conversion 138,139 character set 68

change queue 30

freeze screen 30

local 68

spacing 27

character size 125,130,175

clock 59

real-time 57,59

CN.BTOIB 138,176

CN.BTOIL 138,176

CN.BTOIW 138,176

CN.DATE 59,137

CN.DAY 59,137

CN.DTOF 138,176

CN.DTOI 138,176

CN.FTOD 139,176

CN.HTOIB 138,176

CN.HTOIL 138,176

CN.HTOIW 138,176

CN.ITOBB 139,176

CN.ITOBL 139,176

CN.ITOBW 139,176

CN.ITOD 139,176

CN.ITOHB 139,176

CN.ITOHL 139,177

CN.ITOHW 139,177

code

initialisation 31,33

position-independent 19

restrictions 52

colour 28,74

border 28

ink 28

paper 28

strip 28

command interpreter 17

common heap  7,8

allocation 8,23,147

release 149

console 27

I/O 27-30,46

console channels 27

special properties 29-30

contracts 182-183

coordinate system

graphics 27

pixel 27

CPU interface 64-65

CTS 59

cursor 125

flashing 30

increment 28

position 28

date 137

definition block

channel 31,38,166-167

device driver 31-33

directory device

linkage 38

file system 166-167

physical 38

device 24

decoding 31,140

name 24

device driver(s) 22,24,31-37

access layer 31,32,34-37

BOOT 16

built-in 46

console 46

definition block 32

directory 38-45,60

initialisation 32-33

memory allocation 32

Microdrive 46

network 59

non-directory 39,41

physical layer 21,31,33-34

pipe 46

screen 46

serial I/O 46

serial network link 46

user defined 21

user supplied 31

directory device driver(s) 38-45

access layer 40

initialisation 38

linkage block 39

Microdrive 60

display

control 57-58

modes 27,76

RAM 56

display control register 58

distribution 183-184

draw 123

DTR 59

error

bus 14

keys 158

messages 152,158

exception processing 14-15

EXEC 18

EXEC_W 18

expansion 63-64

extensions, operating system 17,21 external interrupt 14,34

file

BOOT 16

header  26,38

format 26

I/O 26

pointer 26

program 47

shared 41

file delete 41-42

file system definition blocks 168

flag 28

characteristics 66

flashing 30,57,58

floating point storage 50,51

format routine 41,45

fount 120

frame interrupt 14

free memory 7,9,22-23

freeze screen character 30

FS.CHECK 26-27,98,176

FS.FLUSH 26-27,99,176

FS.HEADR 100,176

FS.HEADS101.176

FS. LOAD 102,176

FS.MDINF103,176

FS.POSAB 104,176

FS.POSRE 105,176

FS.SAVE106,176

functions 52

linking 52

superBASIC 21

graphics 29,123

coordinate system 27

operations 29

hardware 56,171-173

add-on 56

heap 23

allocation 8,23,147,149

common 7,8,9,147-149

expanding 23

linking free space into 149

mechanism 8,23

management 72-73

setting up 23

user 23

initialisation

code 31,33

device driver 32,33

directory device driver 38

Qdos 6-16,158-177

system management

tables 16

system variables 16

Input/Output (I/O) 24-30,33

36-37,42,43

console 27-30,46

file 26

queue 30

screen 27-30,46

serial 24,31,46,59,144

Input/Output sub-system 8,24,43

Integer storage 50,51

Intelligent Peripheral

Controller

8049 (IPC) 58,79

link commands 171

interfacing 47-55

interrupt

auto-vectored 13

external 13,24

frame 14

level 10,15

non-maskable 15

polling 34

traps for 14-16interrupt servers 14

I/O see Input/Output

IO.CLOSE 93,174

IO.DELET 41,94,174

IO.EDLIN 29,107,174

IO.FBYTE 108,174

IO.FLINE 29,109,174

IO.FORMT 95,174

IO.FSTRG 108,174

I/O management traps 10-11,93-97

close channel 93,174

delete file 94,174

format medium 95,174

keys 174

open channel 96,174

IO.NAME 35,140,177

IO.OPEN 35,41,96,174

IO.PEND 110,174

IO.QEOF 143.177

IO.QIN 143.177

IO.QOUT 143.177

IO.QSET 143,177

IO.QTEST 143,177

IO.SBYTE 25,111,174

IO.SERIO 37,144,177

IO.SERQ 37,144,177

IOSS see Input/Output

sub-system

IO.SSTRG112.174

I/O traps 11,21,98-133

absolute position 104,125

character based size/position

enquiry 126,174

check all pending

operations 98,176

check for pending input 110,174

clear part or whole

window 114,174

define window 133,174

define window border 113,174

edit a line 107,174enable cursor 115,175

extended operation 117,174

fetch a byte 108,174

fetch a line of bytes 109,174

fetch a string of

bytes 108,174

fill block 118,175

flush buffers 99,176

information about

medium 103,176

keys 173-176

load file 102,176

newline 125,175

next column 125,175

next row 125,175

pan part or whole

window 121,175

pixel based size/

position enquirer 104,126

plot and draw various lines and

arcs 123,175

position file pointer (absolute)

104,176

position file pointer (relative)

105,176

previous column 125,175

previous row 125,175

read file header 100,176

recoloura window 127,175

save file 106,176

scroll part or whole window

128,175

send a byte 111,174

send a string of bytes 112,174

set character size and spacing

132,175

set character size 130,175

set file header 101,176

set fill mode vectors 119,175

set flash and under-score

129,175set fount addresses 120,175

set pixel position 122,175

set screen colours 131,175

set write mode 130,175

suppress cursor 116,175

tab (horizontal position) 125,175

IPC see Intelligent Peripheral

Controller

job(s)10,17-21

active 17-19

format

header 47,164-165

ID 13,18-19

inactive 17

start-up 17-19

suspended 17

table 19

tree 47,49

keyboard

auto-repeat 30

control 58

non-English language 67

special functions 30

type-ahead 30

KEYROW 40,59

line number table 47

linked lists 23,90

linking

functions 52

procedures 52

machine code

procedures 20

programming 17-21

Manager traps 11,69-92

activate a job 69,173

adjust clock 69,173

allocate a bit of a

heap 73,173     allocate BASIC area 71,173

allocate resident procedure area

74,173

allocate space in common heap

72,173

create a job 75,173

find how much free space there is

77,173

force remove a job 77,173

get information on job 81,173

get system information 78,173

keys 173-176

link external interrupt handler

83,174

link in directory driver 83,174

link in I/O driver 83,174

link in polled task 83,174

link in schedulertask 83,174

read clock 84,173

release a bit of a heap 82,173

release a job 86,173

release BASIC area 85,174

release resident procedure area

87,173

release space in common heap

85,174

remove directory driver 89,174

remove external interrupt handler

89,174

remove I/O driver 89,174

remove job 88,173

remove polled task 89,174

remove schedulertask 89,174

send IPC command 79,173

set a job priority 84,173

set baud rate 75,173

set clock 90,173

set display mode 76,173

set pointer to trap redirection

vector 92,173

suspend a job 91,173

Master chip 57MD.READ 60,146,177

MD.SECTR 12,60,146,177 MD.VERIN 60,146,177

MD.WRITE 60,146,177

medium name 42

memory

allocation 8-10,22,31

block table 166

device driver 31

free 7,9,22

map 7-10,56

organisation in superBASIC 47-48

Microdrive 46

Microdrives 24,26,46,60

Microdrive support routines 146

MM.ALCHP 22,147,177

MM.ALLOC 22,148,177

MM.LNKFR 22,149,177

MM.RECHP 22,149,177

MT.ACLCK 59,69,173

MT.ACTIV 70,173

MT.ALBAS 22,71,174

MT.ALCHP 8,22,72,174

MT.ALLOC 8,73,173

MT.ALRES 14,74,173

MT.BAUD 59,75,173

MT.CJOB 75,173

MT.DMODE 27,57,58,76,173

MT.FREE 77,173

MT.FRJOB77.173

MT.INF 8,19,67,78,173

MT.IPCOM 58,68,79,173

MT.JINF81,173

MT.LDD 31,39,83,174

MT.LIOD 31,83,174

MT.LNKFR82,173

MT.LPOLL 31,39,83,174

MT.LSCHD 31,39,83,174

MT.LXINT 31,39,83,174

MT. PRIOR 84,173

MT.RCLCK 59,84,173MT. RDD 31,85,89,174

MT.REBAS 14,85,174

MT.RECHP 8,22,85,174,

MT.RELJB 86.173

MT.RERES 22,87,173

MT.RIOD 31,89,174

MT.RJOB 88,173

MT.RPOLL 31,89,174

MT.RSCH 031,89,174

MT.RXINT 31,89,174

MT.SCLCK 59,90,173

MT.SUSJ 691,173

MT.TRAPV 14,92,173

name

decode 31,35,39,140,177

list 48,49

pointer 49

table 48-49,53,134

network 46,59

newline 25,28

non-English 67-68

version codes

NTSC 40

on-board

RAM 56

ROM 56

operating system 6

extensions to 17,21

operations

executing lists of 151

execution of 150

ownership 178

PAL 67

pan 28,121,175

parameter passing 52-53

parameters, actual 53-54

peripheral card addressing 65

peripheral cards 63-65peripheral chip 57

physical definition block 38

physical layer device driver 21,31,33-34

pipe 24,46

pixel coordinate system 27

plot 123

polling interrupt 34

priority 17,84,86

procedures 52

linking 52

SuperBASIC 17,20-21

program file 47

programming 56-62

promotion 183-184

publication 178

Qdos

initialisation 7

keys 105-

routines 10-14

queue(s) 143

asynchronous 31

handling 144

header 170

I/O 30

type-ahead 30

RAM 7,22-23

add-on 56,63

base 7

display 6,56

on-board 56

screen 56

test 16

real-time clock 57,59

recolouring 127

resident procedure area 7,9,10,20,22

restrictions on code 52

return list 47

RI.EXEC 105,150

RI.EXECB105,150Rl stack see arithmetic stack

ROM 3,10,24 -34

add-on 10,56,63,65,66

format 46

on-board 56

plug-in 56

RS232 see serial I/O

save area 97

scheduler loop 34

screen

colour 131

I/O 27-30,46

RAM 56

screen character output operations

28

screen driver 46

datablock169

scrolling 128

SD.ARC 29.123

SD.BORDR 28,113,174

SD.CHENQ 28,126,174

SD.CLEAR 28,114,175

SD.CLRBT 28,114,175

SD.CLRLN 28,114,175

SD.CLRRT 28,114,175

SD.CLRTP 28,114,175

SD.CURE 28,115,175

SD.CURS 28,116,175

SD.ELIPS 29,123,175

SD.EXTOP 30,117,174

SD.FILL 28,118,175

SD.FLOOD 29,119,175

SD.FOUNT29,120,175

SD.GCUR 29,123,175

SD.LINE 29,123,175

SD.NCOL 125,175

SD.NL 125,175

SD.NROW 125,175

SD.PAN 28,121,175

SD.PANLN 28,121,175SD.PANRT 28,121,175

SD.PCOL 125,175

SD.PIXP 122.175

SD.POINT 29,123,175

SD.POS 125,175

SD.PROW 125,175

SD.PXENQ 28,126,174

SD.RECOL 28,127,175

SD.SCALE 29,123,175

SD.SCRBT 28,128,175

SD.SCROL 28,128,175

SD.SCRTP 28,128,175

SD.SETFL 29,129,175

SD.SETIN 28,131,175

SD.SETMD 28,130,175

SD.SETPA 28,131,175

SD.SETST 28,132,175

SD.SETSZ 29,132,175

SD.SETUL 29,129,175

SD.TAB 125,175

SD.WDEF 28,133,175

serial I/O 24,31,36,46,84

device driver 46

serial network link 46

slave block 9,44,166

table 44

slaving 26,40,44-45 software

business 181

commercial 178

compilers, utilities 180

educational 180-181

entertainment 180

games 180

review of 180-181

sound control 58-59

stack

arithmetic 47,54—55

supervisor 13

user 66start-up 6,16

job 17-19

system 16

storage 50-51

array 51

floating point 50,51

integer 50,51

string 51

substring 51

strings, comparison of 152

string storage 51

substring storage 51

SuperBASIC 7,9,10

channel table 9

format 164

data area 20

function 52

initialisation 16

interfacing 47-55

memory organisation 47-48

procedures and functions 20-21

program 9

traps 10-11

variables 7-8,161-163

work area 7,9,47

supervisor

mode 11,13,52

stack 13

suspended job 17

system

job table 19

management tables 7-8

initialisation 16

start-up 16

variables 7-8,20,159-161

base 6,159

initialisation 16

tables

channel 47,55

job 19

line number 47

memory block 166

name 47-49,53,78

system management 7,8,16

tasks 17,21,31

external interrupt 34

polling interrupt 34

scheduler loop 34

time-out 30,36,42

token list 47

transient program area

7,9,10,17,20,22,45

trap(s) 10-11

#0 11,13

#1 11,13

#2 11

#3 11,13

#4 11,21

errors in 11

hardware interrupts 14-15

Input/Output 11,21,98-133

Input/Output control 11,93-97

keys 173-176

manager 11,69-92

redirection 14

software error 14

SuperBASIC 11

user 14

type, name table 47,48

type-ahead queue 30

user

code 8,22

heap 22

traps 14

user stack 66

UT. CON 156,177

UT.CSTR 152.177

UT.ERR 152.177

UT.ERRO 152,177

UT.LINK 153,177

UT.MINT 154,177

UT.MTEXT 155,177

UT.SCR 156,177

UT.UNLNK 153,177

UT.WINDW 156,177

value pointer 49

variables

SuperBASIC 9,161-163

system 7,8,16,19,93-94

variable values area 47,48

vectored routines 12-13,54,134-

157,176-177

error handling 12

video 67

for monitor operation 67

for TV operation 67

windows 27-28

border 28,113

clearing 114

colour 28,127

overlap 27

position 27

properties and operations 27-28

setting up 156

size 27

ZX8301 57

ZX8302 57

# Text boxes

| 1.0 | About this Guide | 4 |
| --- | --- | --- |
| 2.0 | Introduction to Qdos | 6 |
| 2.1 | Memory Map | 7 |
| 2.2 | Calling Qdos Routines | 10 |
| 2.3 | Exception Processing | 14 |
| 2.4 | Start-up | 16 |
| 3.0 | Machine Code Programming on the QL | 17 |
| 3.1 | Jobs | 17 |
| 3.2 | SuperBASIC Procedures and Functions | 20 |
| 3.3 | Tasks | 21 |

| 18.11 | Arithmetic Interpreter | Operation | Codes | 170 |
| --- | --- | --- | --- | --- |
| 18.12 | IPC Link Commands |  |  | 171 |
| 18.13 | Hardware Keys |  |  | 171 |
| 18.14 | Trap Keys |  |  | 173 |

Resident procedure area

Transient program area

SuperBASIC area

Free memory area (used up for slave blocks by the filing system)

Common heap area

System management tables

System variables

Display RAM

| (A6,A5) | Command string |
| --- | --- |
|  | Channel ID Channel ID " " Channel ID |
| (A7) | Number of Channel IDs |
| (A6,A4) | Data area |
|  | Code area |
|  | Job name |
|  | $4AFB |
| (A6) | JMP.L JOB_START |

| Bytes 7-4 | Bytes 3-2 | Bytes 1-0 | Type |
| --- | --- | --- | --- |
| Value pointer Value pointer Value pointer Ptr to RI stack Ptr to RI stack Ptr to RI stack Value pointer Value pointer Value pointer Value pointer Value pointer Value pointer Value pointer Line no in msw Line no in msw Line no in msw Line no in msw Value pointer Value pointer Abs. address Abs. address | Name pointer Name pointer Name pointer -1 -1 -1 Name pointer Name pointer Name pointer -1 Name pointer Name pointer Name pointer Name pointer Name pointer Name pointer Name pointer Name pointer Name pointer Name pointer Name painter | $0001 $0002 $0003 $0101 $0102 $0103 $0201 $0202 $0203 $0300 $0301 $0302 $0303 $0402 $0501 $0502 $0503 $0602 $0702 $0800 $0900 | Unset string Unset floating point number Unset integer String expression Floating point expression Integer expression String Floating point number Integer Substring String array Floating point array Integer array SuperBASIC procedure SuperBASIC string function SuperBASIC f.p. function SuperBASIC integer function REPeat loop index FOR loop index Machine code procedure Machine code function |

| Hex |  | String |
| --- | --- | --- |
| 0004 | 41424344 | "ABeD" |
| 0003 | 414243xx | "ABC" |
| 0000 |  | "" |

Add-on ROM (Up to 128 kbytes)

Add-on peripherals (8 slots of up to 16 kbytes each)

Add-on RAM (Up to 512 kbytes)

On-board user RAM (96 kbytes)

Screen RAM (32 kbytes)

On-board I/O (Partially decoded)

Plug-in ROM cartridge (16 kbytes)

On-board ROM (48 kbytes)

| Address (Hex) | Function (Read) | Function (Write) |
| --- | --- | --- |
| $18023 $18022 $18021 $18020 $18003 $18002 $18001 $18000 | Microdrive data (track 2) Microdrive data (track 1) Interrupt/lPC link status Microdrive/RS-232-C status Real-time clock byte 3 Real-time clock byte 2 Real-time clock byte 1 Real-time clock byte 0 | Display control Microdrive/RS-232-C data Interrupt control Microdrive control IPC link control Transmit control Real-time clock step Real-time clock reset |

\

| A0 | base of area to be freed | A0 | ??? |
| --- | --- | --- | --- |
| A1 |  | A1 | ??? |
| A2 |  | A2 | ??? |
| A3 |  | A3 | ??? |

| SV_CAPS SV_ARBUF | $88 $8A | word word | caps lock autorepeat | buffer |
| --- | --- | --- | --- | --- |
| SV_ARDEL SV_ARFRQ | $8C $8E | word word | autorepeat autorepeat | delay 1/freq |
| SV_ARCNT | $90 | word | autorepeat | count |
| SV_CQCH | $92 | word | keyboard change queue character code |
| SV_SOUND | $96 | word | sound status |
| SV_SER1C | $98 | long | receive channel 1 queue address |
| SV_SER2C | $9C | long | receive channel 2 queue address |
| SV_TMODE | $AO | byte | ZX8302 transmit mode (includes |
|  |  |  | baudrate) |
| SV_CSUB SV_TIMO SV_TIMOV | $A2 $A6 $A8 | long word word | subroutine to jump to on CAPSLOCK timeout for switching transmit mode value of switching timeout (two |
|  |  |  | characters) |
| SV_FSTAT | $AA | word | flashing cursor status |

| BV_BTP BV_BTBAS BV_TGP | $48 $4C $50 | long long long | backtrack temporary | stack during parsing graph stack during parsing |
| --- | --- | --- | --- | --- |
| BV_TGBAS | $54 | long |  |  |
| BV_RIP BV_RIBAS | $58 $5C | long long | arithmetic | stack |
| BV_SSP | $60 | long | system stack (real one!) |
| BV_SSBAS | $64 | long |  |
| BV_ENDPT | $64 |  | end of pointers |
| BV_LlNUM BV_LENGTH BV_STMNT | $68 $6A $6C | word word byte | current line number current length current statement on line |
| BV_CONT BV_INLIN | $6D $6E | byte byte | continue ($80) or stop (0) processing processing in-line clause or not |
|  |  |  | loop (1), other ($FF), not (0) |
| BV_SING BV_INDEX | $6F $70 | byte word | single line execution on ($FF) or off (0) name table row of last in-line loop index |
| BV_VVFREE | $72 | long | read first free space in variable value table |
| BV_SSSAV | $76 | long | saved sp for out/mem to go back to |
| BV_RAND | $80 | long | random number |
| BV_COMCH | $84 | long | command channel |
| BV_NXLlN BV_NXSTM BV_COMLN BV_STOPN BV_EDIT BV_BRK BV_UNRVL | $88 $8A $86 $8C $8E $8F $90 | word byte byte word byte byte byte | which line number to start after which statement to start after command line saved ($FF) or not (0) which stop number set program has been edited ($FF) or not (0) there has been a break (0) or not ($80) need to unravel ($FF) or not (0) |
| BV_CNSTM | $91 | byte | statement to CONTINUE from |
| BV_CNLNO | $92 | word | line to CONTINUE from |

| BV_DALNO | $94 | word | current DATA line number |
| --- | --- | --- | --- |
| BV_DASTM | $96 | byte | current DATA statement number |
| BV_DAITM | $97 | byte | next DATA item to read |
| BV_CNIND | $98 | word | in-line loop index to CONTINUE with |
| BV_CNINL | $9A | byte | in-line loop flag for CONTINUE |
| BV_LSANY | $9B | byte | whether checking list ($FF) or not (0) |
| BV_LSBEF | $9C | word | invisible top line |
| BV_LSBAS BV_LSAFT | $9E $AO | word word | bottom line in window invisible bottom line |
| BV_LENLN | $A2 | word | length of window line |
| BV_MAXLN | $A4 | word | max nr of window lines |
|  |  |  | The 2 words immediately following this |
|  |  |  | will be overwritten on changing lenln |
|  |  |  | and maxln |
| BV_TOTLN | $A6 | word | nr of window lines so far |
| BV_AUTO | $AA | byte | whether AUTO/EDIT on ($FF) or off (0) |
| BV_PRINT | $AB | byte | print from prtok ($FF) or leave in |
|  |  |  | buffer (0) |
| BV_EDLIN | $AC | word | line number to edit next |
| BV_EDINC | $AE | word | increment on edit range |
| BV_TKPOS | $BO | long | pos of A4 in tklist on entry to PROC |
| BV_PTEMP | $B4 | long | temp pointer for GO_PROC |
| BV_UNDO | $B8 | byte | undo rt stack IMMEDIATELY then redo |
|  |  |  | procedure |
| BV_ARROW | $B9 | byte | down ($FF) or up (01) or no (00) arrow |
| BV_LSFIL | $BA | word | fill window when relisting at least to here |
| BV_WRLNO | $BC | word | when error line number |
| BV_WRSTM | $BE | byte | when error statement |
| BV_WRINL | $BF | byte | when error in-line ($FF) or not (0) |
| BV_WHERR | $CO | byte | processing when error ($80) or not (0) |
| BV_ERROR | $C2 | long | last error code |
| BV_ERLIN | $C6 | word | line number of last error |
| BV_WVNUM | $C8 | word | number of watched (WHEN) variables |
| BV_WVBAS BV_END | $CA $100 | long | base of WHEN variable table wrt WBAS top of BV area |

"

| BT.UNAV | 00000000B | block | is unavailable to file system |
| --- | --- | --- | --- |
| BT.EMPTY | 00000001B | block | is empty |
| BT.RREQ | 00001001B | block | required to be read from |
| microdrive |
| BT.TRUE | 00000011B | block | is a true representation of file |
| BT.AVER | 00001011B | block | is awaiting verify |
| BT.UPDT | 00000111B | block | is updated |

| RDS2_CMD 7 | read RS232 channel 2 |
| --- | --- |
| RDKB_CMD | 8 | read keyboard |
| KBDR_CMD | 9 | keyboard direct read |
| INSO_CMD | 10 | initiate sound process |
| KISO_CMD | 11 | kill sound process |
| MDRS_CMD | 12 | Microdrive reduced sensitivity |
| BAUD_CMD | 13 | change baud rate |
| RAND_CMD | 14 | random number generator |
| TEST_CMD | 15 | test |

| PC_TCTRL | $18002 | transmit control |
| --- | --- | --- |
| PC_MCTRL | $18020 | Microdrive control/status and IPC status |
| PC_IPCRD | $18020 | IPC read is the same |
| PC_IPCWR | $18003 | IPC write |
| PC_INTR | $18021 | interrupt control/status |

| PC..SEL | 0 | Microdrive | select bit |
| --- | --- | --- | --- |
| PC..SCLK | 1 | Microdrive | select clock bit |
| PC..WRIT | 2 | Microdrive | write |
| PC..ERAS | 3 | Microdrive | erase |
| PC..TXFL | 1 | Microdrive | Xmit buffer full |
| PC..RXRD | 2 | Microdrive | read buffer ready |
| PC..GAP | 3 | gap |  |
| PC..DTR1 | 4 | DTR on port 1 |
| PC..CTS2 | 5 | CTS on port 2 |

| MT.ALBAS | $16 | allocate BASIC area |
| --- | --- | --- |
| MT.REBAS | $17 | release BASIC area |
| MT.ALCHP | $18 | allocate space in common heap |
| MT.RECHP | $19 | release space in common heap |
| MT.LXINT | $1A | link in external interrupt handler |
| MT.RXINT | $1B | remove external interrupt handler |  |
| MT.LPOLL | $1C | link in polled task |  |
| MT.RPOLL | $1D | remove polled task |  |
| MT.LSCHD | $1E | link in scheduler task |  |
| MT.RSCHD | $1F | remove scheduler task |  |
| MT.LlOD | $20 | link in IO driver |  |
| MT.RIOD | $21 | remove IO driver |  |
| MT.LDD | $22 | link in directory driver |  |
| MT.RDD | $23 | remove directory driver |  |

| IO.PEND | $00 | check for pending input |
| --- | --- | --- |
| IO.FBYTE | $01 | fetch a byte |
| IO.FLlNE | $02 | fetch a line of bytes |
| IO.FSTRG | $03 | fetch a string of bytes |
| IO.EDLIN | $04 | edit a line |
| IO.SBYTE | $05 | send a byte |
| IO.SSTRG | $07 | send a string of bytes |
| SD.EXTOP | $09 | external operation (A3) |
| SD.PXENQ | $0A | pixel based size/position enquiry |
| SD.CHENQ SD.BORDR | $0B $0C | character based size/position enquiry define window border |

| BP.lNIT | $110 | add m/c procs/fns to BASIC |
| --- | --- | --- |
| BP.LET | $120 | assign tos to variable |
| BV.CHRIX | $11A | reserve space on RI stack |
| CA.GTINT | $112 | get word parameters to RI stack |
| CA.GTFP | $114 | get floating point numbers |
| CA.GTSTR | $116 | get strings |
| CA.GTLIN | $118 | get long integers |
| CN.BTOIB | $104 | ASCII binary to byte |
| CN.BTOlL | $108 | ASCII binary to long |
| CN.BTOIW | $106 | ASCII binary to word |
| CN.DATE | $EC | get ASCII date and time |
| CN.DAY | $EE | get ASCII day of week |
| CN.DTOF | $100 | ASCII to floating point |
| CN.DTOI CN.FTOD | $102 $F0 | ASCII to integer floating point to ASCII |
| CN.HTOIB | $10A | ASCII hex to byte |
| CN.HTOlL | $10E | ASCII hex to long |
| CN.HTOIW | $10C | ASCII hex to word |
| CN.lTOBB | $F4 | byte to ASCII binary |
| CN.lTOBL | $F8 | long to ASCII binary |
| CN.lTOBW | $F6 | word to ASCII binary |
| CN.lTOD | $F2 | word integer to ASCII |
| CN.lTOHB | $FA | byte to ASCII hex |